## Slide 1: Comparison of Compression Performance of HEVC versus AVC for UHD-1 sequences
JCTVC-M0166
Incheon, KR, 18–26 Apr. 2013
M. Arena, P. Sunna (RAI)
Philippe BORDES, P. Andrivon (Technicolor)

## Slide 2: Purpose
Compare objective performance (BD-rate metric) between :
  HEVC draft 10 Main (10) profile(s)
  versus
  AVC High (10) profile(s)
Benchmark on:
  2160p@50 Rec.709 (3840x2160) 8 and 10-bit

## Slide 3: Test material
Material available from the recent UHD-1 EBU shooting http://tech.ebu.ch/docs/tech-i/ebu_tech-i_013.pdf

## Slide 4: Sequences
waterfall_pan
Lupo_candlelight
Public test set
Sony F65 capture
Low light
Complex Motion
rain_fruits
Public test set
Sony F65 capture
Hugely textured
Complex illumination
fountain_lady
Test set
Sony F65 capture
Colorful
Complex motion
Lupo_confetti
Test set
Sony F65 capture
Very complex motion with sparse objects
Test set
Sony F65 capture
Hugely textured
Pan
Notes: <number>

## Slide 5: Test settings
Comparison between:
  HEVC Main/Main 10 Profile (HM-10.0) versus
  AVC High Profile/High 10 Profile (JM-18.4)
Tests performed using common test conditions with configurations:
  All Intra (AI)
  Random Access (RA)
  Low Delay B (LB)
Sequences converted to 8-bit or 10-bit 4:2:0 Y’CbCr Rec.709
Encoded 250 frames (5 seconds) per sequence

## Slide 6: HEVC Main Profile vs AVC High Profile (8-bit)
 | Y | U | V
AI | -26.5% | -22.7% | -30.5%
RA | -47.3% | -34.8% | -41.3%
LB | -48.7% | -33.2% | -41.5%
All gains of HM10.0 over JM18.4 are around 25 % for AI, 45% for both RA and LB configurations

## Slide 7: HEVC Main 10 Profile vs AVC High 10 Profile (10-bit)
 | Y | U | V
AI | -25.5% | -20.8% | -26.9%
RA | -46.8% | -23.6% | -31.1%
LB | -50.8% | -28.5% | -37.3%
Results are consistent with those of the previous slide

## Slide 8: HEVC Main and Main 10 Profiles comparison considerations
 | Y | U | V
AI | -3.6% | -8.5% | -10.8%
RA | -4.9% | -14.4% | -18.2%
LB | -5.4% | -16.4% | -19.6%
Results tend to show that for the considered versatile test material and test conditions, Main 10 profile outperforms Main profile BD-rate performances for 10-bit source inb terms of objective fidelity to the source.

## Slide 9: Conclusion
Considering 3840x2160 digitally acquired material:
HEVC (HM10.0)
better than (BD-rate)
H.264/AVC (JM18.4)
  25 % for All Intra
  45 % for Random Access
  45% for Low Delay B

## Slide 10: Any questions?
Pierre Andrivon Philippe Salmon
Philippe Bordes
(Technicolor)
Marco Arena
Paola Sunna
(RAI)