## Slide 1: AHG5: Range Extensions and High Bit Depths CABAC Efficiency
JCTVC-M0178
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
From the studies at higher bit-depths, with
  MAX_TR_DYNAMIC_RANGE = bitDepth+5
  ENTROPY_CODING_DYNAMIC_RANGE = bitDepth+6
  Transform matrix precision = 14
  Transform skip, RDOQ and PCM disabled

## Slide 3: Background
Coding higher bit-depth data gradually becomes more and more costly.
For the sequences tested:
  For 16-bit data,
    The sequences are actually inflated at their useful operating range: (MSE <= 1, SNR >= 96.3, i.e. QP <= -32)
    The base-band video rate is 1920x1080x16x3x50 = ~ 5 Gbps.
    The lossless PCM mode would therefore be used.
  For 14-bit data,
    The sequences are inflated for a substantial part of their operating range: (MSE <= 0.5, SNR >= 81.3, i.e. at QP <= -26)
    Their 14-bit base-band video rate is ~4.4 Gbps.
    In simple terms, 13-bit video data would be compressible; 14-bit video data would be better coded as raw / PCM.
    This occurs for AVC as well.

## Slide 4: Increase CABAC Efficiency
To address this issue, the addition of a “fixed bits” scheme to the entropy coding is proposed.
  Conceptually, the algorithm is (for a number of fixed bits BF):
  For each significant coefficient, C,
    split the value C into CMSB and CLSB, where CLSB comprises the BF least-significant bits of C.
    Code CMSB as for normal coefficients in a group.
    After the sign bits are coded, code the bits for CLSB using EP bins.
      (Sign bit hiding is based upon the entire coefficient C.)

## Slide 5: Further Detail
  In order that zero-value coefficients can still be signalled using only the significance map, the processing is slightly different.
    (This aids implementation since no changes are required to coefficient group, significance map or sign bit processing).
    Instead,
      CMSB = (abs(C) - 1) >> BF
      CLSB = (abs(C) - 1) - (CMSB << BF)
    The greater-than-1 map signals whether CMSB is greater than 0.
    The greater-than-2-flag signals whether CMSB is greater than 1.
      (noting that when BF is 0, these syntax elements have the same meaning as in the original entropy coding scheme)

## Slide 6: Proposed Response with Fixed Bits
The curves below use the recommended internal accuracy settings.
In addition to those, new curves with fixed bits are included (dotted).
  These have BF = max(0, int(QP / -6))

## Slide 7: Conclusion
The fixed bits system provides a significant coefficient coding efficiency improvement for low QPs.
  At QP = -48 (16-bit data), 35% saving in bit rate has been achieved.
  At QP = -12 (10-bit data), 10% saving in bit rate has been achieved.
  Results are now significantly better than using PCM or baseband.
It is recommended for all QPs <= -6.
The number of fixed bits BF would be determined by the encoder:
    A general estimate is BF = max(0, int(QP / -6)).
    This value is passed in the stream via the slice header.
    The use of fixed bits is indicated in the SPS header, and the presence of this flag is dependent on the profile.
See interactive Excel Spreadsheet “High Bit Depth Fixed Bit Results.xlsx”