## Slide 1: AHG5: Range Extensions and High Bit Depths Internal Accuracies
JCTVC-M0178
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Introduction
Range Extensions has been mandated to support higher bit depths.
  Currently 14 bit is specified, but from the outset, 16-bit was seen as a possibility.
This section of the proposal studies the capabilities of HEVC at higher bit depths.
  There are three other sections of this proposal that study other aspects.

## Slide 3: Required Operating Range
When considering operation at higher bit depths the target PSNR must also be higher.
  There is no point in a 16-bit system producing a maximum PSNR of 94.6 (ignoring compression efficiency).
    This equates to an MSE of 1.5, which can be achieved by rounding the coefficients to 14-bits and using an almost-lossless 14-bit system.
      i.e. the two least-significant bits in the output are effectively random noise.
  Note that at these high-bit depth operating points, numerical behaviour is paramount, since subjective behaviour is not observable to the human eye.

## Slide 4: Test Conditions
  The behaviour of the PSNR/bitrate curves for the full range of negative QPs is considered.
  MSEs of 1 (or less) are sought for all bit depths.
  RDOQ is disabled.
    At lower QPs, as coefficients become larger, RDOQ becomes less relevant.
  PCM mode is not used.
    This will prevent studies of the core image processing from being examined.
  The lowest 12 even QPs for each bit depth are studied.

## Slide 5: Test Conditions
  Traffic RGB (12-bit) from the Range Extensions test material and the 5 SVT HD sequences (16-bit) are used.
    Generally, only 10 frames are used from each, due to the large number of simulations required.
    The SVT sequences are quite noisy in nature, and generally suit 4x4 TU coding. Therefore, to encourage a different behaviour, two of the sequences have also been processed after a [1 2 1] or [1 4 6 4 1] filter has been applied horizontally and vertically to the source data.
  To aid analysis of transforms,
    The TU size was set to minimum values of 4, 8, 16 and 32.
      Noting that because the image dimensions are not divisible by 32, smaller TUs were permitted at the edges.

## Slide 6: Current HEVC Range Extensions
After making some small bug fixes to the HM10.0_RExt2.0 software, the following curves were produced:
  (OldTownCross, Green channel)

## Slide 7: Current HEVC Range Extensions
However, all TUs at high bit depths had selected to use transform skip.
Transform Skip was disabled, and the below curves were observed:

## Slide 8: Changes to Internal Accuracies
The results indicated that:
  The transform matrix precision is not high enough.
    Transform skip (TS) is always preferable.
  MAX_TR_DYNAMIC_RANGE is not high enough.
    This causes the PSNR to be limited to 70dB when coding 16-bit data.
    This also causes the curves to level off at 80dB (with TS disabled).
  In addition, there is clipping to MAX_TR_DYNAMIC_RANGE at:
      Output of quantiser.
      Input to inverse quantiser.
    This causes the roll-off for the extremely negative QPs.
      For larger TUs, this roll-off occurs at less negative QPs.

## Slide 9: Changes to Internal Accuracies
The following minima are recommended:
  MAX_TR_DYNAMIC_RANGE >= bitDepth + 5
  ENTROPY_CODING_DYNAMIC_RANGE >= bitDepth + 6
  Transform Precision >= bitDepth - 2
    Where ENTROPY_CODING_DYNAMIC_RANGE is the range at the input to the Entropy Encoder/output of the Entropy Decoder (replacing MAX_TR_DYNAMIC_RANGE).
  Note that for sequences that use 32x32 TUs, MAX_TR_DYNAMIC_RANGE equal to bitDepth + 6 produces a better rate-control response for the lowest 4 even QPs.
    See the low-pass filtered versions of DucksTakeOff and InToTree.
    These low QPs would be more applicable to these types of sequences.
    This would mean that ENTROPY_CODING_DYNAMIC_RANGE and MAX_TR_DYNAMIC_RANGE could be unified once more.

## Slide 10: New Response
The following curves were produced with:
  MAX_TR_DYNAMIC_RANGE = bitDepth + 5
  ENTROPY_CODING_DYNAMIC_RANGE = bitDepth + 6
  Transform matrix precision = 14
  Transform skip, RDOQ and PCM disabled

## Slide 11: New Response
For some sequences, using MAX_TR_DYNAMIC_RANGE = bitDepth + 6 is advantageous. In comparison:
  DucksTakeOff smoothed using a [1 2 1] filter.
  For MAX_TR_DYNAMIC_RANGE = bitDepth + 5:

## Slide 12: New Response
For some sequences, using MAX_TR_DYNAMIC_RANGE = bitDepth + 6 is advantageous. In comparison:
  DucksTakeOff smoothed using a [1 2 1] filter.
  For MAX_TR_DYNAMIC_RANGE = bitDepth + 6:

## Slide 13: Results
Accompanying this contribution are a number of interactive Excel spreadsheets.
  On all spreadsheets, a number of graph pages are available, where the blue shaded cells can be adjusted as required.
  “High Bit Depth Internal Accuracy Results.xlsx”
    This spreadsheet allows individual precision settings to be explored
  “High Bit Depth Fixed Bit Results.xlsx”
    This spreadsheet allows entropy coding refinements, as described in the following presentations, to be explored.
  “High Bit Depth AVC Comparison.xlsm”
    This spreadsheet compares the proposed system (which includes fixed bits and CABAC alignment) against AVC and HEVC RExt base.
    This includes results with (I)PCM mode enabled and disabled.
  “High Bit Depth Base HEVC Comparison.xlsm”
    This spreadsheet compares the proposed system (which includes fixed bits and CABAC alignment) against HEVC RExt base for all frames.

## Slide 14: Conclusion
To provide better support for higher bit depths, internal accuracies should be increased:
  MAX_TR_DYNAMIC_RANGE >= bitDepth + 6
  ENTROPY_CODING_DYNAMIC_RANGE >= bitDepth + 6
  Transform matrix precision >= bitDepth - 2
The following sections in this proposal/presentation:
  The next section of this proposal presents a scheme to significantly improve the coding efficiency at these higher bit-depth operating points.
  The 3rd section increases throughput of EP bins.
  A starting point for profile discussion is included in the 4th section of this proposal, based upon these results.