## Slide 1: JCTVC-M0197 AHG14: Color Gamut Scalablility using 3D LUT
P.Bordes
13th JCT-VC Meeting: Incheon, April 18-26, 2013

## Slide 2: AHG14: Color Gamut Scalable
  M24484 – “Requirements for the scalable enhancement of HEVC” (S-2.10)
  The scalability extension shall support :
    BL and EL with different color spaces
    Combination of color space scalability and spatial scalability.
    Tristimulus values in EL that can not be represented in the BL color space.
  Proposal: use of “Color Difference Predictor” function (see also L0334,K0241)

## Slide 3: Color Difference Predictor (1)
  The determination of the color transfer function is not straightforward because the content creation workflows may include deterministic processing but also non-deterministic operations.
  The last digital cameras used in Digital Cinema (DC) allow to capture video signal with wide color gamut and extended luminance range.
  Raw data represent much more information than what will be distributed/displayed

## Slide 4: Color Difference Predictor (2)
  Deterministic processing
    Color Space conversion: Rec.709 to Rec.2020 (basically not linear) only ?
      Besides, new video signal definitions, new display technology capabilities (e.g. OLED…), End-device rendering characteristics/capabilities adaptation ?
  Non-deterministic operations
    Bit-depth scaling / tone mapping: luminance range mapping vs Reference Output Display characteristics (ODT) (ex: 16 bits vs 8 or 10 bits)
    Color grading: color balancing vs reference display traduces the artistic intent (film director)

## Slide 5: Proposed Color Difference Predictor
  Rationale
  To address a wide range of CGS applications: without any a-priori on the “Color Difference Predictor” model
  Proposal: 3D Color Look-Up Table (LUT)
  3D LUT can be considered as a sub-sampling of the 3D color space 1, where each vertex is associated with a color triplet corresponding to the color space 2 (predicted) values.
  For a given BL color sample (color space 1), the computation of its prediction in (EL) color space 2 is made using tri-linear interpolation

## Slide 6: 3D LUT Coding
  Rationale
  Octree based description of the 3D LUT: unused (or less used) 3D color space regions are encoded with coarsely lattice size
  At most 8 vertices per octant
  Each color component of a vertex is predicted with previously encoded color components of neighboring parent octant vertices (tri-linear interpolation)
  Only non-zero residuals tri-color components are encoded

## Slide 7: 3D LUT Coding
  Advantages
  Many Color processing tools uses 3D LUTs to represent and save their intermediate and final color grading operations. In these cases, the 3D LUT information can be made available to the encoder easily
  The 3D LUT size (number of vertices in one direction), is a parameter read in the bit-stream. In that way, the encoder may choose the best trade-off between “Color Difference Predictor” module accuracy and encoding cost
  3D color LUT interpolation module for color conversion is implemented in many STBs and display devices (graphics card).
  If size=1 (one single octant with 8 vertices), and the color components of the vertices are set appropriately (see 6-Annex), then the 3D LUT is equivalent to the Gain-Offset model previously proposed in JCTVC-L0334.

## Slide 8: Color Gamut Scalability Tests
  (1) Color Grading
  Use Color Grading tool (CineStyle) to create 3D Color LUTs

## Slide 9: Color Gamut Scalability Tests
  (2) Color Space conversion Rec.709 to Rec.2020

## Slide 10: Conclusions
  Proposal of a Color Gamut Scalability model based on 3D LUT
    Color graded content experiments (8 bits)
    Rec.709 – rec.2020 experiments (8 bits)
  A generic model scalable in complexity and hence accuracy:
    Allows addressing low complexity use cases equivalent to GO model previously proposed in JCTVC-L0334
    Allows addressing more general use cases where the Color mapping function in between the BL and EL is more complex than a simple linear transformation.
  Propose to include CGS in SHM
  Propose JCT-VC to create a HEVC Scalable Extensions Core Experiment in order to assess Color Gamut Scalability inter-layer prediction related methods