## Slide 1
Independent tile upsampling for SHVC (JCTVC-M0198)
Karsten Sühring, Robert Skupin, Yago Sanchez, Thomas Schierl

## Slide 2: Introduction
HEVC facilitates parallelism of tiles with loop filter restrictions
Tool restrictions in SHVC should enable layer parallelism
Currently, picture based upsampling in SHVC restricts layer parallelism
Proposal: flag controlled restriction of upsampling filter to not cross tile boundaries

## Slide 3: Proposed solution
      Upsampling of individual tiles through G.8.1.4 Resampling process for inter layer reference pictures (JCTVC-L1007)
      When the proposed constraint is enabled, samples location are clipped such that they are located within the reference layer tile
Recon BL tileId 0
Recon BL tileId 1
Recon BL tileId 2
Recon BL tileId 3
Upsampled BL
tileId 0

## Slide 4: Proposed solution
add restriction flag to PPS extension that indicates upsampling restriction for a bitstream subset
pic_parameter_set_extension( ) { | Descriptor
… | 
if( tiles_enabled_flag ) { | 
independent_tile_upsampling_flag | u(1)
} | 
… | 
} | 

## Slide 5: Proposed solution
add restriction flag to PPS extension that indicates upsampling restriction for a bitstream subset
independent_tile_upsampling_idc signals whether the spatial upsampling filter shall be constrained at tile boundaries. If independent_tile_upsampling_flag is equal to 1, no base layer samples that lie outside the picture area that corresponds to the enhancement layer tile shall be used for upsampling. If independent_tile_upsampling_flag is equal to 0 the upsampling filter is not constrained.

## Slide 6: Simulation results - RefIdx
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.1% | 0.1% |  |  | 
Class B | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Overall (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
EL only (Test vs Ref) | 0.1% | 0.2% | 0.2% | 0.2% | 0.2% | 0.2%
Enc Time[%] | 97.7% |  |  | 100.1% |  | 
Dec Time[%] | 94.2% |  |  | 95.4% |  | 
BL Match | Matched |  |  | Matched |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Overall (Test vs Ref) | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
EL only (Test vs Ref) | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 98.4% |  |  | 100.0% |  | 
Dec Time[%] | 93.3% |  |  | 95.9% |  | 
BL Match | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
Overall (Test vs Ref) | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
EL only (Test vs Ref) | 0.1% | 0.0% | 0.1% | 0.1% | 0.2% | 0.2%
Enc Time[%] | 100.0% |  |  | 101.5% |  | 
Dec Time[%] | 96.2% |  |  | 95.1% |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 7: Simulation results - IntraBL
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.1% | 0.1% |  |  | 
Class B | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Overall (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
EL only (Test vs Ref) | 0.1% | 0.1% | 0.2% | 0.2% | 0.2% | 0.2%
Enc Time[%] | 100.1% |  |  | 99.7% |  | 
Dec Time[%] | 98.7% |  |  | 95.7% |  | 
BL Match | Matched |  |  | Matched |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.1% | 0.1% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall (Test vs Ref) | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
EL only (Test vs Ref) | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 100.4% |  |  | 100.0% |  | 
Dec Time[%] | 96.9% |  |  | 95.4% |  | 
BL Match | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | -0.1%
Overall (Test vs Ref) | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1%
EL only (Test vs Ref) | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | 0.0%
Enc Time[%] | 100.1% |  |  | 100.5% |  | 
Dec Time[%] | 96.7% |  |  | 96.1% |  | 
BL Match | Matched |  |  | Matched |  |