## Slide 1
Layer decoding delay indication for SHVC and 3D/MV-HEVC (JCTVC-M0200)
Robert Skupin, Karsten Sühring, Yago Sanchez, Thomas Schierl

## Slide 2: Introduction
JCT3V-C0062 proposed delay signalling based on CTUs to facilitate layer parallelism
HEVC high level parallelism tools for spatial segmentation
Spatial segments can also enable layer parallelism
    Begin EL processing before BL processing is completed
    Referenced BL area for EL (spatial segement) needs to be available
Proposal: Signal delay in units of CTBs or spatial segments

## Slide 3: Proposed solution
      Depending on spatial segmentation tools used:
    Signal a delay in units of slices, tiles, wavefront ctb rows wrt the collocated spatial segment in the reference layer
      Based on flag, signal a delay in units of CTBs
Reference Layer
Dependent
Layer
Collocated area
Indicated delay
WPP
Tiles
CTB based

## Slide 4: Proposed solution
Syntax: two syntax elements in the SPS extension VUI
sps_extension_vui_parameters( ) { | Descriptor
… | 
if( bitstream_restriction_flag ) { | 
ctb_based_delay_enabled_flag | u(1)
min_spatial_segment_delay | ue(v)
… | 
} | 
… | 
} | 

## Slide 5: Proposed solution
Semantics:
ctb_based_delay_enabled_flag being equal to 1 indicates that the delay signalled with min_spatial_segment_delay is given in units of CTBs. ctb_based_delay_enabled_flag indicates that min_spatial_segment_delay is not given in units of CTBs.
min_spatial_segment_delay describes the decoding delay of the current layer introduced by coding dependencies with respect to the corresponding base layer in terms of spatial segments or CTBs.

## Slide 6: Proposed solution
Semantics:
… if ctb_based_delay_enabled_flag is equal to 1:
Reference Layer: CtbSizeYA, PicWidthInCtbsYA, ctbAddrRsA
Dependent Layer: CtbSizeYB, PicWidthInCtbsYB, ctbAddrRsB
CtbScalingFactorBA = ( PicWidthInCtbsYA / PicWidthInCtbsYB )
CtbRowBA(ctbAddrRs) =
Ceil( ( Floor( ctbAddrRs / PicWidthInCtbsYB ) + 1 ) * CtbScalingFactorBA) - 1
CtbColBA(ctbAddrRs) =
Ceil( ( ( ctbAddrRs % PicWidthInCtbsYB ) + 1 ) * CtbScalingFactorBA ) - 1
When decoding the CTB with ctbAddrRsB of the current enhancement layer/view B, all necessary base layer resources are available when the base layer CTB with ctbAddrRsA being equal to PicWidthInCtbsYA * CtbRowBA( ctbAddrRsB) + CtbColBA(ctbAddrRsB) + min_spatial_segment_delay is decoded completely.

## Slide 7: Proposed solution
Semantics:
… if ctb_based_delay_enabled_flag is equal to 0 and no Tiles, no WPP:
…all base layer resources for the decoding process of any slice segment A of the current layer in bit stream order are available when the first slice segment C that follows (min_spatial_segment_delay -1) slices in bitstream order in the base layer after the last slice segment B in bitstream order that contains at least a part of the same image area with respect to slice A in the current layer is decoded completely.

## Slide 8: Proposed solution
Semantics:
… if ctb_based_delay_enabled_flag is equal to 0 and Tiles:
…all base layer resources for the decoding process of any tile A of the current layer in bitstream order are available when the first tile C that follows (min_spatial_segment_delay -1) tiles in bitstream order after the last tile B in bitstream order that contains at least a part of the same image area with respect to tile A are completely decoded.

## Slide 9: Proposed solution
Semantics:
… if ctb_based_delay_enabled_flag is equal to 0 and WPP:
…all base layer resources for the decoding process of the any CTB row A in the current layer are available when the first CTB row C that follows (min_spatial_segment_delay -1) CTB rows after the last CTB row B of the base layer that covers at least part of the same image area with respect to CTB row A of the enhancement layer in bitstream order are completely decoded.

## Slide 10: Summary
      Depending on spatial segmentation tools used:
    Signal a delay in units of slices, tiles, wavefront ctb rows wrt the collocated spatial segment in the reference layer
      Based on flag, signal a delay in units of CTBs
Reference Layer
Dependent
Layer
Collocated area
Indicated delay
WPP
Tiles
CTB based