## Slide 1
Ultra-low delay multi-layer decoding by interleaving of decoding units in SHVC and 3D/MV-HEVC (JCTVC-M0204)
Karsten Sühring, Robert Skupin, Yago Sanchez, Thomas Schierl

## Slide 2: Introduction
HEVC allows parallelization and ultra-low decoding based on high-level parallelization tools such as tiles, wavefronts and slice segments
Decoding units allow to access sub-pictures in the bitstream
In order to support ultra-low delay effectively in SHVC and 3D/MV-HEVC parallel decoding of decoding units of different layers would be desirable

## Slide 3: Proposed solution
Interleave DUs from the same access unit (at same time instant)
  no interleaving
  with interleaving
Decoding units ordered so that necessary reference sub-pictures are available

## Slide 4: Access unit definition
Since an access unit is a set of NAL units in consecutive order, NAL units of different layers have to pertain to the same access unit to allow interleaving
However, if unequal GOP sizes in layers are to be allowed (e.g. proposed in JCTVC-L0171) NAL units of different layers should be contained in different access units

## Slide 5: Access unit definition
Proposed rule:
  Consecutive layers that share the same display time are collected in one access unit.
  Consecutive layers that do not share the same display time will start new access units.
    No interleaving shall be applied within different GOP structures

## Slide 6: Access unit definition
Proposed rule:
Same AU
Different AUs

## Slide 7: Proposed solution
du_interleaving_enabled_flag
du_interleaving_enabled_flag equal to 1, specifies that decoding units of different coded view/layer picture components may be interleaved within an access unit. When du_interleaving_enabled_flag is equal to 0, for each view/layer picture component, all decoding units follow each other directly in the bitstream (i.e. no interleaving is used.)

## Slide 8: VLC NAL unit order
Basic ordering rule for interleaving:
VCL NAL unit order is restricted so that no dependency to future VCL NAL units exists
For simplicity the following definitions are using min_spatial_segment_delay which is proposed in JCTVC-M0200 but not a requirement for this proposal.

## Slide 9: VLC NAL unit order
VCL NAL unit order within a layer as for HEVC
Let sliceSegAddrA and sliceSegAddrB be the slice_segment_address values of any two coded slice segment NAL units A and B within the same coded layer picture component. When either of the following conditions is true, coded slice segment NAL unit A shall precede the coded slice segment NAL unit B:
    TileId[ CtbAddrRsToTs[ sliceSegAddrA ] ] is less than TileId[ CtbAddrRsToTs[ sliceSegAddrB ] ].
    TileId[ CtbAddrRsToTs[ sliceSegAddrA ] ] is equal to TileId[ CtbAddrRsToTs[ sliceSegAddrB ] ] and CtbAddrRsToTs[ sliceSegAddrA ] is less than CtbAddrRsToTs[ sliceSegAddrB ]

## Slide 10: VLC NAL unit order
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag equal to 0
min_spatial_segment_delay-1 slices more necessary in layer N (red) from the “collocated” slice onwards to decode a slice in layer N+1 (blue)
PicWidthInCtbsYA * CtbRowBA(sliceSegAddrC-1) + CtbColBA(sliceSegAddrC-1) shall be smaller than sliceSegAddrA-1

## Slide 11: VCL NAL unit order
tiles_enabled_flag is equal to 0 and entropy_coding_sync_enabled_flag equal to 1
slice A with sliceSegAddrA and slice B with sliceSegAddrB are consecutive NAL units from different layers where the layer containing slice B depends on the layer containig slice A
(CtbRowBA(sliceSegAddrB) – Floor((sliceSegAddrA) / PicWidthInCtbsYA) + 1) is equal or greater than min_spatial_segment_delay

## Slide 12: VCL NAL unit order
tiles_enabled_flag is equal to 1 and entropy_coding_sync_enabled_flag equal to 0
slice A with sliceSegAddrA is any slice in layer N (red) and slice B with sliceSegAddrB the next slice in layer N+1 (blue)
TileId[ CtbAddrRsToTs[ PicWidthInCtbsYA * CtbRowBA(sliceSegAddrB-1) + CtbColBA(sliceSegAddrB-1) ] ] - TileId[ CtbAddrRsToTs[ sliceSegAddrA-1] ] shall be equal or greater than min_spatial_segment_delay

## Slide 13: End
Following slides contain proposed definitions for reference

## Slide 14: Definitions
access unit: A set of NAL units that are associated with each other according to a specified classification rule, are consecutive in decoding order, and contain exactly one coded picture.
coded layer picture component: A coded representation of a layer picture component containing all coding tree units of a layer picture component.
coded picture: A coded representation of all coded layer picture components at a specific display time.
layer picture component: An array of luma samples in monochrome format or an array of luma samples and two corresponding arrays of chroma samples in 4:2:0, 4:2:2, and 4:4:4 colour format, which coded representation consists of the NAL units from a specific layer among all NAL units in an access unit.
picture: A picture is a set of all layer picture components at a specific display time.

## Slide 15: Definitions
If the specifications shall allow different GOP structures per layer or view, the following alternatives are proposed for coded picture and picture:
coded picture: A coded representation of a one or more coded layer picture components that are consecutive in bitstream order and are displayed at the same display time.
picture: A picture is a set of one or more layer picture components that are consecutive in bitstream order and are displayed at the same display time.