## Slide 1: M0209/ D0082: On Design for Signaling Inter-layer Prediction
Sachin Deshpande
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
A “strawman” design for signaling of inter-layer prediction indication was discussed during 12th JCTV-VC meeting.
The syntax and semantics for this design considered for signaling inter-layer prediction indication was described in JCTVC-L0449.
This document proposes following additions to the design considered for signaling inter-layer prediction.
  Proposal 1: A change to the marking process for sub-layer non-reference pictures not needed for inter-layer prediction is proposed.
  Proposal 2: A change to the decoding of inter-layer reference picture set and reference picture list construction is proposed.
<number>
JCTVC-L0449: Design Considered for Signaling
Inter-layer Prediction Indication
Notes: <number>

## Slide 3: Proposal 1 (1/2)
A change to the marking process for sub-layer non-reference pictures not needed for inter-layer prediction is proposed.
When using the proposed change in the marking process sub-layer non-reference pictures of target layers could be marked “unused for reference” based on the VPS signalling regarding use of sub-layer and RAP pictures of various layers for inter-layer prediction.
It is asserted that this proposed approach has the advantage that additional sub-layer non-reference pictures of target layers could be marked “unused for reference”. Thus DPB size / memory could be reduced.
<number>
Notes: <number>

## Slide 4: Proposal 1 (2/2)
The proposed changes are highlighted compared to JCTVC-L1008 SHVC draft text 1 and JCTVC-C1004 MV-HEVC draft text 3 and using syntax defined in JCTVC-L0449.
<number>
Notes: <number>

## Slide 5: Proposal 2 (1/3)
A change to the decoding of inter-layer reference picture set and reference picture list construction is proposed.
When using our proposed change in the decoding process for inter-layer reference picture set an additional check is performed regarding the TemporalId of the inter-layer pictures for pictures with nuh_layer_id values corresponding to the layers which are direct reference layers for the current layer with picture order count equal to the current picture.
  If the value of the TemporalId for the said inter-layer picture is greater than max_sublayer_for_ilp_plus1[i]-1 then those inter-layer pictures are not added to the inter-layer reference picture set.
  Additionally if the value of max_sublayer_for_ilp_plus1[i] is zero then the said inter-layer picture is not added to the inter-layer reference picture set unless it is a RAP picture.
  The inter-layer reference picture set is then used for reference picture list construction.
<number>
Notes: <number>

## Slide 6: Proposal 2 (2/3)
<number>
The proposed changes are highlighted compared to JCTVC-L1008 SHVC draft text 1 and JCTVC-C1004 MV-HEVC draft text 3 and using syntax defined in JCTVC-L0449.
Notes: <number>

## Slide 7: Proposal 2 (3/3)
<number>
Notes: <number>

## Slide 8: Conclusion
A “strawman” design for signalling of inter-layer prediction indication was discussed during 12th JCTV-VC meeting and was described in JCTVC-L0449.
This document proposes additions to the design considered for signaling inter-layer prediction.
  Proposal 1: A change to the marking process for sub-layer non-reference pictures not needed for inter-layer prediction is proposed.
  Proposal 2: A change to the decoding of inter-layer reference picture set and reference picture list construction is proposed.
We propose to adopt JCTVC-L0449 and our two proposals in SHVC and MV-HEVC draft texts.
<number>