## Slide 1: Follow-up of JCTVC-M0211
Ohji Nakagami

## Slide 2: Maximum coded bits for a scaling list set
Scaling list set
  4x4TU: Y/Cb/Cr; intra/inter
  8x8TU: Y/Cb/Cr; intra/inter
  16x16TU: Y/Cb/Cr; intra/inter (stored in 8x8 + DC)
  32x32TU: Y; intra/inter (store in 8x8 + DC)
  Each element is 8bit (-128 to 127) + 7bit (suffix)
Bits required for the worst case per set
  (4*4*3*2 + 8*8*3*2 + (8*8+1)*3*2 + (8*8+1)*2) * 15[bit]
  = 15,000[bit]

## Slide 3: Typical coded bits for a scaling list set
(Subtest2.1, option2b) | symmetry1 | symmetry2 | symmetry3 | symmetry4 | symmetry5 | symmetry6
Total Bit | 1312 | 850 | 1712 | 1704 | 1288 | 1390
(Subtest2.1, option2b) | asymmetry1 | asymmetry2 | asymmetry3 | asymmetry4 | asymmetry5 | asymmetry6
Total Bit | 1788 | 1278 | 2578 | 3896 | 1936 | 2240
Cited from JCTVC-H0230
The matrices (=(a)symmetroy1-6) were chosen as CE4 condition at that time.
Option2b is a current scheme.
From the results, 1K ~ 4K bits are necessary for a scaling list set.

## Slide 4: Bitrate for scaling list
Scaling list would be changed in GOP level, sometimes in picture by picture in some application. (Ref: JCTVC-E056)
Picture by picture change case
  Worst case scaling list
    15[kbit] * 60 [fps] = 900 [kbps]
  Typical scaling list
    1~ 4 [kbit] * 60 [fps] = 60 ~ 240 [kbps]
GOP-level change case
  Worst case scaling list
    15 [kbit] * 2~4 [fps] = 30 ~ 60[kbps]
  Typical scaling list
    1~ 4 [kbit] * 2~4 [fps] = 2 ~ 16 [kbps]

## Slide 5: backup

## Slide 6: Memory size to store a scaling list set
Scaling list set
  4x4TU: Y/Cb/Cr; intra/inter
  8x8TU: Y/Cb/Cr; intra/inter
  16x16TU: Y/Cb/Cr; intra/inter (stored in 8x8 + DC)
  32x32TU: Y; intra/inter (store in 8x8 + DC)
  Each element is 8bit
Memory size per set
  (4*4*3*2 + 8*8*3*2 + (8*8+1)*3*2 + (8*8+1)*2) * 8 [bit]
  = 8000[bit]