## Slide 1: M0214: On Color Gamut Scalable Video Coding
Sachin Deshpande, Louis Kerofsky, Andrew Segall
Sharp Labs of America
<number>
Notes: <number>

## Slide 2: Introduction
The upcoming deployment of UHDTV will use wide color gamut.
  HD uses the ITU-R BT.709 recommendation, while UHDTV will use the ITU-R BT.2020 recommendation.
  A key difference between BT.709 and BT.2020 is that the color gamut of UHDTV is significantly larger than HD. A motivation for our proposed support for color gamut scalability is this difference between color gamut of base and enhancement layers when complying with the ITU-R recommendations.
With the scalable extension design, it is important to completely address the requirements of future applications that require scalability.
  A use case for the spatial scalability is to support UHDTV spatial resolution enhancement layer with HD resolution base layer.
  M24484 - Requirements for the scalable enhancement of HEVC section 2.10 captures that:
    The scalability extension shall support a base and enhancement layer with different color spaces.
    The scalability extension shall support a combination of color space scalability and spatial scalability.
    The scalability extension shall support tristimulus values in the enhancement layer that can not be represented in the base layer color space.
Typical consumer applications using BT.709 have an 8-bit sample depth while BT.2020 only defines 10-bit and 12-bit sample depths.
  Bit-depth scalability thus becomes an essential part of supporting color gamut scalability between BT.709 and BT.2020
  Interlayer prediction between FHD and UHD layers thus relies upon defining prediction across sample bit-depths.
<number>
Notes: <number>

## Slide 3: Proposals Summary
Previously we presented technique for achieving color gamut scalable video coding
  JCTVC-K0264: based on extensions of the HEVC design and
  JCTVC-L0334: based on the SMuC design
This document proposes changes to SHVC draft text and test model to support color gamut scalability
This document proposes:
1. A new bit depth scaling process for reference pictures to support color gamut scalable coding.
2. It additionally proposes signaling color gamut and bit depth information regarding each layer in VPS extension.
<number>
Notes: <number>

## Slide 4: Proposal 1 (1/2)
A new bit depth scaling process for reference pictures to support color gamut scalable coding is proposed.
The proposed changes are highlighted compared to JCTVC-L1007_v3. These changes are defined in Annex G (Reference index based scalable extension) but also apply to Annex H (Texture based scalable extension) where they are proposed to be invoked in the similar manner after invoking H.8.8.3 (which invokes G.8.1.4.3) and after invoking H.8.8.4 (which invokes G.8.1.4.4).
<number>
Notes: <number>

## Slide 5: Proposal 1 (2/2)
<number>
Notes: <number>

## Slide 6: Proposal 2 (1/2)
The information about bit depth of luma and chroma components of each layer and about chromaticity coordinates of the source primaries of each layer can be useful for session negotiation in allowing end devices to select layers to decode based on their bit depth and color support capability.
This document proposes signaling color gamut scalability and bit depth information regarding layers in VPS extension.
The proposed changes are highlighted compared to JCTVC-L1008 draft text specification
<number>
Notes: <number>

## Slide 7: Proposal 2 (2/2)
<number>
bit_depth_layer_luma_minus8[ id ] + 8 specifies the bit depth of the samples of the luma array for the layer with layer id id, as specified by
BitDepthLY [ id ] = 8 + bit_depth_layer_luma_minus8[ id ]bit_depth_layer_luma_minus8[ id ] shall be in the range of 0 to 6, inclusive.
bit_depth_layer_chroma_minus8[ id ] + 8 specifies the bit depth of the samples of the chroma arrays for the layer with layer id id, as specified by
BitDepthLC [ id ] = 8 + bit_depth_layer_chroma_minus8[ id ]bit_depth_layer_chroma_minus8[ id ] shall be in the range of 0 to 6, inclusive.
layer_color_gamut[ id ] equal to 1 specifies that the chromaticity coordinates of the source primaries for layer id are defined as per Rec. ITU-R BT.2020. layer_color_gamut[ id ] equal to 0 specifies that the chromaticity coordinates of the source primaries for layer id are defined as per Rec. ITU-R BT.709.
Notes: <number>

## Slide 8: Conclusion
This document proposes:
1. A new bit depth scaling process for reference pictures to support color gamut scalable coding.
2. Signaling color gamut scalability and bit depth information regarding layers in VPS extension.
We propose to adopt the proposed changes in SHVC and MV-HEVC.
<number>