## Slide 1: JCT-VC M0215: Non-SCE4: Adaptive up-sampling of base layer picture using Simplified Separable bilateral filters
Jie Zhao, Kiran Misra, Andrew Segall
Presenter: Andrew Segall

## Slide 2: Introduction
Background:
  In SCE4.2.6 (JCTVC-M0213), we proposed using a bi-lateral filter for inter-layer texture prediction. Similarly, SCE4.2.5 also studied bi-lateral filtering.
  In the SCE, we observed good coding efficiency improvement – especially for 2x compression.
    4.2.6 achieved ~1.4% BD rate improvement
    4.2.5 achieved ~1%BD rate improvement.
  The primary difference between 4.2.5 and 4.2.6 is the filter size.
    4.2.6: 5x5
    4.2.5: 3x3

## Slide 3: Goal of Contribution
Contribution of this proposal:
  Here, we provide a lower complexity operation point for the approach.
  Specific characteristics
    Filter is separable (3x1)
    Filter applied directly after computing an upsampled pixel – removing need for additional buffering.
    Single lookup table for weight calculations
    Reciprocal LUT for normalization
    Complexity: 9 mults/15 adds per sample (luma+chroma).
      Compared to 37 mults/32 adds for upsampler

## Slide 4: Algorithm
Approach
  Apply bilateral filter during separable upsampling operation
  Input to filter
    Current pixel (after interpolation)
    Left and right neighbors from low-resolution input
  Filter

## Slide 5: Algorithm

## Slide 6: Algorithm
Main novelty/difference from previous work (SCE4.2.6):
  Separable filter
    Lower complexity and can be combined into upsampling process.
  Only integer-pel and single interpolated pixel used for calculation
    Removes dependency on neighboring pixels
    Reduces delay/buffering.
  No additional memory access.

## Slide 7: Signaling
Signaled at CU level
  Additionally, slice level signaling to enable/disable the tool

## Slide 8: Experimental Result
Experimental results
  SHM1.0 IntraBL framework.
  SCE4 test configuration.
  Decoder timing is from picture based implementation.

## Slide 9: Experimental Result
Results continued…
Average 0.9/0.8/1.0% rate reduction for AI/RA/LD_P 2X cases.
0.2/0.0/0.3% rate reduction for AI/RA/LD_P 1.5X cases.

## Slide 10: Experimental Result
Supplemental timing information
  We also implemented CU based upsampler/filter at decoder side into SHM1.0 and into our test software.
  1st tables shows the speedup of CU based upsampler vs. picture based upsampler in SHM1.0.
  2nd table shows the decoder timing ratio of our proposed tool vs. SHM1.0 anchor, both using CU based upsampler.
Decoder Timing of SHM1.0 with CU based upsampler
vs. SHM1.0 with picture based upsampler
Decoder Timing of SHM1.0 with CU based upsampler
vs. SHM1.0 with picture based upsampler

## Slide 11: Complexity (Worst Case)
Worst case complexity analysis
  9 multiplication and 15 additions for each sample (including both luma and chroma)
  By comparison – fixed upsampler requires 37 multiplication and 32 adds.

## Slide 12: Complexity
Memory bandwidth
  Complexity results shown in the table include both the proposed tool and the existing fixed upsampler.
  Shows no additional memory access (as asserted)
  Changes are from mode decision.

## Slide 13: Summary
Proposed a non-linear and content adaptive bilateral filtering process
  Separable filter combined with upsampler
Coding efficiency improvement of 0.9/0.8/1.0% for AI/RA/LD_P 2X spatial scalability respectively, 0.2/0.0/0.3% rate reduction for AI/RA/LD_P 1.5x scalability.
Complexity
  9 mults/15 additions; no increase in memory bandwidth
Cross checked by Samsung (JCTVC-M0250)
Software distributed to SCE4 members on April 4
Propose to adopt into SHM

## Slide 14: JCT-VC M0215: Non-SCE4: Adaptive up-sampling of base layer picture using Simplified Separable bilateral filters
Jie Zhao, Kiran Misra, Andrew Segall
Presenter: Andrew Segall