## Slide 1: JCTVC-M0216 SCE2: Results of Test 1.1 on skipped ILTP block signaling in Inter slice
<number>
Do-Kyoung Kwon and Madhukar Budagavi
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
In SHM-1.0, skipped IntraBL CU is signaled by using rqt_root_cbf in all slice types
It is proposed to signal skipped IntraBL CU by using cu_skip_flag in Inter slice (P, B) to improve coding efficiency
  cu_skip_flag is set to 1 by either inter skip mode or IntraBL mode
  If cu_skip_flag is 1, merge_idx is signaled only if CU is not IntraBL
For Intra (I) slice, there is no change required
Notes: <number>

## Slide 3: Proposed CU-level signaling
<number>
coding_unit( x0, y0, log2CbSize ) { | Descriptor
…… | 
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
if( nuh_layer_id > 0 && InterLayerTextureRlEnableFlag) | 
texture_rl_flag[ x0 ][ y0 ] | ae(v)
if( cu_skip_flag[ x0 ][ y0 ] && !texture_rl_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( nuh_layer_id > 0 && InterLayerTextureRlEnableFlag) | 
texture_rl_flag[ x0 ][ y0 ] | ae(v)
if( ! texture_rl_flag[ x0 ][ y0 ] ) { | 
…… | 
} | 
if( !pcm_flag[ x0 ][ y0 ] ) { | 
if(( PredMode[ x0 ][ y0 ] != MODE_INTRA && !(PartMode = = PART_2Nx2N && merge_flag[x0][y0])) ¦¦ (slice_type = = I && PredMode[ x0 ][ y0] = = MODE_TEXTURE_RL)) | 
rqt_root_cbf | ae(v)
…… | 
} | 
} | 
} | 
Notes: <number>

## Slide 4: Experimental results
<number>
Provides luma BD-rate gains up to 0.3% (for LB-P and LD-B 1.5x)
Notes: <number>

## Slide 5: Conclusions
<number>
Proposed to signal skipped IntraBL CU by using cu_skip_flag in Inter slice
Signaling position of texture_rl_flag is changed without additional signaling of syntax element
Improved luma BD-rate up to 0.3%
Notes: <number>