## Slide 1: JCTVC-M0217 SCE2: Results of Test 1.2 and Test 1.3 on inter-layer texture prediction
<number>
Do-Kyoung Kwon and Madhukar Budagavi
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
SHM-1.0 supports inter-layer texture prediction (ILTP) for 2Nx2N block (CU level)
In Test 1.2, it is proposed to support ILTP for non-2Nx2N block (PU level) by modifying merge process
In Test 1.3, Test 1.2 is combined with Test 1.1
No additional signaling of syntax elements
Notes: <number>

## Slide 3: PU-level ILTP by the merge process (Test 1.2)
<number>
Modified merge candidate list derivation
Modified PU decoding process using merge_idx
  After checking the first 4 candidates, if numMergeCand < 4 ,
  ILTP mode is added into the merge candidate list,
  For ILTP mode, refIdLx = -1 and predFlagLx = 0 for x = 0, 1
  If derived refIdxLx = -1 for x= 0, 1,
  PU is predicted from the collocated BL

## Slide 4: Experimental results (Test 1.2)
<number>
Provides a luma BD-rate gains of 0.1% ~ 0.4%
Notes: <number>

## Slide 5: Experimental results (Test 1.3)
<number>
Provides a luma BD-rate gains of 0.1% ~ 0.6%
  Test 1.1 and Test 1.2 show additive gain
Notes: <number>

## Slide 6: Conclusions
<number>
In Test 1.2, ILTP for non-2Nx2N block (PU level) was enabled by modifying merge process
In Test 1.3, Test 1.2 was combined with Test 1.1
Test 1.2 improved a luma BD-rate by 0.1% ~ 0.4%
Test 1.1 + Test 1.2 provide a luma BD-rate gain of 0.1% ~ 0.6%, but do not introduce new syntax elements
Notes: <number>