## Slide 1: JCTVC-M0219 Reference-layer cropping offsets signaling in SHVC
<number>
Do-Kyoung Kwon and Madhukar Budagavi
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
JCTVC-L0178 proposed to use output ref layer picture for inter-layer prediction and signals syntax elements for scaled ref offset in SPS
If output ref layer picture is much smaller than coded ref layer picture, coding efficiency may decrease
This contribution proposes to signal ‘ref layer offsets’ (as well as ‘scaled ref layer offsets’) so that any ref layer picture area can be used for inter-layer prediction
Notes: <number>

## Slide 3: Proposed syntax elements
<number>
If scaled_ref_layer_offset_flag is equal to 0, all scaled ref layer offsets are inferred to be 0.
ScaledRefLayerLeftOffset = 2 * scaled_ref_layer_left_offset
ScaledRefLayerRightOffset = 2 * scaled_ref_layer_right_offset
ScaledRefLayerTopOffset = 2 * scaled_ref_layer_top_offset
ScaledRefLayerBottomOffset = 2 * scaled_ref_layer_bottom_offset
If ref_layer_offset_flag is equal to 0, all ref layer offsets are inferred to be 0.
RefLayerLeftOffset = 2 * ref_layer_left_offset
RefLayerRightOffset = 2 * ref_layer_right_offset
RefLayerTopOffset = 2 * ref_layer_top_offset
RefLayerBottomOffset = 2 * ref_layer_bottom_offset

## Slide 4: Applications of the proposed offsets (1)
Arbitrary ROI of ref layer picture can be used for inter-layer prediction and scaled to a whole enhancement layer
  Non-zero ref layer offsets
  Zero scaled ref layer offsets
Output ref layer picture (instead of coded ref layer picture) can be used for inter-layer prediction by signaling ref layer offsets same to output offsets
<number>

## Slide 5: Applications of the proposed offsets (2)
Arbitrary ROI of ref layer picture can be used for inter-layer prediction and scaled to any area in enhancement layer
  Non-zero ref layer offsets
  Non-zero scaled ref layer offsets
<number>

## Slide 6: Conclusions
Proposed to signal ‘ref layer offsets’ and ‘scaled ref layer offset’ in SPS
Any ROI of ref layer picture can be used for inter-layer prediction and can be mapped to any area in enhancement layer
When output ref layer picture is smaller than coded ref layer picture, possible coding efficiency improvement by utilizing larger area of ref layer picture for inter-layer prediction
<number>