## Slide 1: JCTVC-M0234 Combined Scalable + Multiview HEVC coding results
<number>
Do-Kyoung Kwon and Madhukar Budagavi
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
HEVC extension is being designed to support scalable (SHVC) and multi-view coding (MV-HEVC) at the same time
However, software and results are not available for SHVC + MV-HEVC
In this contribution,
  Inter-view prediction is implemented on top of SHM-1.0
    Inter-view prediction based on HTM-6.0
    Inter-view prediction works with both TextureRL and RefIdx approaches
  4 layers (D0V0, D0V1, D1V0 and D1V1) are coded for multi-view SNR coding application
  Performances of inter-layer prediction are evaluated
  TextureRL and RefIdx approaches are evaluated in the SHVC + MV-HEVC context
Notes: <number>

## Slide 3: Inter-layer prediction structures
The following inter-layer prediction structures are evaluated
  Simulcast
    All layers are coded independently
  MV-HEVC simulcast
    V1 is predicted from V0 at the same D layer by using inter-view prediction
  SHVC + MV-HEVC
    In addition to inter-view prediction, D1 is predicted from D0 at the same V layer
<number>
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
Simulcast
MV-HEVC simulcast
SHVC + MV-HEVC
BL_D
EL_D

## Slide 4: Test sequences
Left and right views of MV-HEVC test sequences are used for test
D0 and D1 have the same resolution (i.e. SNR scalability)
Same QP for the view pictures at the same D layer.
  D0 (i.e. D0V0 and D0V1) is coded using QP = 26, 30. 34 and 38
  Delta QP for D1 (i.e. D1V0 and D1V1) is set to -4 and -6.
<number>
 | V0 | V1 | Frames
1 | Ballon_1024x768_1.yuv | Ballon_1024x768_5.yuv | 300
2 | Dancer_c_1_1920x1088.yuv | Dancer_c_9_1920x1088.yuv | 250
3 | GT_Fly_c_1_1920x1088.yuv | GT_Fly_c_9_1920x1088.yuv | 250
4 | kendo_1024x768_1.yuv | Kendo_1024x768_5.yuv | 300
5 | Newspaper_R_1024x768_2.yuv | Newspaper_R_1024x768_6.yuv | 300
6 | Poznan_Hall2_1920x1088_depth_cam05.yuv | Poznan_Hall2_1920x1088_depth_cam07.yuv | 200
7 | Poznan_Street_1920x1088_depth_cam03.yuv | Poznan_Street_1920x1088_depth_cam05.yuv | 250

## Slide 5: Experimental results
Tools enabled
  Default SHM-1.0 tools (inter-layer texture prediction and motion predictions) are enabled
  Inter-view prediction based on HTM-6.0
  For RefIdx approach, inter-layer reference is added before inter-view reference in reference picture list
BD-rate calculation
  Performance is evaluated in terms of ‘BL_D + EL_D’ BD-rate
  Bitrate and PSNR of BL_D (dependency base layer)
    BitrateBL_D = BitrateD0V0 + BitrateD0V1
    PSNRBL_D = (PSNRD0V0 + PSNRD0V1) / 2
  Bitrate and PSNR of EL_D (dependency enhancement layer)
    BitrateEL_D = BitrateD1V0 + BitrateD1V1
    PSNREL_D = (PSNRD1V0 + PSNRD1V1) / 2
<number>

## Slide 6: Simulcast vs. TextureRL SHVC + MV-HEVC
Inter-view and Inter-layer predictions improve average BD-rate by 40.5% ~ 18.1%
<number>
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
Simulcast
SHVC + MV-HEVC
BL_D
EL_D
BL_D
EL_D

## Slide 7: MV-HEVC Simulcast vs. TextureRL SHVC + MV-HEVC
Inter-layer prediction improves average BD-rate by 24.7% ~ 10.7% on top of inter-view prediction
<number>
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
SHVC + MV-HEVC
V0
V1
D0
D1
D0V0
D1V0
D1V1
D0V1
MV-HEVC simulcast
BL_D
EL_D
BL_D
EL_D

## Slide 8: TextureRL vs. RefIdx for SHVC + MV-HEVC
When compared to RefIdx approach, TextureRL approach improves BD-rate gain by 0.4% ~ 2.0% for multi-view SNR scalable coding
<number>

## Slide 9: Conclusions
Inter-view prediction is implemented on top of SHM-1.0
Performances of inter-layer prediction are evaluated for multi-view SNR scalable coding
  Inter-layer and inter-view predictions improve average BD-rate by 40.5% ~ 18.1%
  Inter-layer prediction improves average BD-rate by 24.7% ~ 10.7% on top of inter-view prediction
  TextureRL outperforms RefIdx by 0.4% ~ 2.0% in multi-view SNR scalable coding
It is recommended to evaluate TextureRL and RefIdx approaches in SHVC + MV-HEVC context
<number>