## Slide 1: Modified motion vector signalling and prediction under reference index based SHVC
Kiran Misra, Jie Zhao, Andrew Segall
(JCTVC-M0258)

## Slide 2: Organization
Introduction
Proposed changes
Results
Conclusion

## Slide 3: Introduction
In JCTVC-L0251:
  Skip motion vector predictor flag and motion vector difference when referencing base layer picture
In JCTVC-K0031
  If the temporally collocated prediction unit refers their collocated base layer picture then an alternative scaled motion vector predictor is obtained from the current base layer picture

## Slide 4: Proposed change: Infer zero MV
In reference index based SHVC (SHM-1.0):
Infer zero motion vector when referencing co-located BL picture

## Slide 5: Proposed change: Alternate motion candidate
In reference index based SHVC (SHM-1.0):
Use scaled BL motion of current picture if temporal collocated MVP references its BL

## Slide 6: Experimental Results
Anchor: SHM-1.0 reference index framework
Luma BD rate
 | EL+BL |  | 
 | 2x | 1.5x | SNR
All-intra | -0.1% | -0.1% | 
Random access | -0.8% | -0.6% | -0.6%
Low delay P | -0.4% | -0.1% | 0.0%
Low delay B | -0.4% | -0.1% | 0.0%
Cross-check: JCTVC-M0365 (Thanks to Interdigital)

## Slide 7: Alternate motion candidate (as a buffer update)
In reference index based SHVC (SHM-1.0):
Replace mapped BL motion information with motion information from EL, if EL motion does not reference its BL.
Does not require block-level changes
Performance versus SHM-1.0 anchor (reference index framework):
RA: -0.4% (2x) / -0.2% (1.5x) / x.xx% (SNR)

## Slide 8: Conclusion
Zero motion vector is inferred when referencing co-located base layer picture.
Use scaled BL motion of current picture if temporal collocated MVP references its BL
The proposed changes achieves the following average luma BD rate improvements with SHM-1.0 reference index framework as anchors:
-0.1%/-0.1% (AI 2x/AI 1.5x)
-0.8%/-0.6%/-0.6% (RA 2x/RA 1.5x/RA SNR)
-0.4%/-0.1%/-0.1% (LDP 2x/LDP 1.5x/LDP SNR)
-0.4%/-0.1%/-0.1% (LDB 2x/LDB 1.5x/LDB SNR)
Proposed a mapped BL motion buffer update mechanism:
-0.4%/-0.2%/x.xx% (RA 2x/RA 1.5x/RA SNR)
Recommend: Adopt to SHVC test model

## Slide 10: Supplemental data (JCTVC-L0251)
  BD rate improvement for zero motion vector infer only as reported in JCTVC-L0251
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.2% | -0.2% |  |  | 
Class B | -0.1% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1%
Overall (EL+BL) | -0.1% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1%
Overall (EL) | -0.2% | -0.3% | -0.3% | -0.3% | -0.3% | -0.2%
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.3% | -0.8% | -0.7% |  |  |  | -0.1% | -0.8% | -0.8%
Class B | -0.2% | -0.6% | -0.6% | -0.1% | -0.1% | -0.1% | -0.2% | -0.4% | -0.5%
Overall (EL+BL) | -0.2% | -0.6% | -0.6% | -0.1% | -0.1% | -0.1% | -0.2% | -0.5% | -0.6%
Overall (EL) | -0.3% | -0.9% | -0.9% | -0.2% | -0.1% | -0.1% | -0.3% | -0.8% | -0.8%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.4% | -0.3% |  |  |  | -0.3% | -0.3% | -0.3%
Class B | -0.3% | -0.1% | 0.0% | -0.3% | -0.1% | 0.1% | -0.3% | 0.1% | 0.3%
Overall (EL+BL) | -0.4% | -0.2% | -0.1% | -0.3% | -0.1% | 0.1% | -0.3% | 0.0% | 0.1%
Overall (EL) | -0.5% | -0.3% | -0.1% | -0.4% | -0.1% | 0.1% | -0.5% | -0.1% | 0.1%