## Slide 1: JCTVC-M0275: Non-SCE3: Simplified Generalized Residual Prediction
X. Li, J. Chen, K. Rapaka, M. Karczewicz

## Slide 2: Overview
SCE 3.3 is simplified by two ways
  Replacing the 4-tap GRP up-sampling/smoothing filter with 3-tap filter
  Further constraint on block size that GRP cannot be applied to 4x16/16x4 blocks
Simulation results and discussions
  Crosschecked by MediaTek (JCTVC-M0226) and Intel (JCTVC-M0321)
Conclusions

## Slide 3: GRP simplifications based on SCE 3.3 test case 2
 | GRP weighting modes | Bi-linear interpolation | GRP up-sampling/ smoothing | Common GRP block size constraint | No GRP for chroma | No GRP filtering in SNR | Additional ME
SCE 3.3 Test case 2 | 0, res-0.5, 1, diff-0.5 | Y | 4-tap | Uni: 8x8 Bi: 16x16 | N | N | N
Simp #1 | unchanged | unchanged | 3-tap | unchanged | unchanged | unchanged | unchanged
Simp #2 | unchanged | unchanged | unchanged | Uni: 8x8 No 16x4/4x16 Bi: 16x16 | unchanged | unchanged | unchanged

## Slide 4: Complexity in Worst Case
Test case | Mul | Adds | MemBand (4x2) | MemBand (8x2) | Ref num in pred | Additional picture buffer | Size of lookup table
SCE 3.3 Test case 2 | 76% | 67% | 108% | 106% | 180% | 0% | 146% (280 Bytes)
Simp #1 | 61% | 49% | 98% | 96% | 180% | 0% | 138% (264 Bytes)
Simp #2 | 76% | 67% | 98% | 91% | 180% | 0% | 146% (280 Bytes)

## Slide 5: RD results
Case | Conf | Y | U | V | EncT | DecT
SCE 3.3 test case 2 | RA | -2.0% | -3.7% | -3.9% | 119% | 126%
 | LD-P | -5.3% | -5.7% | -5.1% | 125% | 128%
 | LD-B | -3.1% | -4.6% | -4.5% | 116% | 127%
 | Aver 2 | -3.7% | -4.7% | -4.5% | 122% | 127%
 | Aver 3 | -3.5% | -4.7% | -4.5% | 120% | 127%
3-tap filter | RA | -2.0% | -3.6% | -3.8% | 114% | 122%
 | LD-P | -5.3% | -5.5% | -4.9% | 120% | 123%
 | LD-B | -3.0% | -4.5% | -4.4% | 111% | 121%
 | Aver 2 | -3.7% | -4.6% | -4.4% | 117% | 123%
 | Aver 3 | -3.4% | -4.5% | -4.4% | 115% | 122%
No 4x16 or16x4 uni-pred | RA | -2.0% | -3.7% | -3.9% | 113% | 121%
 | LD-P | -5.3% | -5.6% | -5.0% | 115% | 120%
 | LD-B | -3.1% | -4.6% | -4.5% | 107% | 119%
 | Aver 2 | -3.7% | -4.7% | -4.5% | 114% | 121%
 | Aver 3 | -3.5% | -4.6% | -4.5% | 112% | 120%

## Slide 6: Average Complexity
Case | Conf | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
Test case 2 | RA | 120% | 120% | 120% | 114% | 111%
 | LD-P | 140% | 143% | 143% | 130% | 125%
 | LD-B | 130% | 130% | 130% | 121% | 117%
 | Aver | 130% | 131% | 131% | 122% | 118%
3-tap filter | RA | 118% | 115% | 116% | 108% | 105%
 | LD-P | 135% | 130% | 131% | 117% | 110%
 | LD-B | 126% | 122% | 123% | 112% | 107%
 | Aver | 126% | 122% | 123% | 112% | 107%
No 4x16 or16x4 uni-pred | RA | 120% | 120% | 120% | 114% | 111%
 | LD-P | 140% | 143% | 143% | 130% | 125%
 | LD-B | 130% | 130% | 130% | 121% | 117%
 | Aver | 130% | 131% | 131% | 121% | 118%

## Slide 7: Conclusions
SCE3.3 test case 2 is further simplified by two different ways
  Replacing the 4-tap GRP filter to 3-tap
  Restricting the GRP cannot be applied to 4x16/16x4 blocks
The worst-case complexity of the two simplifications are both lower than that of HEVC single layer coding
Thanks MediaTek and Intel for the crosschecking