## Slide 1: A use case and high level syntax of SHVC: Scalability based region of interest
Cheung Auyeung, Jun Xu, Ali Tabatabai, Ohji Nakagami
Sony Electronics Inc. and Sony Corporation

## Slide 2: Use Cases
ROI
ROI
Would like to get more
detail in ROI in BL.
By providing more detail of ROI in EL.
Would like to get higher quality in ROI in BL.
By providing higher PSNR in ROI in EL.
(a) Spatial Scalability
(b) SNR Scalability
ROI
ROI

## Slide 3: Region of Interest Scalability
To align with SHM-1.0, this contribution proposes to define the followings:
  A ROI is a rectangular collection of coding tree units (CTU).
  An enhancement layer picture has one or more non-overlapping ROIs.
ROI
ROI
ROI
ROI
A picture with two well-separated ROIs.
A picture with two connected ROIs.

## Slide 4: Non-Signficant Slice Segment
Two ways that can be used to support ROI scalability:
  Non-significant slice segment and the associated NAL type.
    All the CTUs within the slice segment are constructed either by copying
      the corresponding base layer in case of SNR scalability,
      the up-sampled version of base layer in case of spatial scalability.
  Non-significant tile.
    All the CTUs within the tile are constructed either by copying
      the corresponding base layer in case of SNR scalability,
      the up-sampled version of base layer in case of spatial scalability.

## Slide 5: Non-Significant Slice Segment
A non-significant slice segment layer has (slice_segment_size_minus1+1) number of CTU.
  Signaled in a NAL unit with a new nal_unit_type (e.g. JCTVC-L0055) indicating that it carries a non-significant slice segment RBSP.
  CTUs in ROI are signaled by regular slice segments.
  CTUs outside ROIs are signaled by non-significant slice segments.
non_significant_slice_segment_layer_rbsp( ) { | Descriptor
slice_segment_header( ) | 
slice_segment_size_minus1 | ue(v)
rbsp_slice_segment_trailing_bits( ) | 
} | 

## Slide 6: Non-Significant Tile
Combine tile and non-significant slice segment together to signal the ROIs as in this example:
May combine with JCTVC-L0049 to use SEI messages to indicate that motion compensation is restricted to within a significant tile.
A picture is divided into 16 tiles.
Only tile 5 and tile 10 are significant.
Non-significant tiles are signaled by non-significant slice segment layer RBSP
The significant tiles are signaled by regular slice segment layer RBSP.
Tile0
Tile1
Tile3
Tile4
ROI Tile5
Tile7
Tile12
Tile13
Tile15
Tile2
ROI Tile10
Tile6
Tile14
Tile11
Tile8
Tile9
Seg0 (5 tiles)
Seg1
Seg 5 (5 tiles)
Seg4
(1 tile)
Seg3
(4 tiles)
Seg2

## Slide 7: Conclusion
Presented the idea of ROI scalability and proposed a HLS approach to support it.
Propose for further discussions and studies on different ways to support ROI scalability.