## Slide 1: JCTVC-M0297 Non-SCE3: Bandwidth reduction for combined inter mode
Vadim Seregin and Marta Karczewicz

## Slide 2: Combined inter prediction tested in SCE3.2
CU based inter mode
One context is added for combined inter mode flag
Applied only to luma component
  – inter prediction
  – Intra-BL prediction
Chroma is predicted with normal inter prediction
33% bandwidth increase in the worst case comparing with HEVC
Memory configuration | SHM1.0 | Combined Mode | Ratio
4x2 | 15.0 | 20.0 | 133%
8x2 | 18.0 | 24.0 | 133%

## Slide 3: Bandwidth reduction
No combined mode for non-2Nx2N 8x8 CU
Restrict bi-prediction with combined mode similar to 8x4 and 4x8 PUs in HEVC:
  For merge mode, bi-directional MV candidate is converted to uni-directional motion vector from RefPicList0
  For AMVP mode, only uni-directional MV can be chosen at encoder side and inter direction signaling is restricted to the uni-direction only
 | 8x8 |  | 16x16 |  |  | > 16x16
 | 2NxN, Nx2N | 2Nx2N | NxN | 2NxN, Nx2N | 2Nx2N | 
SCE3.2 | uni | bi | bi | bi | bi | bi
Method 3 | X | uni | uni | bi | bi | bi
Method 1 | X | uni | uni | uni | bi | bi
Method 2 | X | uni | uni | uni | uni | uni

## Slide 4: Experimental results
Luma component
Chroma component on average
Test | RA 2x | RA 1.5x | RA SNR | LB 2x | LB 1.5x | LB SNR | LP 2x | LP 1.5x | LP SNR | Enc | Dec
SCE3.2 | -0.28 | -0.44 | -0.72 | -0.45 | -0.31 | -0.79 | -1.30 | -1.38 | -2.55 | 113% | 100%
Method3 | -0.28 | -0.42 | -0.67 | -0.42 | -0.29 | -0.71 | -1.30 | -1.38 | -2.55 | 108% | 97%
Method1 | -0.25 | -0.40 | -0.63 | -0.40 | -0.27 | -0.68 | -1.30 | -1.38 | -2.55 | 109% | 98%
Method2 | -0.21 | -0.31 | -0.38 | -0.34 | -0.21 | -0.44 | -1.30 | -1.38 | -2.55 | 106% | 99%
Test | RA 2x | RA 1.5x | RA SNR | LB 2x | LB 1.5x | LB SNR | LP 2x | LP 1.5x | LP SNR | Enc | Dec
SCE3.2 | -2.63 | -3.18 | -4.51 | -2.59 | -3.39 | -4.65 | -4.10 | -5.87 | -8.23 | 113% | 100%
Method3 | -2.58 | -3.14 | -4.49 | -2.63 | -3.48 | -4.78 | -4.04 | -5.87 | -8.14 | 108% | 97%
Method1 | -2.39 | -2.97 | -4.23 | -2.50 | -3.33 | -4.53 | -4.04 | -5.87 | -8.14 | 109% | 98%
Method2 | -1.60 | -1.83 | -2.36 | -1.89 | -2.41 | -2.95 | -4.04 | -5.87 | -8.14 | 106% | 99%

## Slide 5: Results on average
Average for RA, LB, and LP
Test | BD-Y | BD-UV | Worst Mult | Average |  |  |  |  | Enc | Dec
 |  |  |  | 8b/8b | 64b/256b | 64b/512b | Mults | Adds |  | 
SCE3.2 | -0.91 | -4.35 | 145% | 106% | 105% | 105% | 106% | 107% | 113% | 100%
Method3 | -0.89 | -4.35 | 123% | 105% | 104% | 104% | 105% | 107% | 108% | 97%
Method1 | -0.87 | -4.22 | 112% | 105% | 104% | 104% | 105% | 106% | 109% | 98%
Method2 | -0.79 | -3.45 | 100% | 103% | 102% | 102% | 104% | 105% | 106% | 99%

## Slide 6: Conclusion
Three methods are suggested to reduce bandwidth for combined mode
Method 3 has almost same performance comparing to combined mode test from SCE3, while method 2 does not use bi-prediction for combined mode input
Thanks to Samsung (JCTVC-M0347) and Mediatek (JCTVC-M0396) for cross-verification