## Slide 1: JCTVC-M0298 Bandwidth reduction for range extension
Vadim Seregin, Xianglin Wang, Joel Sole, Marta Karczewicz

## Slide 2: Problem statement
In HEVC, to reduce bandwidth, bi-prediction is restricted for 4x8 and 8x4 PUs
Bandwidth goes up for YUV 4:4:4
Bandwidth assessment from JCTVC-L0440 applied to 4:2:0 and 4:4:4:
For consumer applications using 4:4:4, it is desired to keep bandwidth requirement similar to YUV 4:2:0
Memory configuration | 4:2:0 | 4:4:4 | Ratio
4×2 | 15.0 | 20.5 | 137%
8×2 | 18.0 | 24.0 | 133%

## Slide 3: Solutions
Method 1
  Restrict bi-prediction for 8x8 CU
  For merge mode, bi-directional MV candidate is converted to uni-directional motion vector from RefPicList0
  For AMVP mode, only uni-directional MV can be chosen at encoder side and inter direction signaling is restricted to uni-direction only
Method 2
  For 8x8 CU, restrict bi-prediction for chroma component only
  Bi-directional MV candidate is converted to uni-directional MV from RefPicList0 during chroma motion compensation, while luma component is still bi-predicted
Memory configuration | 4:4:4 | Method 1/2 | Ratio
4×2 | 20.5 | 16.3 | 79%
8×2 | 24.0 | 21.0 | 88%

## Slide 4: Experimental results
BD-rate using RExt common conditions (JCTVC-L1006)
Thanks to Samsung for cross-verification (JCTVC-M0345)
Test | Chroma Format | RA HE Main | RA HE High | LB HE Main | LB HE High
Method1 | RGB 4:4:4 | 1.4 | 1.6 | 1.4 | 1.4
 | YUV 4:2:2 | 0.6 | 0.8 | 0.7 | 0.9
 | YUV 4:4:4 | 0.8 | 1.1 | 0.6 | 0.9
Method2 | RGB 4:4:4 | 1.2 | 1.3 | 1.3 | 1.3
 | YUV 4:2:2 | 0.2 | 0.4 | 0.2 | 0.4
 | YUV 4:4:4 | 0.2 | 0.4 | 0.2 | 0.3

## Slide 5: Conclusion
Two methods are suggested to reduce bandwidth for YUV 4:4:4
Second method provides smaller performance penalty