## Slide 1: <JCTVC-M0304> Non-RCE1/Non-RCE2: Simplified level coding for Transform skip and lossless coding
Seung-Hwan Kim Andrew Segall
<number>
Notes: <number>

## Slide 2: Motivation
More generalized contents/condition considered in range extension.
  Input formats: YUV 4:4:4, YUV 4:2:2, RGB 4:4:4, …
  Contents: natural images, screen contents, medical images
  More conditions: high bitrates, lossless, near-lossless
The importance of transform skipped mode
  Impact of transform skip on screen content sequences [JCTVC-L0428]
    BD-Rate change for disabling transform skip 25.9 % (AI), 23.5% (RA), 20.2% (LD)
  Lossless coding
  The different statistics of residual data
Current Residual Coding
  Designed for transformed coefficients
  Keep the coding performance for natural sequences and deal with test sequences from range extension
  A lot of room for improvement in the aspect of complexity reduction and coding performance
<number>
Notes: <number>

## Slide 3: Motivation
Current Residual Coding
  Designed for transformed coefficients
  Keep the coding performance for natural sequences and deal with test sequences from range extension
  A lot of room for improvement in the aspect of complexity reduction and coding performance
<number>
Notes: <number>

## Slide 4: Contribution
Contribution
  Transform skipped block or transform_quant_bypass (lossless)
  - Remove GR_than_1 and GR_than_2
  Modified remaining level coding for lossless coding
  - signal the corresponding rice-parameter
  - Remove rice-parameter update process
<number>
Notes: <number>

## Slide 5
<number>
Significance Map
Decoding loop
Remaining Level
decoding
HM10.0
Greater_than_1 flag
Decoding loop
Greater_than_2 flag
Decoding
Sign data
decoding
Rice_parameter = 0
Update rice-parameter
Remove GR_than_1
Remove GR_than_2
Method I
Significance Map
Decoding loop
Remaining Level
decoding
Method 1
Greater_than_1 flag
Decoding loop
Greater_than_2 flag
Decoding
Sign data
decoding
Rice_parameter = 0
Update rice-parameter

## Slide 6
<number>
Significance Map
Decoding loop
Remaining Level
decoding
HM10.0
Method II
Greater_than_1 flag
Decoding loop
Greater_than_2 flag
Decoding
Sign data
decoding
Significance Map
Decoding loop
Remaining Level
Decoding loop
Sign data
coding
Rice_parameter = 0
Decode rice parameter
Update rice-parameter
Remove GR_than_1
Remove GR_than_2
Code rice parameter (Truncated Unary)
- 1 context bin
- 4 bypass bins
4. Remove Rice-parameter update process
Method II

## Slide 7: Result for RCE1 (Method I)
<number>
 | All Intra Main-tier |  |  | All Intra High-tier |  |  | All Intra Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
 | RA Main-tier |  |  | RA High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.1% | 0.1% | 0.1% | 0.0% | 0.1%
YCbCr 4:4:4 | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.1% | 0.0% | -0.1% | 0.1% | 0.2% | 0.1%
Overall | 0.0% | 0.0% | -0.1% | 0.1% | 0.1% | 0.1%
 | Low delay B Main-tier |  |  | Low delay B High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.1% | 0.1% | 0.1% | 0.2% | 0.1% | 0.3%
YCbCr 4:4:4 | -0.2% | 0.0% | -0.1% | -0.1% | 0.1% | 0.1%
YCbCr 4:2:2 | 0.1% | 0.0% | -0.1% | 0.1% | 0.2% | 0.4%
Overall | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.2%

## Slide 8: Result for RCE2 (Method I)
<number>
 | All Intra Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 4.6 | 4.6 | 1.3%
Class B | 2.1 | 2.1 | 0.6%
SC(GBR) | 7.5 | 7.5 | 0.4%
RangeExt | 2.2 | 2.2 | 1.4%
Overall | 5.3 | 5.3 | 0.8%
 | Random Access Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 29.3 | 28.2 | 3.7%
Class B | 2.6 | 2.5 | 1.1%
SC(GBR) | 88.8 | 88.5 | 1.0%
RangeExt | 2.5 | 2.5 | 2.3%
Overall | 51.0 | 50.6 | 1.8%
 | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 47.4 | 44.2 | 4.7%
Class B | 2.6 | 2.5 | 1.1%
SC(GBR) | 301.9 | 302.1 | 0.7%
RangeExt | 2.5 | 2.5 | 2.2%
Overall | 161.2 | 160.7 | 1.8%
Method I for Lossless
  Remove GR_than_1
  Remove GR_than_1
  Worst case context bin reduced by 38%
  (1.56 bins/pixel  1bin/pixel)
  Coding loss

## Slide 9: Result for RCE2 (Method II)
<number>
 | All Intra Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 4.6 | 4.7 | -1.0%
Class B | 2.1 | 2.2 | -1.0%
SC(GBR) | 7.5 | 8.1 | -6.2%
RangeExt | 2.2 | 2.2 | -0.4%
Overall | 5.3 | 5.6 | -3.5%
 | Random Access Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 29.3 | 28.6 | 2.5%
Class B | 2.6 | 2.6 | -0.2%
SC(GBR) | 88.8 | 95.8 | -4.8%
RangeExt | 2.5 | 2.5 | 1.1%
Overall | 51.0 | 54.4 | -1.7%
 | Low delay B Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 47.4 | 44.6 | 3.9%
Class B | 2.6 | 2.6 | -0.2%
SC(GBR) | 301.9 | 328.8 | -4.4%
RangeExt | 2.5 | 2.5 | 1.0%
Overall | 161.2 | 174.0 | -1.3%
Method II for Lossless
  Method I + RP
  Reduce the maximal number of context bin reduced by 32%
  (1.56 bins/pixel  1.06bin/pixel)
  Improved coding performance

## Slide 10: Conclusion
Conclusion
  Need to update residual coding part for the transform skipped block
  Update remaining level coding for lossless coding
<number>

## Slide 11: Impact of transform skip on screen contents (JCTVC-L0428)
<number>
BD-Rate changes for disabling transform skip are shown in the tables below:
 | AI-HEMT |  | 
 | Y | U | V
sc_cad_waveform | 34.8% | 37.0% | 39.7%
sc_pcb_layout | 46.1% | 44.4% | 45.7%
sc_ppt_doc_xls | 33.3% | 43.6% | 35.4%
sc_video_conf. | 29.9% | 30.9% | 33.0%
sc_web_browsing | 12.2% | 23.7% | 19.1%
sc_cg_twist_tunnel | 39.0% | 35.8% | 37.0%
sc_wordEditing | 14.2% | 12.4% | 13.3%
sc_map | 5.5% | 7.3% | 11.2%
sc_programming | 18.2% | 13.8% | 14.0%
Overall | 25.9% | 27.6% | 27.6%
Notes: <number>