## Slide 1
JCTVC-M0312
Non-SCE1 : Inter-layer intra mode prediction
Junghye Min, Elena Alshina

## Slide 2: Summary
Propose an inter-layer intra mode prediction method
  If intra mode from the co-located base layer (CorDir) is angular mode (>1)
    MPMlist = {CorDir,CorDir+1,CorDir-1}
  Otherwise, intra modes from left and above neighbor (LeftDir and AboveDir) are checked and MPM setting is performed using LeftDir,AboveDir and CorDir.
  performance
    Method 1 : (-0.4%,-0,2%,-0.2%) in AI 2x, (-0.1%, 0.0%, 0.0%) in AI 1.5x
    Method 2: (-0.4%,-0.2%, -0.2%) in AI 2x, (-0.1%, 0.0%, 0.0%) in AI 1.5x

## Slide 3: Approach
Method 1
  If CorDir is angular (>1), MPM0=CorDir, MPM1=CorDir+1, MPM2=CorDir-1. (mpm setting is completed)
  Otherwise, if CorDir!=LeftDir and CorDir!=AboveDir and LeftDir!=AboveDir,
  MPM0=CorDir, MPM1=LeftDir, MPM2=AboveDir. (mpm setting is completed)
  Otherwise, same MPM setting process using LeftDir and AboveDir in SHM1.0 is used.
Method 2
  If CorDir is angular (>1), MPM0=CorDir, MPM1=CorDir+1, MPM2=CorDir-1. (mpm setting is completed)
  Otherwise, if LeftDir==AboveDir, AboveDir=CorDir.
  same MPM setting process using LeftDir and AboveDir in SHM1.0 is used.
  Both methods use left top position of the PU to get CorDir.

## Slide 4: Test results
Test result of method 1
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.2% | -0.1% |  |  | 
Class B | -0.4% | -0.3% | -0.3% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.0% | 13.4% | 13.1% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.5% | -0.4% | -0.4% | -0.1% | 0.1% | 0.0%
Enc Time[%] | 106.3% |  |  | 106.3% |  | 
Dec Time[%] | 100.7% |  |  | 100.2% |  | 
Enc Mem[%] | 100.8% |  |  | 99.8% |  | 
BL Match | Matched |  |  | Matched |  | 
Test result of method 1 with MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | 0.0% | 0.0% |  |  | 
Class B | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.2% | -0.1% | 0.0% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.1% | 13.6% | 13.3% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Enc Time[%] | 104.0% |  |  | 104.1% |  | 
Dec Time[%] | 100.4% |  |  | 99.9% |  | 
Enc Mem[%] | 100.7% |  |  | 100.6% |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 5: Test results
Test result of method 2
Test result of method 2 with MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.1% | 0.0% |  |  | 
Class B | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.1% | 13.6% | 13.3% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Enc Time[%] | 104.2% |  |  | 104.2% |  | 
Dec Time[%] | 100.7% |  |  | 100.3% |  | 
Enc Mem[%] | 100.5% |  |  | 100.5% |  | 
BL Match | Matched |  |  | Matched |  | 
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.2% | -0.1% |  |  | 
Class B | -0.4% | -0.3% | -0.3% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.0% | 13.4% | 13.1% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.5% | -0.4% | -0.4% | -0.1% | 0.1% | 0.0%
Enc Time[%] | 104.0% |  |  | 104.0% |  | 
Dec Time[%] | 101.0% |  |  | 100.7% |  | 
Enc Mem[%] | 99.8% |  |  | 99.8% |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 6: Conclusions
Proposed methods exploit intra pred modes from base layer (CorDir) in a different way depending on whether CorDir is angular or not.
  When CorDir is angular, there is no need to derive LeftDir and AboveDir.
Proposed methods are consistent with previous SHEVC specification with minimal changes.
Proposed methods provide -0.4%,-0.2%,-0.2% performance gains for AI 2x.
We recommend to consider this proposed method for SCE1.
We would like to thank TI for the crosscheck of this proposal.

## Slide 7
additional test results
(not crosschecked yet)

## Slide 8: Test results (fast encoding for method 2)
Test result of method 2
Test result of method 2 with MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.2% | -0.1% |  |  | 
Class B | -0.4% | -0.3% | -0.3% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.0% | 13.4% | 13.1% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.5% | -0.4% | -0.4% | -0.1% | 0.1% | 0.0%
Enc Time[%] | 101.0% |  |  | 101.4% |  | 
Dec Time[%] | 100.5% |  |  | 99.9% |  | 
Enc Mem[%] | 100.9% |  |  | 100.9% |  | 
BL Match | Matched |  |  | Matched |  | 
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.1% | 0.0% |  |  | 
Class B | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall (Test vs Ref) | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0%
Overall (Test vs single layer) | 12.1% | 13.6% | 13.3% | 10.2% | 10.3% | 9.7%
EL only (Test vs Ref) | -0.4% | -0.2% | -0.2% | -0.1% | 0.0% | 0.0%
Enc Time[%] | 101.0% |  |  | 101.5% |  | 
Dec Time[%] | 98.9% |  |  | 98.3% |  | 
Enc Mem[%] | 101.0% |  |  | 100.8% |  | 
BL Match | Matched |  |  | Matched |  |