## Slide 1: JCTVC-M0334: Parallel Processing Indications for Tiles in HEVC Extensions
K. Rapaka, W. Pu, X. Li, J. Chen, Y.-K. Wang, M. Karczewicz (Qualcomm)

## Slide 2: Motivation
Ease parallel and synchronized processing with tiles across layers
Current challenges :
  Inter-layer prediction dependencies
  Non-aligned tiles across the layers.
  Resampling process across tile boundaries in reference layer pictures.

## Slide 3: Proposal
Two methods are proposed to ease parallel processing with tiles across layers.
  Indication of encoder constraint on inter-layer Prediction beside tile alignment
  Tile based upsampling filter beside tile alignment

## Slide 4: Solution 1 : Encoder constraint on inter-layer prediction
A VUI flag indicating an encoder constraint that the tiles in enhancement layer and base layer are aligned and no CU/PU in an enhancement tile is inter-layer texture predicted or inter-layer syntax predicted from a collocated CU/PU that belongs or partially belongs to a non-aligned tile.
Vui_parameters( ) { | Descriptor
… | 
bitstream_restriction_flag | u(1)
if( bitstream_restriction_flag ) { | 
tiles_fixed_structure_flag | u(1)
inter_layerpred_not_along_tile_boundary_flag | u(1)
… | 
} | 
} | 

## Slide 5: Indication of Encoder constraint on inter-layer prediction
inter_layerpred_not_along_tile_boundary_flag equal to 1 indicates that tile boundaries of different layers are aligned and inter-layer texture prediction and inter-layer syntax prediction are not allowed along/across the tile boundaries such that any enhancement layer tile can decoded without decoding any non-aligned base layer tile. The alignment of tile boundaries means that any two enhancement layer picture samples that lie within the same enhancement layer tile, the collocated base layer samples shall also lie within the same base layer tile.
inter_layerpred_not_along_tile_boundary_flag equal to 0 indicates that there is no restriction on the tile configurations among layers. When inter_layerpred_not_along_tile_boundary_flag is not present in bitstream, it shall be inferred to be equal to 0.

## Slide 6: Solution 2 : Tile Based Upsampling
Base layer pixels are re-sampled and used as interlayer reference.
The base layer picture is coded with tiles, tile boundaries are treated as picture boundaries so that no up-sampling will be across tile boundaries.
tile_based_resampling_filter_enable_flag equal to 0 specifies that picture based up-sampling is enabled. tile_based_resampling_filter_enable_flag equal to 1 specifies that tile based up-sampling is enabled and tile boundaries of different layers are aligned. When tile_based_resampling_filter_enable_flag not present it is inferred to be equal to 0.
if( sps_extension_flag ) { | 
... | 
tile_based_resampling_filter_enable_flag | u(1)
... | 
} |