## Slide 1
Quantitative measurement for subjectively lossless
screen content coding
JCTVC-M0348
18 April – 26 April 2013
Tao Lin

## Slide 2
In screen content coding, mathematical losslessness is an overkill requirement
  By allowing subjective losslessness, compression ratio can have 2x or more improvement
In real practice, subjective or perceptual losslessness can not always be assessed by visual inspection
  A quantitative measurement is indispensable
  Must absolutely guarantee subjective losslessness in real applications
Content-dependent Rate-Distortion measurement is required
Motivation

## Slide 3
Well-known human visual masking effect
  The reduction of the visibility of one stimulus, called the target, by a spatiotemporally contiguous second stimulus, called the mask
The number of distinct colors (stimulus to the eye) and color contrast in a small area is directly related to the visibility (visual sensitivity and response of human eye) of the area
  The more distinct colors a 4x4 block has, the less sensitivity to the color deviation of the block human eye has, thus the lower PSNR the block can allow to maintain subjective (perceptual) losslessness
Theoretic Basis

## Slide 4
Color-count-dependent-PSNR measurement
  The following color-count-dependent-PSNR measurement condition is satisfied for all 4x4 blocks of the picture
Proposed Measurement
Distinct color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 16
PSNR value (dB) | > 65 | > 60 | > 55 | > 50 | > 45 | > 40
Maximum error allowed (Square Root of MSE) | 0.1434 | 0.255 | 0.4535 | 0.8064 | 1.434 | 2.55
This is still a very tight condition
  May use more relaxed PSNR values

## Slide 5
Draw two types of maps to see the correlation between the color count in a 4x4 block and PSNR of the block
  For an original picture, a 4x4 block color count map is drawn and each 4x4 block is filled with a solid color based on the color count of the block
  For a reconstructed picture, a 4x4 block psnr map is drawn and each 4x4 block is filled with a solid color based on the psnr of the block
Experiments
color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 12 | 13 ~ 14 | 15 ~ 16
psnr | 65 ~ ∞ | 60 ~65 | 55 ~ 60 | 50 ~ 55 | 45 ~ 50 | 40 ~ 45 | 35 ~ 40 | 0 ~ 35
map color | white | yellow | red | purple | cyan | green | blue | black

## Slide 6
Experimental Data
color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 12 | 13 ~ 14 | 15 ~ 16
psnr | 65 ~ ∞ | 60 ~65 | 55 ~ 60 | 50 ~ 55 | 45 ~ 50 | 40 ~ 45 | 35 ~ 40 | 0 ~ 35
map color | white | yellow | red | purple | cyan | green | blue | black
Color-count map
PSNR map (QP=6)
sc_map_1280x720_60_8bit

## Slide 7
Experimental Data
Color-count map
PSNR map (QP=6)
color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 12 | 13 ~ 14 | 15 ~ 16
psnr | 65 ~ ∞ | 60 ~65 | 55 ~ 60 | 50 ~ 55 | 45 ~ 50 | 40 ~ 45 | 35 ~ 40 | 0 ~ 35
map color | white | yellow | red | purple | cyan | green | blue | black
sc_programming_1280x720_60_8bit

## Slide 8
Experimental Data
Color-count map
PSNR map (QP=6)
color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 12 | 13 ~ 14 | 15 ~ 16
psnr | 65 ~ ∞ | 60 ~65 | 55 ~ 60 | 50 ~ 55 | 45 ~ 50 | 40 ~ 45 | 35 ~ 40 | 0 ~ 35
map color | white | yellow | red | purple | cyan | green | blue | black
sc_wordEditing_1280x720_60_8bit

## Slide 9
Experimental Data
Color-count map
PSNR map (QP=8)
color count | 1 ~ 2 | 3 ~ 4 | 5 ~ 6 | 7 ~ 8 | 9 ~ 10 | 11 ~ 12 | 13 ~ 14 | 15 ~ 16
psnr | 65 ~ ∞ | 60 ~65 | 55 ~ 60 | 50 ~ 55 | 45 ~ 50 | 40 ~ 45 | 35 ~ 40 | 0 ~ 35
map color | white | yellow | red | purple | cyan | green | blue | black
VenueVu_1920x1080_30_8bit

## Slide 10
Conclusions
Color-count-dependent (CCD)-PSNR measurement makes more sense than single PSNR measurement
Not for assessing subjective losslessness only
Can also help developing new subjectively lossless coding tools
Can also be used as a base for content-adaptive R-D requirement and measurement
Currently, simple color-count is used
Some sort of color quantization/clustering may be needed before counting the color
Test condition: QP=0, 5, 10, 15 + CCD-PSNR

## Slide 11
THANK YOU