## Slide 1: AhG8: Simplified update of the coefficient level Rice parameter JCTVC-M0366
Joel Sole, Marta Karczewicz

## Slide 2: Background
A target application for HEVC Range Extensions 4:4:4 is wireless display
  Consumer application
  Requires visually lossless coding without the increase in encoder/decoder complexity of professional applications
  Code screen content, natural content and a mix of both

## Slide 3: Introduction
Prediction error of screen content has different statistics than the natural content case
  This can be exploited at the residue coding by a fast update process for the Rice parameter (cRiceParam)
In HEVC, the Rice parameter is conditionally updated depending on the absolute value of the coefficient:
cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )

## Slide 4: Simpler, fast update process for the Rice Parameter
Original:
cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )
Proposed:
cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 << cLastRice ) ), 4 )
Fast adaptation and removal of a condition in the coefficient coding loop
Method tested for lossless and lossy scenarios
Tested with maximum Rice parameter equals 4 and 5

## Slide 5: Alternatively, for the lossy case, the proposed update is used only for transform skip
Fast update applied only when there is no transform (transform skip and the lossless transform bypass)
  In this way, exercised mainly for screen content with no impact for natural content
Proposed:
If transform_skip_flag is equal to 1 or cu_transquant_bypass_flag is equal to 1,
  cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 << cLastRice ) ), 4 )
Otherwise,
  cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )

## Slide 6: Gains on lossless, with large gains for screen content
 | Max Rice = 4 | Max Rice = 5
All Intra Main |  | 
Class F | -0.9% | -0.9%
Class B | -0.1% | 0.2%
SC(GBR) | -4.3% | -6.8%
RangeExt | -0.3% | 0.1%
Overall (w/o SC) | -0.5% | -0.3%
Overall (w/ SC) | -2.4% | -3.5%
Random Access Main |  | 
Class F | -0.4% | -0.5%
Class B | -0.1% | 0.0%
SC(GBR) | -3.5% | -5.6%
RangeExt | -0.3% | -0.2%
Overall (w/o SC) | -0.3% | -0.3%
Overall (w/ SC) | -1.9% | -3.0%
Low delay Main |  | 
Class F | -0.2% | -0.1%
Class B | -0.1% | -0.1%
SC(GBR) | -3.4% | -5.2%
RangeExt | -0.3% | -0.3%
Overall (w/o SC) | -0.2% | -0.2%
Overall (w/ SC) | -1.8% | -2.7%

## Slide 7: Lossy gains are mainly on screen content, and small losses on natural content
BD-rate YUV | Max Rice = 4 |  |  | Max Rice = 5 |  | 
All Intra HE Main-tier |  |  |  |  |  | 
Class F | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0%
Class B | 0.2% | 0.2% | 0.2% | 0.2% | 0.2% | 0.2%
RGB 4:4:4 SC | -0.7% | -0.6% | -0.6% | -0.4% | -0.4% | -0.4%
YCbCr 4:2:2 | 0.1% | 0.2% | 0.1% | 0.1% | 0.2% | 0.2%
YCbCr 4:4:4 | 0.1% | 0.2% | 0.2% | 0.1% | 0.2% | 0.2%
All Intra HE High-tier |  |  |  |  |  | 
Class F | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | 0.0%
Class B | 0.3% | 0.4% | 0.4% | 0.3% | 0.4% | 0.4%
RGB 4:4:4 SC | -1.4% | -1.4% | -1.3% | -1.0% | -0.9% | -0.9%
YCbCr 4:2:2 | 0.2% | 0.3% | 0.3% | 0.3% | 0.3% | 0.3%
YCbCr 4:4:4 | 0.2% | 0.3% | 0.3% | 0.2% | 0.3% | 0.3%
All Intra HE Super High-tier |  |  |  |  |  | 
Class F | -0.3% | -0.4% | -0.3% | -0.1% | -0.2% | -0.1%
Class B | 0.4% | 0.5% | 0.5% | 0.4% | 0.5% | 0.5%
RGB 4:4:4 SC | -2.5% | -2.7% | -2.6% | -2.3% | -2.5% | -2.5%
YCbCr 4:2:2 | 0.4% | 0.4% | 0.4% | 0.4% | 0.5% | 0.5%
YCbCr 4:4:4 | 0.3% | 0.4% | 0.4% | 0.3% | 0.4% | 0.4%

## Slide 8: Larger gains when applied to transform skip only, and no losses for natural content
BD-rate YUV | Max Rice = 4 |  |  | Max Rice = 5 |  | 
All Intra HE Main-tier |  |  |  |  |  | 
Class F | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -0.8% | -0.8% | -0.8% | -0.6% | -0.6% | -0.6%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
All Intra HE High-tier |  |  |  |  |  | 
Class F | -0.4% | -0.4% | -0.4% | -0.2% | -0.2% | -0.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.7% | -1.7% | -1.7% | -1.3% | -1.3% | -1.3%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
All Intra HE Super High-tier |  |  |  |  |  | 
Class F | -0.6% | -0.6% | -0.6% | -0.4% | -0.5% | -0.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -2.9% | -3.1% | -3.1% | -2.7% | -3.0% | -3.0%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 9: For random access and low delay, gains of 1.5% for screen content
BD-rate YUV | Max Rice = 4 |  |  | Max Rice = 5 |  | 
Random Access HE High-tier |  |  |  |  |  | 
Class F | -0.2% | -0.3% | -0.2% | -0.1% | -0.1% | -0.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB 4:4:4 SC | -1.5% | -1.5% | -1.4% | -1.2% | -1.2% | -1.2%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Low delay B HE High-tier |  |  |  |  |  | 
Class F | -0.2% | -0.4% | -0.4% | -0.1% | -0.1% | -0.5%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
RGB 4:4:4 SC | -1.7% | -1.7% | -1.7% | -1.3% | -1.3% | -1.4%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 10: Conclusions
Effective Rice parameter update process for screen content
  Removes one condition present in HEVC version 1
Large gains for lossless
  For lossy, gains for screen content and small losses for natural content
In lossy, most effective when applied only for transform skip
Propose to adopt the method for both, lossless and lossy

## Slide 11: AhG8: Simplified update of the coefficient level Rice parameter JCTVC-M0366
Joel Sole, Marta Karczewicz