## Slide 1: Complexity reduction for residual DPCM in HEVC lossless coding JCTVC-M0439
R&D
© BBC MMXIII
Matteo Naccari, Marta Mrak and Andrea Gabriellini
BBC Research and Development

## Slide 2: Outline
Introduction
Proposed residual DPCM chunking
Experimental results
Conclusion

## Slide 3: Introduction
Residual DPCM has been proposed for HEVC lossless coding in proposals JCTVC-L0117 and JCTVC-M0079
It improves the compression efficiency by exploiting spatial redundancy in intra predicted residuals
Inverse residual DPCM at the decoder

## Slide 4: Proposed residual DPCM chunking
For larger PU sizes, the residual at column or row N-1 depend on the samples at position N-2, N-3, and so on
In order to limit this dependency it is proposed to apply residual DPCM on chunks of residuals with fixed length (8 in proposal)
Example for horizontal DPCM
Chunk 0
Chunk 1
Chunk K
The parallelism can be increased

## Slide 5: Experimental results
Config. Class | All Intra | Random Access | Low Delay B
 | Bit-rate saving | Bit-rate saving | Bit-rate saving
Class F | -9.3% | -5.7% | -4.6%
Class B | -4.5% | -0.9% | -0.6%
SC (GBR) | -11.1% | -7.7% | -7.1%
RangeExt | -2.8% | -0.7% | -0.6%
Overall (w/o SC) | -5.7% | -2.7% | -2.2%
Overall (w/ SC) | -8.4% | -5.2% | -4.6%
Enc Time[%] | 101% | 100% | 100%
Dec Time[%] | 98% | 102% | 98%
Config. Class | All Intra | Random Access | Low Delay B
 | Bit-rate saving | Bit-rate saving | Bit-rate saving
Class F | -9.1% | -5.6% | -4.5%
Class B | -4.5% | -0.9% | -0.6%
SC (GBR) | -11.0% | -7.6% | -7.3%
RangeExt | -2.8% | -0.7% | -
Overall (w/o SC) | -5.7% | -2.7% | -
Overall (w/ SC) | -8.4% | -5.2% | -
Enc Time[%] | 102% | 104% | -
Dec Time[%] | 99% | 106% | -
Compression efficiency for residual DPCM
Compression efficiency for residual DPCM plus proposed chunking

## Slide 6: Conclusions
The proposed residual DPCM chunking may increase the parallelism without compromising the compression performance
It is proposed to accept the presented chunking