## Slide 1: Signaling of Phase Offset in Up-sampling Process and Chroma Sampling Location (JCTVC-M0465)
Qualcomm, InterDigital and Nokia

## Slide 2: Introduction
Up-sampling in SHVC
  Position mapping
    In software: H.264/SVC method (division-free)
    In Test Model texts: division for each position
    Update: problem solved as the meeting decided to take H.264/SVC method
  Assuming fixed chroma sampling location
  Assuming zero-phase down-sampling
Proposed
  Signal chroma sampling location information
  Signal the up-sampling phase shift

## Slide 3: Chroma sampling locations
6 possible locations defined in H.264 and HEVC
a
b
c
d
e
f
H.264/SVC allows different chroma sampling locations in different layers
The adopted position mapping in Incheon meeting only allows fixed location (b) for both layers.

## Slide 4: Zero-phase and symmetric down-sampling
Zero-phase
symmetric
SHVC defines up-sampling assuming down-sampling is zero-phase
If base layer is generated by symmetric down-sampling, perform drop
is observed

## Slide 5: Proposed
Signal chroma sampling location.
Signal phase shift in the up-sampling filtering
sampling_grid_information( ) { | Descriptor
phase_offset_present_flag | u(1)
if ( sampling_grid_info_present_flag ) { | 
horizontal_phase_offset16 | ue(v)
vertical_phase_offset16 | ue(v)
chroma_phase_x_flag | u(1)
chroma_phase_y | u(2)
} | 
sps_extension ( ) { | Descriptor
sampling_grid_information( ) | 
} | 

## Slide 6: Simulation
Codebase: SHM1.0 (IntraBL setting)
In the experiment, reference layer generated with different down-sampling filter phases are used. Performance of using unmatched and matched up-sampling phase are compared.
 | 2X | 1.5X
AI | -10.4% | -9.6%
RA | -7.2% | -7.1%
LDP | -5.7% | -6.7%
Test 1: reference layer is generated with down-sampling of zero phase
Y BD-rate reduction

## Slide 7: Simulation
 | 2X | 1.5X
AI | -9.4% | -8.2%
RA | -6.8% | -6.4%
LDP | -5.6% | -6.4%
Test 2: reference layer is generated with symmetric down-sampling

## Slide 8: Conclusions
Up-sampling in SHVC is analyzed
Proposed:
  Signal chroma sampling location
  Signal luma sampling phase shift
Experimental results show matched up-sampling filter can provide 5%-10% BD-rate reduction compared to mismatched one.

## Slide 9: Filter coefficients used in simulation (Luma)
phase p | interpolation filter coefficients |  |  |  |  |  |  | 
 | fC[ p, 0 ] | fC[ p, 1 ] | fC[ p, 2 ] | fC[ p, 3 ] | fC[ p, 4 ] | fC[ p, 5 ] | fC[ p, 6 ] | fC[ p, 7 ]
0 | 0 | 0 | 0 | 64 | 0 | 0 | 0 | 0
1 | 0 | 1 | -3 | 63 | 4 | -2 | 1 | 0
2 | 0 | 2 | -6 | 61 | 9 | -3 | 1 | 0
3 | -1 | 3 | -8 | 60 | 13 | -4 | 1 | 0
4 | -1 | 4 | -10 | 58 | 17 | -5 | 1 | 0
5 | -1 | 4 | -11 | 52 | 26 | -8 | 3 | -1
6 | -1 | 4 | -11 | 50 | 29 | -9 | 3 | -1
7 | -1 | 4 | -11 | 45 | 34 | -10 | 4 | -1
8 | -1 | 4 | -11 | 40 | 40 | -11 | 4 | -1
9 | -1 | 4 | -10 | 34 | 45 | -11 | 4 | -1
10 | -1 | 3 | -9 | 29 | 50 | -11 | 4 | -1
11 | -1 | 3 | -8 | 26 | 52 | -11 | 4 | -1
12 | 0 | 1 | -5 | 17 | 58 | -10 | 4 | -1
13 | 0 | 1 | -4 | 13 | 60 | -8 | 3 | -1
14 | 0 | 1 | -3 | 9 | 61 | -6 | 2 | 0
15 | 0 | 1 | -2 | 4 | 63 | -3 | 1 | 0

## Slide 10: Filter coefficients used in simulation (Chroma)
phase p | interpolation filter coefficients |  |  | 
 | fC[ p, 0 ] | fC[ p, 1 ] | fC[ p, 2 ] | fC[ p, 3 ]
0 | 0 | 64 | 0 | 0
1 | -2 | 62 | 4 | 0
2 | -2 | 58 | 10 | -2
3 | -4 | 56 | 14 | -2
4 | −4 | 54 | 16 | −2
5 | −6 | 52 | 20 | −2
6 | −6 | 46 | 28 | −4
7 | -4 | 42 | 30 | -4
8 | -4 | 36 | 36 | -4
9 | -4 | 30 | 42 | -4
10 | -4 | 28 | 46 | -6
11 | -2 | 20 | 52 | -6
12 | -2 | 16 | 54 | -4
13 | -2 | 14 | 56 | -4
14 | -2 | 10 | 58 | -2
15 | 0 | 4 | 62 | -2

## Slide 11: Filter coefficients used in simulation (Chroma)
phase p | interpolation filter coefficients |  |  | 
 | fC[ p, 0 ] | fC[ p, 1 ] | fC[ p, 2 ] | fC[ p, 3 ]
0 | 0 | 64 | 0 | 0
1 | -2 | 62 | 4 | 0
2 | -2 | 58 | 10 | -2
3 | -4 | 56 | 14 | -2
4 | −4 | 54 | 16 | −2
5 | −6 | 52 | 20 | −2
6 | −6 | 46 | 28 | −4
7 | -4 | 42 | 30 | -4
8 | -4 | 36 | 36 | -4
9 | -4 | 30 | 42 | -4
10 | -4 | 28 | 46 | -6
11 | -2 | 20 | 52 | -6
12 | -2 | 16 | 54 | -4
13 | -2 | 14 | 56 | -4
14 | -2 | 10 | 58 | -2
15 | 0 | 4 | 62 | -2

## Slide 12: Chroma sample position

## Slide 13: Symmetric vs Zero-phase (with matched resampling filters)
 | 2X | 1.5X
AI | 0.3% | 0.4%
RA | 0.3% | 0.2%
LDP | 0.3% | 0.2%
Anchor: Zero-phase down-sampled BL
Tested: Symmetric down-sampled BL