## Slide 1: Restriction on the Residual DPCM block size JCTVC-N0042
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
Residual DPCM introduces a linear transformation of the lossless residue
  For example, for the vertical intra mode, the decoder derives the residue r by
  RDPCM is applied for block sizes 4×4 to 32×32

## Slide 3: Limiting RDPCM size
Goal
  Complexity reduction: avoid RDPCM transform for large block sizes
  Keep RDPCM performance
Proposal
  Restrict RDPCM size
  Tested max size of 4×4, 8×8 and 16×16

## Slide 4: RDPCM 4×4 provides most of RDPCM gains, while RDPCM 8×8 has no performance loss
RPCM <=16 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
RA | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
LB | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
RPCM <=8 |  |  |  |  | 
AI | 0.2% | 0.0% | -0.1% | 0.0% | 0.0%
RA | 0.1% | 0.0% | -0.1% | -0.1% | 0.0%
LB | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
RPCM <=4 |  |  |  |  | 
AI | 0.8% | 0.2% | -0.1% | 0.4% | 0.0%
RA | 0.6% | 0.0% | -0.1% | 0.2% | 0.0%
LB | 0.5% | 0.0% | -0.1% | 0.1% | 0.0%
RPCM <=0 |  |  |  |  | 
AI | 11.4% | 4.6% | 15.3% | 13.3% | 2.5%
RA | 6.7% | 0.9% | 10.6% | 9.3% | 0.7%
LB | 5.3% | 0.6% | 10.2% | 7.7% | 0.6%
No 32×32 RDPCM
No RDPCM
Only for 4×4 and 8×8
No performance impact

## Slide 5: Conclusions
Restricting RDPCM to 8×8 captures all the gains provided by RDPCM
No need to support RDPCM for large block sizes

## Slide 6: Restriction on the Residual DPCM block size JCTVC-N0042
Joel Sole, Rajan Joshi, Marta Karczewicz