## Slide 1: RCE2 Test B.1: Residue rotation and significance map context JCTVC-N0044
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Introduction
Rotation of the residue was presented in JCTVC-J0093
Constant context for the significance map in JCTVC-J0069
Combination of both in JCTVC-J0468 and in JCTVC-M0333 for HEVC Range Extensions
These are low complexity methods providing efficiency improvement for lossy and lossless coding

## Slide 3: Residue rotation
Residue rotation reverses the scan order for lossless and transform skip
This implies changing the line of code for reading the residue
Change for transform skip:
pResidual[(y*uiStride)+x] = (plCoef[((height-1-y)*width)+(width-1-x)] + offset) >> iTransformShift
Same applies to lossless (i.e., when cu_transquant_bypass_flag equals 1)
For lossless, tested restricting max size of rotation to 4×4 and 8×8

## Slide 4: Constant context for significance map
Transform skip and lossless are coded with one context
  Same context used for all positions
Simplifies context derivation, especially for lossless
Separates the statistics of the natural content from the screen content
  Natural content tends to use transform coding
  Screen content tends to use transform skip

## Slide 5: Rotation gains on lossless for all types of content
Rotation 4×4 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -0.6% | -0.4% | -0.3% | -0.4% | -0.3%
RA | -0.4% | -0.3% | -0.1% | -0.2% | -0.3%
LB | -0.3% | -0.3% | -0.2% | -0.5% | -0.3%
Rotation up to 8×8 |  |  |  |  | 
AI | -0.6% | -0.3% | -0.2% | -0.5% | -0.3%
RA | -0.2% | -0.2% | 0.0% | -0.1% | -0.2%
LB | -0.2% | -0.2% | -0.1% | -0.5% | -0.2%
Rotation for all sizes |  |  |  |  | 
AI | -0.6% | -0.3% | -0.2% | -0.4% | -0.3%
RA | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
LB | -0.2% | -0.1% | 0.1% | -0.4% | -0.1%
Rotation limited to 4×4 performs the best

## Slide 6: Gains are additive with constant context
Constant context performance for lossless
Combination with residue rotation 4×4 lossless
 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -0.5% | -0.2% | 0.1% | -0.1% | -0.1%
RA | -0.4% | -0.1% | 0.0% | 0.0% | -0.1%
LB | -0.3% | -0.1% | 0.0% | 0.1% | -0.1%
 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.3% | -0.6% | -0.2% | -0.6% | -0.4%
RA | -0.9% | -0.5% | -0.3% | -0.6% | -0.4%
LB | -0.8% | -0.5% | -0.3% | -0.7% | -0.4%

## Slide 7: Rotation gains on lossy for screen content
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.5% | -1.7% | -1.9% | -1.4% | -1.5% | -1.7% | -1.3% | -1.3% | -1.4%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.2% | -2.2% | -2.1% | -1.9% | -2.0% | -1.9% | -1.7% | -1.7% | -1.6%
SC YUV 444 | -2.4% | -2.4% | -2.2% | -2.2% | -2.4% | -2.2% | -2.1% | -2.2% | -2.0%
RangeExt | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1%
Enc Time[%] | 101% |  |  | 101% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 102% |  |  | 103% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.0% | -1.3% | -1.4% | -0.9% | -1.1% | -1.2% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.6% | -1.5% | -1.4% | -1.5% | -1.4% | -1.3% |  |  | 
SC YUV 444 | -1.5% | -1.7% | -1.4% | -1.4% | -1.6% | -1.4% |  |  | 
RangeExt | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.8% | -0.9% | -0.4% | -0.6% | -0.7% | -0.6% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -0.9% | -0.8% | -0.9% | -1.0% | -0.9% | -0.9% |  |  | 
SC YUV 444 | -1.1% | -1.0% | -0.9% | -1.0% | -1.0% | -1.0% |  |  | 
RangeExt | 0.0% | -0.3% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
Enc Time[%] | 103% |  |  | 103% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 101% |  |  |  |  | 

## Slide 8: Constant context gains on lossy
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.1% | -0.7% | -0.8% | -1.1% | -0.9% | -1.0% | -1.2% | -1.0% | -1.1%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | -0.1% | 0.2% | 0.1%
SC RGB 444 | -1.3% | -1.0% | -1.0% | -1.2% | -1.0% | -1.0% | -1.1% | -1.0% | -1.0%
SC YUV 444 | -0.8% | -0.6% | -0.5% | -0.8% | -0.6% | -0.6% | -0.8% | -0.7% | -0.6%
RangeExt | -0.1% | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.2% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 102% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 102% |  |  | 103% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.7% | -0.4% | -0.4% | -0.7% | -0.4% | -0.5% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -0.8% | -0.5% | -0.5% | -0.9% | -0.7% | -0.7% |  |  | 
SC YUV 444 | -0.2% | 0.0% | 0.1% | -0.2% | 0.0% | 0.0% |  |  | 
RangeExt | -0.1% | 0.0% | 0.0% | -0.1% | 0.1% | 0.1% |  |  | 
Enc Time[%] | 96% |  |  | 97% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 102% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | 0.5% | 0.1% | -0.5% | 0.0% | -0.3% |  |  | 
Class B | 0.0% | -0.1% | -0.2% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -0.6% | -0.4% | -0.5% | -0.9% | -0.6% | -0.7% |  |  | 
SC YUV 444 | -0.2% | 0.1% | -0.1% | -0.2% | -0.1% | -0.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.1% | 0.2% | 0.4% |  |  | 
Enc Time[%] | 102% |  |  | 102% |  |  |  |  | 
Dec Time[%] | 105% |  |  | 104% |  |  |  |  | 

## Slide 9: Combination gains
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -2.1% | -1.9% | -2.1% | -2.1% | -2.0% | -2.2% | -2.0% | -1.9% | -2.1%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1%
SC RGB 444 | -2.8% | -2.6% | -2.5% | -2.6% | -2.5% | -2.3% | -2.3% | -2.2% | -2.1%
SC YUV 444 | -2.7% | -2.6% | -2.3% | -2.6% | -2.7% | -2.4% | -2.5% | -2.6% | -2.3%
RangeExt | -0.2% | -0.1% | -0.2% | -0.2% | 0.0% | -0.1% | -0.2% | 0.0% | -0.1%
Enc Time[%] | 100% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 103% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.4% | -1.4% | -1.4% | -1.4% | -1.3% | -1.4% |  |  | 
Class B | 0.0% | 0.2% | -0.1% | 0.0% | 0.1% | -0.1% |  |  | 
SC RGB 444 | -2.1% | -1.8% | -1.7% | -1.9% | -1.6% | -1.6% |  |  | 
SC YUV 444 | -1.9% | -1.9% | -1.6% | -1.7% | -1.7% | -1.4% |  |  | 
RangeExt | -0.1% | -0.1% | 0.0% | -0.1% | 0.1% | 0.0% |  |  | 
Enc Time[%] | 97% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 102% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.0% | -0.3% | -1.0% | -1.0% | -0.6% | -1.2% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -1.6% | -1.3% | -1.3% | -1.9% | -1.7% | -1.6% |  |  | 
SC YUV 444 | -0.9% | -0.8% | -0.9% | -1.1% | -1.1% | -1.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 0.3% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 105% |  |  | 104% |  |  |  |  | 

## Slide 10: Conclusions
Simple methods
Gains for screen content
Consistent gains for lossless for all types of content
  Rotation restricted to 4×4 performs better

## Slide 11: RCE2 Test B.1: Residue rotation and significance map context JCTVC-N0044
Joel Sole, Rajan Joshi, Marta Karczewicz