## Slide 1: Signaling and restriction of scaled reference layer offsets (JCTVC-N0054)
JCT-VC 14th Meeting in Vienna, AT, 25 July - 2 Aug. 2013
Takeshi Tsukuba, Tomoyuki Yamamoto
SHARP Corporation

## Slide 2: Summary
Two possible issues relating scaled reference layer offsets:
  Offsets signaling: Syntax num_scaled_ref_layer_offsets is redundant since the number of direct reference pictures for the target layer is already known after decoding video parameter set.
  Inter layer sample prediction outside or across the boundary: It does not contribute much to improve coding efficiency while it brings additional complexity of changing boundary operation depends on offsets position.
  Proposal
    Modified signalling of scaled reference layer offsets
      Remove num_scaled_ref_layer_offsets
      Add scaled_ref_layer_offset_params_present_flag
      Add scaled_ref_layer_offset_present_flag
    Semantics restriction on inter layer sample prediction
      Restrict using inter layer sample prediction outside or across the boundary specified by scaled reference layer offsets.

## Slide 3: A ) A modified signaling on scaled reference layer offsets
sps_extension( ) { | Descriptor
inter_view_mv_vert_constraint_flag | u(1)
sps_extension_vui_parameters( ) | 
num_scaled_ref_layer_offsets | ue(v)
if (NumDirectRefLayers[ nuh_layer_id ] > 1) | 
scaled_ref_layer_offset_params_present_flag | u(1)
for( i = 0; i < num_scaled_ref_layer_offsetsNumDirectRefLayers[ nuh_layer_id ] && scaled_ref_layer_offset_params_present_flag; i++) { | 
scaled_ref_layer_offset_present_flag | u(1)
if ( scaled_ref_layer_offset_present_flag ){ | 
scaled_ref_layer_left_offset[ i ] | se(v)
scaled_ref_layer_top_offset[ i ] | se(v)
scaled_ref_layer_right_offset[ i ] | se(v)
scaled_ref_layer_bottom_offset[ i ] | se(v)
} | 
} | 
} | 
G.7.4.3.2.1 Sequence parameter set extension semantics
scaled_ref_layer_offset_params_present_flag equal to 1 indicates that the scaled reference layer offset parameters for each direct reference layer are present in the SPS. scaled_ref_layer_offset_params_present_flag equal to 0 indicates that indicates that these offsets for each direct reference layer are not present. If not present and NumDirectRefLayers[ nuh_layer_id ] is equal to 0, scaled_ref_layer_offset_params_present_flag is inferred to be equal to 0. Otherwise (If not present and NumDirectRefLayers[ nuh_layer_id ] is equal to 1), scaled_ref_layer_offset_params_present_flag is inferred to be equal to 1.
scaled_ref_layer_offset_present_flag [ i ] equal to 1 indicates that the scaled reference layer offset parameters between the luma sample of the i-th resampled direct reference layer picture with layer_id equal to RefLayerId[ nuh_layer_id ][ i ] and the luma sample of the current picture are present in the SPS. scaled_ref_layer_offset_flag [ i ] equal to 0 indicates that these offsets are not present.
scaled_ref_layer_left_offset[ i ] specifies the horizontal offset between the upper-left luma sample of the resampled i-th direct reference layer picture ,with layer_id equal to RefLayerId[ nuh_layer_id ][ i ], used for inter-layer prediction and the upper-left luma sample of the current picture in units of two luma samples. When not present, the value of scaled_ref_layer_left_offset[ i ] is inferred to be equal to 0.
scaled_ref_layer_top_offset[ i ] specifies the vertical offset between the upper-left luma sample of the resampled i-th direct reference layer picture, with layer_id equal to RefLayerId[ nuh_layer_id ][ i ], used for inter-layer prediction and the upper-left luma sample of the current picture in units of two luma samples. When not present, the value of scaled_ref_layer_top_offset[ i ] is inferred to be equal to 0.
scaled_ref_layer_right_offset[ i ] specifies the horizontal offset between the bottom-right luma sample of the resampled i-th direct reference layer picture ,with layer_id equal to RefLayerId[ nuh_layer_id ][ i ], used for inter-layer prediction and the bottom-right luma sample of the current picture in units of two luma samples. When not present, the value of scaled_ref_layer_right_offset[ i ] is inferred to be equal to 0.
scaled_ref_layer_bottom_offset[ i ] specifies the vertical offset between the bottom-right luma sample of the resampled i-th direct reference layer picture ,with layer_id equal to RefLayerId[ nuh_layer_id ][ i ], used for inter-layer prediction and the bottom-right luma sample of the current picture in units of two luma samples. When not present, the value of scaled_ref_layer_bottom_offset[ i ] is inferred to be equal to 0.

## Slide 4: B) Semantics restriction on inter layer sample prediction
Re-sampled reference layer picture rsPic
Current picture currPic
Following semantics are added after scaled reference layer offsets section:
At the decoding process of a block of current picture, it is not allowed to use inter layer sample prediction (ILP), if a prediction block in the resampled reference picture for ILP satisfies one of the following conditions: ( i.e. inter layer sample prediction outside or across the bounds specified by scaled reference layer offsets parameters shall not be used. )
Case 1: The most-left samples of the prediction block for ILP is outside the most-left samples of the bounds.
xP < max ( 0, ScaledRefLayerLeftOffset )
Case 2: The most-right samples of the prediction block for ILP is outside the most-right samples of the bounds.
xP + wPb -1 > min ( PicWidthinSamplesL - 1, PicWidthInSamplesL - ScaledRefLayerRightOffset -1 )
Case 3: The most-top samples of the prediction block for ILP is outside the most-top samples of the bounds.
yP < max ( 0, ScaledRefLayerTopOffset )
Case 4: The most-bottom samples of the prediction block for ILP is outside the most bottom samples of the bounds.
yP + hPb - 1 > min( PicHeightInSamplesL -1, PicHeightInSamplesL - ScaledRefLayerBottomOffset - 1)
where, ( xP, yP ) indicates the top-left sample location of the prediction block relative to the top-left sample location of the resampled reference picture, ( wPb, hPb ) is the size ( width, height ) of the prediction block.
The boundary specified
by scaled reference layer offsets
Reference layer picture rlPic
(xP,yP)
Case2
(xP,yP)
wPb
hPb
Case1
(xP,yP)
Case3
(xP,yP)
Case4
(xP,yP)
: padding area
A reference block for
Inter layer sample prediction

## Slide 5: Conclusion
  Proposal
    A modified signaling on scaled reference layer offsets
      Remove num_scaled_ref_layer_offsets
      Add scaled_ref_layer_offset_params_present_flag
      Add scaled_ref_layer_offset_present_flag
      ⇒ Remove redundant signalling of offset params
    Semantics restriction on inter layer sample prediction
      Restrict using inter layer sample prediction outside or across the boundary specified by scaled reference layer offsets.
      ⇒ Reduce implementation cost by remove additional boundary operation.