## Slide 1: On resampling process for outside-bounds sample (JCTVC-N0055)
JCT-VC 14th Meeting in Vienna, AT, 25 July - 2 Aug. 2013
Takeshi Tsukuba, Tomoyuki Yamamoto, Tomohiro Ikai
SHARP Corporation

## Slide 2: Summary
Motivation
  In SHM2.0, the resampling process for the samples outside the boundary specified by scaled reference layer offsets ( ROI ) is considered as an additional padding process after interpolation.
  The picture boundary padding process already exists before interpolation.
  It would be desirable to unify padding process.
  Proposal
    Remove an additional padding process for outside-bounds samples
      e.g. ( Clip3( leftStartL, rightEndL – 1, xP ), Clip3( topStartL, bottomEndL – 1, yP ) )
  Experimatal results
    Common Test condition: No BD-Rate changes
  Conclusion
    The modification is beneficial to remove the additional padding process.

## Slide 3: Resampling process for outside-bounds samples in SHM2.0
Outside-bounds sample (xP, yP) is derived as follows:
Figure 1: resampling process for outside-bounds sample
in SHM2.0
Two padding process exist.
However, the picture boundary padding process already exits. (i.e. first padding process )
It would be desirable to unify padding process.
Derive reference sample location
(xRef, yRef) corresponding to boundary sample location (xP’,yP’)
Pad samples outside rlPic on the filter area including (xRef, yRef)
(i.e. first padding process)
Derive a sample value of (xP’, yP’) by resampling
Set / Copy the resample value to that of (xP, yP)
(i.e. second padding process )
Notes: 1 ) Derive reference sample location (xRef, yRef) corresponding to boundary sample location (xP’, yP’) instead of (xP, yP).
2) Pad samples outside picture boundary on the filter area with picture boundary samples on rlPic. (i.e. first padding as in Figure 1)
3) Generate a resampled value of (xP’, yP’) by filtering samples on the filter area
4) Set / Copy the resampled value to that of (xP, yP)
(i.e. second padding process in Figure 1)

## Slide 4: Proposed resampling process for outside-bounds samples
Outside-bounds sample (xP, yP) is derived as follows:
Figure 2: proposed resampling process
for outside-bounds sample
Directly derive a reference sample location and remove second padding process.
Therefore, padding process can be unified.
Directly derive a reference sample location (xRef, yRef) corresponding to boundary sample location (xP, yP)
Pad samples outside rlPic on the filter area including (xRef, yRef)
(i.e. first padding process)
Derive a sample value of (xP, yP) by resampling
Set / Copy the resample value to that of (xP, yP)
(i.e. second padding process )
Notes: 1 ) Derive reference sample location (xRef, yRef) corresponding to boundary sample location (xP’, yP’) instead of (xP, yP).
2) Pad samples outside picture boundary on the filter area with picture boundary samples on rlPic. (i.e. first padding as in Figure 1)
3) Generate a resampled value of (xP’, yP’) by filtering samples on the filter area
4) Set / Copy the resampled value to that of (xP, yP)
(i.e. second padding process in Figure 1)

## Slide 5: Experimental results ( common test condition)
Proposed method is implemented on top of SHM2.0.
A bug on SHM2.0 which padding process for outside bounds samples is not correct when scaled reference layer offsets are set to positive values is fixed. ( see next page )
BD-Rate gain: No changes compared to SHM2.0 + bugfix

## Slide 6: A bug on SHM2.0
Figure 3: resampled reference layer (BQTerrace, bl qp=26, el qp=26, frameNo=1) on SHM2.0. Red boxes indicate padding area on additional test condition.
The length of left-side padding area is not correct.
It shoud be fixed.

## Slide 7: Additional experimental results
In order to evaluate coding efficiency when scaled reference layer offsets having positive values, additional tests were done as described in Table 1.
BD-rate gain( EL only ) : 0.00%, -0.01% and -0.01% for AI 2x, RA 2x and LB 2x compared to SHM2.0 + bugfix.
Sequences | Class B
The number of frames | Full frame
EL resolution | 1920x1080 (no change)
BL resolution | 920x496 (cropped from 960x540)
scaled_ref_layer_left_offset | 20
scaled_ref_layer_top_offset | 22
scaled_ref_layer_right_offset | 20
scaled_ref_layer_bottom_offset | 22
Table 1: Test condition

## Slide 8: Conclusion
  Proposal
    Remove an additional padding process for outside-bounds samples
      e.g. ( Clip3( leftStartL, rightEndL – 1, xP ), Clip3( topStartL, bottomEndL – 1, yP ) )
    ⇒ The modification is beneficial to remove the additional padding process.
  Experimatal results
    Common Test condition: No BD-Rate changes
    Additional Test condition: class B, EL:1920x1080, BL:920x496, scaled reference layer offsets are set as follows:
    scaled_ref _layer_left_offset = scaled_ref_layer_right_offset = 20,
    scaled_ref_layer_top_offset = scaled_ref_layer_bottom_offset =22
    BD-rate gain( EL only ) : 0.00%, -0.01% and -0.01% for AI 2x, RA 2x and LB 2x
  It is recommend to adopt the next SHM and WD.
  Many thanks HHI for cross-check.