## Slide 1: RCE2: Experimental results for Test C.1 JCTVC-N0074
R&D
© BBC MMXIII
Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Outline
Introduction
Proposed inter prediction residual DPCM
Experimental results
Conclusion

## Slide 3: Introduction
After motion compensation, the residuals may present spatial correlation, namely in areas with high frequency details (sharp edges, text, etc.)
This spatial redundancy may be exploited in lossless coding by applying Residual DPCM (RDPCM) on top of motion compensated residues
Three RDPCM mode can be tested, the one bring the lowest error energy is selected
No RDPCM
RDPCM horizontal
RDPCM vertical

## Slide 4: Proposed inter residual DPCM
Inter RDPCM is tested for both lossless and lossy coding
For lossless coding, two different implementations are tested:
  CU-based (RDPCM over CU residuals and prediction mode sent one per CU)
  TU-based (RDPCM over TU residuals and prediction mode sent one per TU)
For lossy coding, inter RDPCM is applied when transform skip is selected
The best RDPCM mode is selected by minimising the SAD for the obtained residuals
The inter RDPCM mode is signalled via two binary flags:
  One to indicate whether RDPCM is applied on the selected CU/TU
  One to indicate on which direction RDPCM is applied (horizontal or vertical)

## Slide 5: Experimental results (Lossless)
Inter RDPCM CU-based implementation
Configuration Class | Random Access (RA) | Low Delay (LD)
 | Bit-rate savings [%] | Bit-rate savings [%]
Class F | -3.4% | -5.5%
Class B | -0.4% | -0.5%
SC RGB 444 | -2.7% | -5.1%
SC YUV 444 | -1.7% | -3.4%
Range Ext. | -0.2% | -0.2%
Enc. Time [%] | 104% | 103%
Dec. Time [%] | 98% | 97%
Inter RDPCM TU-based implementation
Configuration Class | Random Access (RA) | Low Delay (LD)
 | Bit-rate savings [%] | Bit-rate savings [%]
Class F | -3.4% | -5.5%
Class B | -0.4% | -0.5%
SC RGB 444 | -3.3% | -5.7%
SC YUV 444 | -2.0% | -4.2%
Range Ext. | -0.2% | -0.3%
Enc. Time [%] | 104% | 102%
Dec. Time [%] | 98% | 95%

## Slide 6: Experimental results (Lossy)
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.1% | -1.0% | -1.1% | -1.3% | -1.2% | -1.2%
SC YUV 444 | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | -0.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 103% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
Class F | -0.2% | -0.2% | -0.3% | -0.3% | -0.3% | -0.3%
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.0%
SC RGB 444 | -3.3% | -3.1% | -3.2% | -3.2% | -3.2% | -3.2%
SC YUV 444 | -1.1% | -1.2% | -1.3% | -1.2% | -1.3% | -1.4%
RangeExt | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 

## Slide 7: Conclusions
Inter residual DPCM brings compression improvements, namely for screen contents
To harmonise lossless and lossy coding application, TU-based implementation should be adopted
It is proposed to consider the inter RDPCM for adoption