## Slide 1: Non-RCE2: Complexity reduction for inter residual DPCM in lossless coding JCTVC-N0075
R&D
© BBC MMXIII
Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Outline
Introduction
Proposed residual DPCM chunking
Experimental results
Conclusion

## Slide 3: Introduction
Inter Residual DPCM (RDPCM) is proposed in JCTVC-N0074 and tested in RCE2 for lossless coding
It improves the compression efficiency by exploiting spatial redundancy in still present in motion compensated residuals
Residual reconstruction at the decoder

## Slide 4: Complexity in inter residual DPCM
At the decoder the average number of operations per sample is: (N-1)/2
In order to lower the number of operation per sample it is proposed to apply inter RDPCM on chunks of residuals with fixed length (8 in proposal)
Example for horizontal DPCM and 32×32 block size

## Slide 5: Experimental results
Inter RDPCM chunking for CU-based implementation
Configuration Class | Random Access (RA) |  | Low Delay (LD) | 
 | Bit-rate savings [%] |  | Bit-rate savings [%] | 
 | Chunking off | Chunking on | Chunking off | Chunking on
Class F | -3.4% | -2.9% | -5.5% | -4.6%
Class B | -0.4% | -0.4% | -0.5% | -0.5%
SC RGB 444 | -2.7% | -2.6% | -5.1% | -4.2%
SC YUV 444 | -1.7% | -1.5% | -3.4% | -3.1%
Range Ext. | -0.2% | -0.2% | -0.2% | -0.2%
Enc. Time [%] | 104% | 103% | 103% | 103%
Dec. Time [%] | 98% | 96% | 97% | 96%
Configuration Class | Random Access (RA) |  | Low Delay (LD) | 
 | Bit-rate savings [%] |  | Bit-rate savings [%] | 
 | Chunking off | Chunking on | Chunking off | Chunking on
Class F | -3.4% | -3.0% | -5.5% | -4.7%
Class B | -0.4% | -0.4% | -0.5% | -0.5%
SC RGB 444 | -3.3% | -3.0% | -5.7% | -5.0%
SC YUV 444 | -2.0% | -1.9% | -4.2% | -3.8%
Range Ext. | -0.2% | -0.2% | -0.3% | -0.3%
Enc. Time [%] | 104% | 105% | 102% | 103%
Dec. Time [%] | 98% | 96% | 95% | 95%
Inter RDPCM chunking for TU-based implementation

## Slide 6: Conclusions
The proposed residual DPCM chunking reduces the average number of operations per sample with a little loss in compression efficiency
It is proposed to accept the presented chunking

## Slide 7
Predictor reset every 8 samples: 8 operations per sample