## Slide 1: On support for alpha channel in HEVC JCTVC-N0077
R&D
© BBC MMXIII
Matteo Naccari and Marta Mrak
BBC Research and Development

## Slide 2: Outline
Introduction
Alpha channel support with secondary pictures and re-use of alpha channel from previous frames
  Proposed syntax and semantics changes
Support for clipping and threshold alpha channel values
  Proposed syntax and semantics changes
Conclusions

## Slide 3: Introduction
Alpha channel is required for professional video coding applications
Alpha channels specify for each pixels in the video its degree of transparency or opacity
Alpha channel signals can be compressed using the coding tools of their texture frame counter parts (both lossy and lossless)
It is crucial to signal alpha channel in the same access unit of the associated texture frame

## Slide 5: Alpha channel support with secondary pictures and re-use of alpha channel from previous frames
To keep texture frames and associated alpha channel together the secondary picture concept is used
Moreover some applications require only one alpha channel which can be then re-used
Same access unit

## Slide 6: Proposed syntax and semantics changes
Three main definitions are added to the RExt WD:
  Primary picture: picture containing texture data and having normative effect in the decoding process
  Secondary picture: carries alpha channel data, same syntax and semantics of monochrome primary picture, no normative effect
  Alpha blending process: non normative process for display purposes
A new syntax element is introduced for the SPS of the RExt:
A new flag is added to the PPS to signal the presence of the secondary picture

## Slide 7: Sequence parameter set for RExt
seq_parameter_set_extension_rbsp( ) {
sps_seq_parameter_set_id
secondary_format_idc
if( secondary_format_idc != 0 ) {
bit_depth_secondary_minus8
alpha_opaque_value
alpha_transparent_value
}
additional_extension_flag
rbsp_trailing_bits( )
}
0 = No secondary picture
1 = One secondary picture for each access unit
2 = One secondary picture may be present for each access unit

## Slide 8: Picture parameter set
pic_parameter_set_rbsp( ) {
...
pps_extension_flag
if( pps_extension_flag ) {
secondary_pic_present_flag
while( more_rbsp_data( ) )
pps_extension_data_flag
}
rbsp_trailing_bits( )
}
0 = No secondary picture in this access unit
1 = Secondary picture present
If secondary picture is not present, the samples of a long-term reference picture in the DPB are used for the current picture

## Slide 9: Secondary picture signalling mechanism
Secondary picture
Repeated
Time
POC
0
1
2
3
4
5
RefPicSetLtCurr[0] = pic0

## Slide 10: Support for clipping and threshold alpha channel values
After decoding alpha channel samples, their value may need clipping in the range [αtransparent, αopaque]
Two different clipping/threshold operations are usually required
Clipping/threshold
To obtain binary alpha channels
To keep the values in the range

## Slide 11: Proposed syntax and semantics changes
seq_parameter_set_extension_rbsp( ) {
sps_seq_parameter_set_id
secondary_format_idc
if( secondary_format_idc != 0 ) {
bit_depth_secondary_minus8
alpha_opaque_value
alpha_transparent_value
alpha_threshold_type
if( alpha_threshold_type == 1 )
alpha_threshold_binary
}
additional_extension_flag
rbsp_trailing_bits( )
}
0 = Alpha channel values unchanged
1 = Binary clipping/threshold
2 = Clipping of the values in the range [αtransparent, αopaque]

## Slide 12: Conclusions
Alpha channel support should be included in the RExt of HEVC
Secondary pictures provide an effective mean for such support
It is proposed to adopt the presented syntax and semantics changes