## Slide 1: JCTVC-N0078
SCE1: Results of Test 2.2 on phase compensation by signaling filter coefficients at PPS with sample shift
Koohyar Minoo and David Baylon
ARRIS

## Slide 2: Problem(s) Being Addressed
Current upsampling filters in SHM are fixed. This will have the following implications:
The down-sampling phase offset should be known during the up-sampling process. Currently these phase offsets are assumed to be known.
To cover a reasonable number of sub-pixel positions at the base layer SHVC needs a large number of filters (for each luma and chroma) to be designed.

## Slide 3: Compensating for the down-sampling phase offset
The following solution is proposed in Test 2.2:
Encoder signals the filter coefficients for each sub-pixel filter index (indices are calculated assuming zero phase offset). The filter coefficients will make sure the interpolation for each index has the proper phase shift.
Signaling of filter parameters occurs at PPS level.

## Slide 4: Performance vs. SHM-2.0
 | 2x |  |  | 1.5x |  | 
 | Y | U | V | Y | U | V
AI | -9.4% | -10.9% | -10.9% | -8.4% | -10.2% | -10.2%
RA | -6.6% | -4.1% | -3.9% | -6.2% | -5.1% | -4.6%
LD-B | -4.8% | -2.7% | -2.5% | -6.1% | -4.9% | -4.4%
LD-P (optional) | -5.8% | -3.2% | -3.1% | -6.9% | -5.5% | -4.7%

## Slide 5: Performance vs. Test 1.2 (1/16 pel)
 | 1.5x |  | 
 | Y | U | V
AI | -0.7% | -0.8% | -0.8%
RA | -0.6% | -0.5% | -0.3%
LD-B | -0.5% | -0.5% | -0.4%
LD-P (optional) | -0.6% | -0.6% | -0.6%

## Slide 6: Advantages of Proposed Approach
Compensates for arbitrary phase shift due to down-sampling with a small number of filters.
No need to design and verify a large set of fixed of filters, given the limited test conditions available and affordable.
Less computation and rounding operations
Optimized filters increase coding efficiency