## Slide 1: Non-RCE2:Simplified sample based intra prediction for lossless coding [JCTVC-N0079]
J.Zhu, W.Zheng and K.Kazui
Fujitsu R&D Center Co., Ltd
FUJITSU LABORATORIES LTD.
14th JCT-VC meeting, Vienna AT, 2013/7/25-8/2

## Slide 2: Summary
Proposal of simplified SAP for lossless mode
  Only 13 out of 35 possible intra prediction modes are used
  DC and planer unchanged as in HEVC ver.1
  Other 11 modes perform sample-based prediction without interpolation
Performance
  All-intra main configuration
  2.8% gain for SC sequences in RGB/YUV
  1.6% gain for RExt sequences
  Encoding time is reduced to 86%

## Slide 3: Background
Sample-based angular intra prediction (SAP) in RExt draft 3
  JCTVC-M0056 Test 4
  Applied only in horizontal and vertical
  Other 31 directions are not sample-based
    Original proposal (JCTVC-L0176) applies SAP to all directions.
Residual DPCM approach in RCE2
  Functionality of DPCM overlaps with that of SAP

## Slide 4: Proposal
Simplified SAP
  Apply SAP to other directions than horizontal and vertical
    Maximum number of angular intra prediction mode is reduced to 11.
    DC and angular are remain the same as in HEVC version 1.
  Simplified pixel prediction
    No interpolation
Benefits
  Reduced complexity
  Coding gain improvement

## Slide 5: Diagram

## Slide 6: Diagram (Cont.)
RExt Draft 3
Proposed

## Slide 7: 11 directions

## Slide 8: 11 directions

## Slide 9: 11 directions

## Slide 10: Signalling
Changes in subclause 8.4.1 (Luma) and 8.4.3 (Chroma)
  Maximum number of angular modes are reduced to 11

## Slide 11: Experimental result
Test conditions: RCE2 based
  All-Intra Main configuration
Anchor: HM 10.1-RExt-3.0 + patch in RCE2
Proposal: On top of anchor
Cross-check by KDDI (JCTVC-N0367)
  Some mismatches are reported in anchor encoding.
 | All Intra Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 5.2 | 5.3 | -0.7%
Class B | 2.2 | 2.2 | 0.2%
SC RGB 444 | 10.1 | 10.4 | -2.8%
SC YUV 444 | 11.1 | 11.6 | -2.8%
RangeExt | 2.3 | 2.3 | -1.6%
Enc Time[%] | 86% |  | 
Dec Time[%] | 99% |  | 

## Slide 12: Complexity (DPCM part)
 | 4×4 |  | 8×8 | 
 | Additional Complexity | Additions/Sample | Additional Complexity | Additions/Sample
Proposed | 24 adds | 1.5 | 224 adds | 3.5

## Slide 13: Conclusion
Simplified SAP
  Improved coding gain: 2.8% for SCC, 1.6% for Rext
  Reduced encoder complexity: 86%
Request to study in RCE