## Slide 1: Non-RCE2: Skip of neighbouring samples filtering in intra prediction for lossless coding [JCTVC-N0080]
J.Zhu and K.Kazui
Fujitsu R&D Center Co., Ltd
FUJITSU LABORATORIES LTD.
14th JCT-VC meeting, Vienna AT, 2013/7/25-8/2

## Slide 2: Summary
Proposal of removing neighboring samples filtering process for lossless coding
  Filtering process is no longer needed for lossless coding
  VCEG-AO11 proposed similar changes to AVC specification
Performance
  All-intra main configuration
  Slightly better coding gain for SCC: 0.2% (RGB), 0.4% (YUV)

## Slide 3: Proposed change
Subclause 8.4.4.2.3
  Inputs to this process are:
  – the neighbouring samples p[ x ][ y ], with x = −1, y = −1..nTbS * 2 − 1 and x = 0..nTbS * 2 − 1, y = −1,
  – a variable nTbS specifying the transform block size.
  Outputs of this process are the filtered samples pF[ x ][ y ], with x = −1, y = −1..nTbS * 2 − 1 and x = 0..nTbS * 2 − 1, y = −1.
  The variable filterFlag is derived as follows:
  – If one or more of the following conditions are true, filterFlag is set equal to 0:
  – cu_transquant_bypass_flag is equal to 1.
  – predModeIntra is equal to INTRA_DC.
  – nTbS is equal 4.
  – Otherwise, the following applies:
  ….

## Slide 4: Experimental result
Test conditions: RCE2 based
  All-Intra Main configuration
Anchor: HM 10.1-RExt-3.0 + patch in RCE2
Proposal: On top of anchor
 | All Intra Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 5.2 | 5.2 | 0.0%
Class B | 2.2 | 2.2 | 0.0%
SC RGB 444 | 10.1 | 10.1 | -0.2%
SC YUV 444 | 11.1 | 11.2 | -0.4%
RangeExt | 2.3 | 2.3 | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 96% |  | 

## Slide 5: JCTVC-N0079 + JCTVC-N0080
 | All Intra Main |  | 
 | compression ratio |  | Bit-rate saving
 | Reference | Tested | 
Class F | 5.2 | 5.3 | -0.7%
Class B | 2.2 | 2.2 | 0.2%
SC RGB 444 | 10.1 | 10.4 | -2.9%
SC YUV 444 | 11.1 | 11.6 | -2.8%
RangeExt | 2.3 | 2.3 | -2.1%
Enc Time[%] | 84.98% |  | 
Dec Time[%] | 97.76% |  | 

## Slide 6: Conclusion
Proposal of removing neighboring samples filtering process for lossless coding
Suggest to adopt in RExt draft.