## Slide 1: RCE2 Test A.3: Simplified update of the coefficient level Rice parameter JCTVC-N0101
Joel Sole, Marta Karczewicz

## Slide 2: Introduction
Prediction error of screen content and lossless coding has different statistics than lossy coded natural content
  This can be exploited at the residue coding by a fast update process for the Rice parameter (cRiceParam)
In HEVC, the Rice parameter is conditionally updated depending on the absolute value of the coefficient:
cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )

## Slide 3: Proposing simple, fast updates for the Rice parameter
Original:
cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )
Method 1:
cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 << cLastRice ) ), 4 )
Method 2:
cRiceParam = Min( cLastRice + ( AbsLevel >> ( 1 + ( 1 << cLastRice ) ) ), 4 )
Method 3:
cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 + cLastRice ) ), 4 )

## Slide 4: Proposing simple, fast updates for the Rice parameter
Fast adaptation and removal of a condition in the coefficient coding loop
Methods tested for lossless and lossy scenarios
  For lossy, tested always and also, only for transform skip
Tested with maximum Rice parameter equals 4 and 5

## Slide 5: Alternatively, for the lossy case, the proposed updates are used only for transform skip
Fast update applied only when there is no transform (transform skip and lossless transform bypass)
  In this way, exercised mainly for screen content
For the method 3 and max Rice parameter equal to 4:
If transform_skip_flag is equal to 1 or cu_transquant_bypass_flag is equal to 1,
  cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 + cLastRice ) ), 4 )
Otherwise,
  cRiceParam = Min( cLastRice + ( AbsLevel > ( 3 * ( 1 << cLastRice ) ) ? 1 : 0 ), 4 )

## Slide 6: Gains on lossless, with large gains for screen content
Method 1 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -0.8% | 0.0% | -4.5% | -3.0% | -0.2%
RA | -0.4% | -0.1% | -3.6% | -2.7% | 0.3%
LB | -0.2% | -0.1% | -3.3% | -2.9% | 0.3%
Method 2 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -0.9% | -0.1% | -4.7% | -3.3% | -0.9%
RA | -0.5% | 0.0% | -3.8% | -2.9% | -0.5%
LB | -0.3% | 0.0% | -3.7% | -3.0% | -0.4%
Method 3 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.0% | 0.0% | -4.8% | -3.4% | -1.1%
RA | -0.5% | 0.0% | -4.0% | -3.0% | -0.6%
LB | -0.3% | 0.0% | -3.7% | -3.1% | -0.6%
Method 1 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -0.9% | 0.1% | -6.9% | -3.7% | 0.5%
RA | -0.4% | -0.1% | -5.6% | -3.4% | 1.3%
LB | -0.1% | -0.1% | -5.2% | -3.6% | 1.3%
Method 2 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.1% | 0.0% | -7.1% | -4.1% | -0.7%
RA | -0.6% | 0.0% | -5.7% | -3.7% | 0.1%
LB | -0.3% | 0.0% | -5.4% | -3.9% | 0.1%
Method 3 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.2% | 0.0% | -7.3% | -4.2% | -0.9%
RA | -0.6% | 0.0% | -6.0% | -3.6% | 0.0%
LB | -0.3% | 0.0% | -5.4% | -3.9% | 0.0%
Max Rice 4
Max Rice 5

## Slide 7: Lossy-case gains are mainly on screen content
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.2% | -0.3% | -0.3% | -0.5% | -0.5% | -0.5% | -0.7% | -0.7% | -0.7%
Class B | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
SC RGB 444 | -1.2% | -1.1% | -1.1% | -2.3% | -2.3% | -2.2% | -3.7% | -3.8% | -3.8%
SC YUV 444 | -0.2% | -0.3% | -0.2% | -0.6% | -0.6% | -0.5% | -1.2% | -1.3% | -1.3%
RangeExt | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 97% |  |  | 97% |  |  | 99% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.3% | -0.3% | -0.3% | -0.4% |  |  | 
Class B | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.1% |  |  | 
SC RGB 444 | -1.1% | -1.1% | -1.1% | -2.0% | -2.0% | -2.0% |  |  | 
SC YUV 444 | 0.1% | 0.0% | 0.2% | -0.2% | -0.2% | -0.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 100% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 100% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.3% | -0.6% | -0.2% | -0.2% | -0.4% | -0.4% |  |  | 
Class B | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.2% | -1.1% | -1.1% | -2.2% | -2.0% | -2.1% |  |  | 
SC YUV 444 | -0.2% | 0.0% | -0.3% | -0.5% | -0.3% | -0.5% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 102% |  |  | 103% |  |  |  |  | 
Dec Time[%] | 104% |  |  | 102% |  |  |  |  | 
Case: Method 2 – Max Rice 4 – Always applied (transform & transform skip)

## Slide 8: Lossy-case gains are mainly on screen content
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.2% | -0.4% | -0.3% | -0.5% | -0.6% | -0.5% | -0.8% | -0.9% | -0.8%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.3% | -1.2% | -1.2% | -2.5% | -2.5% | -2.5% | -4.0% | -4.3% | -4.2%
SC YUV 444 | -0.2% | -0.3% | -0.2% | -0.7% | -0.7% | -0.6% | -1.4% | -1.5% | -1.4%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 101% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.3% | -0.3% | -0.3% | -0.3% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -1.1% | -1.1% | -1.0% | -2.1% | -2.1% | -2.1% |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.1% | -0.3% | -0.3% | -0.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 94% |  |  | 94% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 102% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | 0.1% | 0.4% | -0.2% | -0.1% | -0.1% |  |  | 
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -0.5% | -0.4% | -0.4% | -1.9% | -1.7% | -1.8% |  |  | 
SC YUV 444 | -0.2% | -0.1% | -0.2% | -0.3% | -0.2% | -0.3% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 100% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 102% |  |  |  |  | 
Case: Method 3 – Max Rice 4 – Always applied

## Slide 9: Similar results for maximum Rice equals to 5
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.2% | -0.3% | -0.3% | -0.4% | -0.4% | -0.4% | -0.7% | -0.7% | -0.7%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.2% | -1.2% | -1.1% | -2.3% | -2.3% | -2.3% | -4.1% | -4.5% | -4.4%
SC YUV 444 | -0.2% | -0.3% | -0.2% | -0.6% | -0.6% | -0.5% | -1.3% | -1.3% | -1.3%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  |  | 94% |  |  | 95% |  | 
Dec Time[%] | 101% |  |  | 100% |  |  | 100% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.3% | -0.2% | -0.3% | -0.3% |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1% |  |  | 
SC RGB 444 | -1.1% | -1.1% | -1.0% | -2.2% | -2.1% | -2.1% |  |  | 
SC YUV 444 | 0.0% | 0.0% | 0.0% | -0.3% | -0.3% | -0.2% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 98% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 101% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | -0.4% | 0.1% | -0.2% | -0.3% | -0.2% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -0.9% | -0.8% | -0.8% | -1.8% | -1.7% | -1.8% |  |  | 
SC YUV 444 | -0.3% | -0.2% | -0.2% | -0.4% | -0.4% | -0.4% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 100% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 101% |  |  |  |  | 
Case: Method 3 – Max Rice 5 – Always applied

## Slide 10: Similar results when applied only to transform skip
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.2% | -0.3% | -0.3% | -0.5% | -0.5% | -0.5% | -0.8% | -0.8% | -0.8%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -1.2% | -1.2% | -1.2% | -2.4% | -2.4% | -2.4% | -3.8% | -4.1% | -4.0%
SC YUV 444 | -0.3% | -0.3% | -0.2% | -0.7% | -0.7% | -0.6% | -1.4% | -1.4% | -1.4%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  |  | 95% |  |  | 96% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 102% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.1% | -0.2% | -0.1% | -0.3% | -0.3% | -0.3% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -1.1% | -1.1% | -1.0% | -2.1% | -2.1% | -2.1% |  |  | 
SC YUV 444 | -0.1% | -0.1% | -0.1% | -0.4% | -0.4% | -0.3% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 96% |  |  | 97% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.2% | -0.5% | -0.5% | -0.3% | -0.5% | -0.5% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -0.3% | -0.2% | -0.2% | -1.8% | -1.7% | -1.8% |  |  | 
SC YUV 444 | 0.1% | 0.3% | 0.1% | -0.2% | -0.1% | -0.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 99% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 101% |  |  |  |  | 
Case: Method 3 – Max Rice 4 – Applied to transform skip

## Slide 11: Conclusions
Effective Rice parameter update process for screen content and lossless
  Removes one condition present in HEVC version 1
Large gains for lossless, especially for screen content
  Maximum Rice parameter 4 has better performance for natural content
  Maximum Rice parameter 5 has better performance for screen content
For lossy, methods provide gains for screen content

## Slide 12: RCE2 Test A.3: Simplified update of the coefficient level Rice parameter JCTVC-N0101
Joel Sole, Marta Karczewicz