## Slide 1: JCTVC-N0143 On Mode Dependent Intra Smoothing for Range Extension
G. Laroche, C. Gisquet, T. Poirier
JCT-VC 14th Meeting, Vienna, July 2013

## Slide 2: Current status of MDIS
Mode-dependent Intra Smoothing in HEVC v1
  A way to only predict low frequency content
  Luma-only
    Chroma in 4:2:0 has little high frequency
  No filtering for 4x4 TU size
  No filtering for DC, VER and HOR
  Other modes are filtered according to a table
MDIS in Rext
  Activated for Chroma in 4:4:4 using the same conditions as Luma
  M0106: even more filtering for chroma
TU size |  |  |  | 
 | 4x4 | 8x8 | 16x16 | 32x32
0 (planar) | 0 | 1 | 1 | 1
1 (DC) | 0 | 0 | 0 | 0
2 | 0 | 1 | 1 | 1
3 | 0 | 0 | 1 | 1
4 | 0 | 0 | 1 | 1
5 | 0 | 0 | 1 | 1
6 | 0 | 0 | 1 | 1
7 | 0 | 0 | 1 | 1
8 | 0 | 0 | 1 | 1
9 | 0 | 0 | 0 | 1
10 (HOR) | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 1
12 | 0 | 0 | 1 | 1
13 | 0 | 0 | 1 | 1
14 | 0 | 0 | 1 | 1
15 | 0 | 0 | 1 | 1
16 | 0 | 0 | 1 | 1
17 | 0 | 0 | 1 | 1
18 | 0 | 1 | 1 | 1
19 | 0 | 0 | 1 | 1
20 | 0 | 0 | 1 | 1
21 | 0 | 0 | 1 | 1
22 | 0 | 0 | 1 | 1
23 | 0 | 0 | 1 | 1
24 | 0 | 0 | 1 | 1
25 | 0 | 0 | 0 | 1
26 (VER) | 0 | 0 | 0 | 0
27 | 0 | 0 | 0 | 1
28 | 0 | 0 | 1 | 1
29 | 0 | 0 | 1 | 1
30 | 0 | 0 | 1 | 1
31 | 0 | 0 | 1 | 1
32 | 0 | 0 | 1 | 1
33 | 0 | 0 | 1 | 1
34 | 0 | 1 | 1 | 1

## Slide 3: Proposed modification
Also increase filtering of luma
  Current table more adapted to unequal frequency content behavior between chroma and luma in 4:2:0
  Chroma and luma now behave a lot more similarly for 4:4:4
Complexity considerations
  What should not be modified:
    4x4 because it is the worst case
    DC/HOR/VER do not benefit from filtering and can be considered simple modes for a fast encoder
  Table reuse:
    4x4 not modified
    All other TU sizes use the existing 32x32 table
TU size | N=4 | 8x8 | 16x16 | N>4
0 (planar) | 0 | 1 | 1 | 1
1 (DC) | 0 | 0 | 0 | 0
2 | 0 | 1 | 1 | 1
3 | 0 | 0 | 1 | 1
4 | 0 | 0 | 1 | 1
5 | 0 | 0 | 1 | 1
6 | 0 | 0 | 1 | 1
7 | 0 | 0 | 1 | 1
8 | 0 | 0 | 1 | 1
9 | 0 | 0 | 0 | 1
10 (HOR) | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 1
12 | 0 | 0 | 1 | 1
13 | 0 | 0 | 1 | 1
14 | 0 | 0 | 1 | 1
15 | 0 | 0 | 1 | 1
16 | 0 | 0 | 1 | 1
17 | 0 | 0 | 1 | 1
18 | 0 | 1 | 1 | 1
19 | 0 | 0 | 1 | 1
20 | 0 | 0 | 1 | 1
21 | 0 | 0 | 1 | 1
22 | 0 | 0 | 1 | 1
23 | 0 | 0 | 1 | 1
24 | 0 | 0 | 1 | 1
25 | 0 | 0 | 0 | 1
26 (VER) | 0 | 0 | 0 | 0
27 | 0 | 0 | 0 | 1
28 | 0 | 0 | 1 | 1
29 | 0 | 0 | 1 | 1
30 | 0 | 0 | 1 | 1
31 | 0 | 0 | 1 | 1
32 | 0 | 0 | 1 | 1
33 | 0 | 0 | 1 | 1
34 | 0 | 1 | 1 | 1

## Slide 4: Experiment
Using RExt3.0 software and following K1006 common test conditions
Results for AI configurations
Runtime unaffected
Inter configurations have smaller yet present gain
 | All Intra Main-tier |  |  |  | All Intra High-tier |  |  |  | All Intra Super-High-tier |  |  | 
 | Y | U | V | YUV | Y | U | V | YUV | Y | U | V | YUV
RGB 4:4:4 | -0.5% | -0.3% | -0.3% | -0.4% | -0.4% | -0.2% | -0.3% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2%
YCbCr 4:4:4 | -0.2% | -0.1% | -0.2% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2% | -0.3% | 0.0% | -0.1% | -0.2%
YCbCr 4:2:2 | N.A. |  |  | N.A. |  | N.A. |  | N.A. |  | N.A. |  | N.A.
Overall | -0.4% | -0.2% | -0.3% |  | -0.4% | -0.1% | -0.2% |  | -0.3% | -0.1% | -0.2% | 
Enc Time[%] | 100% |  |  |  | 100% |  |  |  | 100% |  |  | 
Dec Time[%] | 101% |  |  |  | 100% |  |  |  | 100% |  |  | 

## Slide 5: Conclusions
Provides interesting gains for AI (MT/HT/SHT): -0.34%(Y), -0.14%(U), -0.21%(V)
Designed to not increase worst case and reuse
Minor modification
It is proposed to adopt the modification into RExt