## Slide 1: JCTVC-N0145 AHG20: Backwards compatible enhancement of chroma format
K. Ugur, D. Bugdayci, M. M. Hannuksela
Nokia

## Slide 2: Introduction
A mechanism to enable coding of 4:4:4 video in a backwards compatible way with version 1 is proposed:
  Base layer codes 4:2:0 video with HEVC version 1 and enhancement layer codes 4:4:4 U,V colour planes separately, using the separate_colour_plane_flag functionality in HEVC.
Goals:
  Help deployment of 4:4:4 content as initially it is expected HEVC version 1 decoders would be dominating the market.
  Achieve backwards compatibility with significant coding efficiency gains over simulcast.
  Re-uses the mechanisms in HEVC, therefore small changes to the existing HEVC v1 design is needed.

## Slide 3: Proposal
4:2:0 video is coded using a legacy coder. A chroma fidelity enhancement layer is coded where:
The color planes of chroma fidelity EL are coded separately using separate_colour_plane_flag functionality.
The chroma fidelity EL does not contain any slices belonging to luminance component of the picture. During reconstruction, luminance component of base layer is used.
  The chroma components of EL can optionally be coded predictively using the base layer chroma components for improved coding efficiency.

## Slide 4: Results (1) 4:2:0 is calculated by direct subsampling
Gain over simulcast:
4:4:4: 35.4% on average
4:2:2: 42.1% on average
Loss over single layer:
4:4:4: 17.9% on average
4:2:2: 12.5% on average
 | All Intra Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -36.0% | -38.5% | -38.6%
YCbCr 4:2:2 | -41.4% | -45.4% | -45.9%
 | Random Access Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -35.1% | -34.5% | -31.2%
YCbCr 4:2:2 | -42.3% | -43.7% | -42.9%
 | Low delay B Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -35.0% | -34.0% | -29.9%
YCbCr 4:2:2 | -42.6% | -43.0% | -40.3%
 | All Intra Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 16.3% | 9.8% | 11.2%
YCbCr 4:2:2 | 13.4% | 4.9% | 4.3%
 | Random Access Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 18.6% | 17.9% | 25.8%
YCbCr 4:2:2 | 12.3% | 9.2% | 10.9%
 | Low delay B Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 18.9% | 18.2% | 27.9%
YCbCr 4:2:2 | 11.9% | 10.9% | 16.2%

## Slide 5: Results (2) 4:2:0 is calculated by first anti-aliasing filtering
Gain over simulcast:
4:4:4: 36.1% gain on average
4:2:2: 42.9% gain on average
Loss over single layer:
4:4:4: 13.8% on average
4:2:2: 8.8% on average
 | All Intra Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -36.6% | -39.1% | -39.1%
YCbCr 4:2:2 | -42.3% | -46.3% | -46.4%
 | Random Access Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -35.8% | -35.1% | -31.9%
YCbCr 4:2:2 | -43.0% | -44.5% | -44.0%
 | Low delay B Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | -35.8% | -34.7% | -30.7%
YCbCr 4:2:2 | -43.3% | -43.7% | -41.2%
 | All Intra Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 13.2% | 5.9% | 8.1%
YCbCr 4:2:2 | 9.1% | 0.3% | 0.8%
 | Random Access Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 14.4% | 13.4% | 21.5%
YCbCr 4:2:2 | 8.7% | 5.5% | 6.2%
 | Low delay B Main-tier |  | 
 | Y | U | V
YCbCr 4:4:4 | 13.9% | 12.7% | 22.7%
YCbCr 4:2:2 | 8.7% | 7.5% | 12.4%

## Slide 6: Specification text

## Slide 7: Specification text

## Slide 8: Conclusions
Introduces backwards compatible enhancement of chroma format
  Compared to simulcast significant gains are achieved (~36-43% gain on average)
  Compared to single layer small coding efficiency loss (~8.8% – 13.8% overhead on average
Benefits:
  Help deployment of 4:4:4 content as initially it is expected HEVC version 1 decoders would be dominating the market.
  Achieve backwards compatibility with significant coding efficiency gains over simulcast.
  Re-uses the mechanisms already presented in HEVC, therefore small changes to the existing HEVC v1 design is needed.

## Slide 9: Potential options
If there is interest to enable this functionality, there are three options:
1. Functionality could be included as auxiliary pictures
  Full resolution chroma components are coded as auxiliary picture layers
2. Functionality could be included in Rext
3. Functionality could be included in SHVC as a new scalability type
  Brings 4:4:4 functionality to SHVC.