## Slide 1: SCE3: Results of test 3.1 on switchable alternative inter-layer filter
Qualcomm&Samsung

## Slide 2: De-noising inter-layer filter
Applied for interpolation with phase = 0 (int-pel)
5 taps
4 bits precision
2D separable filter
{ -1,3,12,3,-1}/16
Chart: 

## Slide 3: Switchable re-sampling filter for spatial scalability
De-Noising?
SHM2.0 inter-layer filtering:
int-pel
  no filtering
fractional positions
  2D separable
  8-taps for Luma
  4 taps for Chroma
Altentaive inter-layer filtering:
int-pel
  De-noising
fractional positions
  2D separable
  6-taps for Luma
  4 taps for Chroma
no
yes

## Slide 4: Inter-layer reference picture creation
RefList
  …
  ILRef
RefList
  …
  DenoisedILRef
RefList
  …
  ILRef
  DenoisedILRef
SHM2.0
Non-switchable
PU-based
on/off
RefList
  …
  ILRef
  /DenoisedILRef
Pic-based
on/off
+1
JCTVC-M0087
JCTVC-M0273 no additional inter-layer processing
JCTVC-N0151 (modification of existing inter-layer processing)

## Slide 5: Performance Test Results
 | SNR |  | ×2 |  | ×1,5 | 
 | Luma | Chroma | Luma | Chroma | Luma | Chroma
Non-switchable | -1,3% | -0,9% | × | × | × | ×
Pic. based (0-phase) | -1,5% | -0,2% | -0,1% | 0,0% | -0,1% | 0,0%
PU based (0-phase) | -1,9% | -0,1% | -0,2% | 0,1% | -0,1% | 0,1%
Pic. based (all phases) | -1,5% | -0,2% | -0,3% | 0,0% | -0,3% | 0,0%
PU based (all phases) | -1,9% | -0,1% | -0,5% | 0,2% | -0,5% | 0,3%
AI, RA, LD-B, LD-P averaged

## Slide 6: Complexity measurement
Test | spatial |  |  |  | SNR |  |  | 
 | Memory Avg |  | Worst |  | Memory Avg |  | Worst | 
 | PU | Pic | PU | Pic | PU | Pic | PU | Pic
SHM2.0 | 108% | 157% | 145% | 160% | 98% | 160% | 200% | 218%
Non-switchable |  |  |  |  | 98% | 161% | 200% | 219%
Pic on/off | 107% | 157% | 145% | 160% | 98% | 161% | 200% | 219%
PU on/off | 106% | 218% | 145% | 204% | 97% | 220% | 200% | 237%
Pic (all phases) on/off | 107% | 161% | 145% | 160% | 98% | 161% | 200% | 219%
PU (all phases) on/off | 106% | 218% | 145% | 204% | 97% | 220% | 200% | 237%
AI, RA, LD-B, LD-P averaged
2 inter-layer references:
2 × read recBL
2 × write inter-layer Ref

## Slide 7: Complexity measurement
Test | spatial |  |  |  | SNR |  |  | 
 | Memory Avg |  | Worst |  | Memory Avg |  | Worst | 
 | PU | Pic | PU | Pic | PU | Pic | PU | Pic
SHM2.0 | 108% | 157% | 145% | 160% | 98% | 160% | 200% | 218%
Non-switchable |  |  |  |  | 98% | 161% | 200% | 219%
Pic on/off | 107% | 157% | 145% | 160% | 98% | 161% | 200% | 219%
PU on/off | 106% |  | 145% | 167% | 97% |  | 200% | 227%
Pic (all phases) on/off | 107% | 161% | 145% | 160% | 98% | 161% | 200% | 219%
PU (all phases) on/off | 106% |  | 145% | 167% | 97% |  | 200% | 227%
2 inter-layer references:
1 × read recBL
2 × write inter-layer Ref
AI, RA, LD-B, LD-P averaged

## Slide 8: Visual Quality impact
Proposed
Anchor

## Slide 9: Base Layer Rec

## Slide 10: Conclusion
De-noising inter-layer filter doesn’t introduce non-existing in inter-layer process
Positive effect on visual quality was demonstrated
No-switchable de-noising filter
  1,3% in SNR test
  ~1% memory usage in the worst case and in average
Picture based switchable de-noising filter
  1,5% in SNR test / 0,3% in spatial scalability test
  ~1% extra memory usage in the worst case and in average
PU based switchable de-noising filter
  1,9% in SNR test / 0,5% in spatial scalability test
  ~9% extra memory usage in the worst case
  Additional inter-layer reference frame