## Slide 1: HLS: Thumbnail Support In HEVC
Ce Wang, Charlie Wang, Yi-jen Chiu, Wenhao Zhang
Intel Corporation
JCTVC-N0155

## Slide 2: Motivation
  Thumbnails are required in plenty of applications to provide a preview for the video content.

## Slide 3: Motivation
  Currently, video thumbnail is usually generated at client side after full bitstream decoding.
    Content creator has no control.
    Encrypted premium contents make more issues when generating thumbnail preview.
  Scalable HEVC could be a possible solution, but requires compatible decoder.
  Therefore it is proposed to embed thumbnail pictures in regular HEVC bitstream.

## Slide 4: Proposed method
  Thumbnail pictures are coded by HEVC intra coding tools and inserted in premium bitstream.
  Three modifications are proposed to the high level syntax of HEVC.
    A NAL unit type to contain the thumbnail picture.
    A SEI message to transmit auxiliary information.
    One bit in profile_tier_level() to signal the on/off of the thumbnail video in a bit stream.
  All the modifications do not violate the conformance requirement of current HEVC.

## Slide 5: Modification 1
  A new VCL NAL unit type
    The nal_unit_type 10 is renamed to TN_N from RSV_VCL_N10.
    Syntax and semantics are same with normal intra coded VCL NAL unit.
    Non-reference VCL. No DPB impact.
    Resolution and other properties indicated by normal PPS and SPS.
    Thumbnail pictures are sparse, thus take small percent of bit rate.

## Slide 6: Modification 2
  A new SEI message – Thumbnail Picture SEI
    nal_unit_type = PREFIX_SET_NUT (39)
    payloadType=135
    payloadSize = variable
  If thumbnail pictures are inserted periodically, thumbnail_spacing_minus1 will specify the distance between thumbnails.
thumbnail_pictures_info( payloadSize ) { | Descriptor
thumbnail_present_flag | u(1)
if (thumbnail_present_flag) { | 
thumbnail_uniform_spacing_flag | u(1)
if (thumbnail_uniform_spacing_flag) | 
thumbnail_spacing_minus1 | ue(v)
} | 
} | 

## Slide 7: Modification 3
  One bit in profile_tier_level()
    Current general_reserved_zero_44bits is changed to general_thumbnail_flag + general_reserved_zero_43bits.
    If general_thumbnail_flag is equal to 1, thumbnail pictures will be inserted into current bitstream.
profile_tier_level( maxNumSubLayersMinus1 ) { | Descriptor
general_profile_space | u(2)
general_tier_flag | u(1)
general_profile_idc | u(5)
for( j = 0; j < 32; j++ ) | 
general_profile_compatibility_flag[ j ] | u(1)
general_progressive_source_flag | u(1)
general_interlaced_source_flag | u(1)
general_non_packed_constraint_flag | u(1)
general_frame_only_constraint_flag | u(1)
general_thumbnail_flag | u(1)
general_reserved_zero_43bits | u(43)
general_level_idc | u(8)
… … | 

## Slide 8: Example

## Slide 9: Conclusion
  Compatible with HEVC bitstream.
  No impact with normal conformed bitstream decoding.
  No impact on DPB.
  Premium content can be protected by DRM, while thumbnail pictures are in clear. Greatly reduce the headache for preview application.

## Slide 10: Q and A