## Slide 1: JCTVC-N0175 RCE2 Test B.3: Mirroring of Coefficients for Transform Skipping
R&D
© BBC MMXII
Rajitha Weerakkody and Marta Mrak
BBC Research and Development

## Slide 2: Transform skip
Coefficient coding design assumes usage of transforms
  Significant coefficients closer to top-left corner
Suboptimal performance when the transform is skipped (or is not performed to achieve lossless coding)
  Enabling better efficiency in those cases
    Simple rearrangements of coefficients can lead to improved compression

## Slide 3: Proposal - mirroring of coefficients
Before entropy coding residual coefficients are rearranged
  Same at the decoder after entropy decoder
Depending on the scanning order for the given block, the coefficients are rearranged relative to their original spatial positions

## Slide 4: Implementation
Mirroring implemented during transform skipping normalisation
  Before quantization, after dequantization
Decoder:
if (diag)
pResidual[j*uiStride+k]=(plCoef[(width*height)-1-width*k-j]+offset)>> transformSkipShift;
else
pResidual[j*uiStride+k]= (plCoef[k*width + j] + offset) >> transformSkipShift;

## Slide 5: Results Mirroring
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -1.6% | -1.7% | -1.9% | -1.6% | -1.7% | -1.9% | -1.5% | -1.6% | -1.7%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -2.0% | -1.9% | -1.7% | -1.9% | -1.7% | -1.6% | -1.7% | -1.4% | -1.3%
SC YUV 444 | -1.9% | -1.9% | -1.8% | -1.9% | -2.0% | -1.9% | -1.8% | -1.9% | -1.7%
RangeExt | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.1% | -1.3% | -1.5% | -1.1% | -1.3% | -1.3% |  |  | 
Class B | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
SC RGB 444 | -1.5% | -1.4% | -1.3% | -1.5% | -1.4% | -1.3% |  |  | 
SC YUV 444 | -1.4% | -1.3% | -1.1% | -1.2% | -1.3% | -1.1% |  |  | 
RangeExt | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 101% |  |  | 101% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.8% | -0.6% | -1.2% | -0.7% | -0.6% | -1.1% |  |  | 
Class B | 0.0% | 0.2% | -0.2% | 0.0% | 0.1% | -0.1% |  |  | 
SC RGB 444 | -0.6% | -0.4% | -0.4% | -0.7% | -0.5% | -0.4% |  |  | 
SC YUV 444 | -0.8% | -0.6% | -0.5% | -0.7% | -0.7% | -0.7% |  |  | 
RangeExt | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 

## Slide 6: Results Mirroring and constant context for significance map
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -2.1% | -1.9% | -2.2% | -2.1% | -2.1% | -2.3% | -2.1% | -2.1% | -2.2%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | 0.2% | 0.1%
SC RGB 444 | -2.6% | -2.4% | -2.1% | -2.5% | -2.2% | -2.0% | -2.3% | -2.0% | -1.9%
SC YUV 444 | -2.2% | -2.1% | -1.9% | -2.2% | -2.2% | -2.1% | -2.2% | -2.1% | -2.0%
RangeExt | -0.2% | -0.1% | -0.3% | -0.2% | -0.1% | -0.2% | -0.2% | 0.0% | -0.1%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 99% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.4% | -1.3% | -1.5% | -1.5% | -1.3% | -1.5% |  |  | 
Class B | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | -0.1% |  |  | 
SC RGB 444 | -1.9% | -1.6% | -1.5% | -1.9% | -1.5% | -1.4% |  |  | 
SC YUV 444 | -1.9% | -1.7% | -1.5% | -1.7% | -1.6% | -1.4% |  |  | 
RangeExt | -0.1% | -0.1% | -0.1% | -0.1% | 0.1% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -1.0% | -0.5% | -0.6% | -0.9% | -0.7% | -1.1% |  |  | 
Class B | 0.0% | 0.1% | -0.2% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -1.3% | -1.1% | -1.0% | -1.6% | -1.2% | -1.1% |  |  | 
SC YUV 444 | -0.8% | -0.6% | -0.6% | -0.9% | -0.8% | -0.8% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.1% | 0.2% | 0.2% |  |  | 
Enc Time[%] | 100% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  |  |  | 

## Slide 7: Results for lossless coding Mirroring
4x4 blocks
4x4 and 8x8 blocks
All block sizes
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -0.8% | -0.4% | -0.4%
Class B | -0.4% | -0.3% | -0.3%
SC RGB 444 | -0.2% | -0.1% | -0.2%
SC YUV 444 | -0.5% | -0.2% | -0.5%
RangeExt | -0.4% | -0.3% | -0.3%
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -0.8% | -0.4% | -0.3%
Class B | -0.4% | -0.2% | -0.2%
SC RGB 444 | -0.3% | -0.2% | -0.1%
SC YUV 444 | -0.5% | -0.2% | -0.4%
RangeExt | -0.4% | -0.2% | -0.2%
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -0.9% | -0.4% | -0.3%
Class B | -0.4% | -0.1% | -0.1%
SC RGB 444 | -0.4% | -0.2% | 0.0%
SC YUV 444 | -0.6% | -0.2% | -0.3%
RangeExt | -0.4% | -0.2% | -0.1%

## Slide 8: Results for lossless coding Mirroring and constant context for significance map
4x4 blocks
4x4 and 8x8 blocks
All block sizes
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -1.4% | -1.0% | -0.8%
Class B | -0.6% | -0.5% | -0.5%
SC RGB 444 | -0.3% | -0.3% | -0.3%
SC YUV 444 | -0.7% | -0.7% | -0.6%
RangeExt | -0.5% | -0.5% | -0.5%
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -1.4% | -0.9% | -0.7%
Class B | -0.5% | -0.3% | -0.3%
SC RGB 444 | -0.3% | -0.1% | -0.2%
SC YUV 444 | -0.7% | -0.5% | -0.6%
RangeExt | -0.5% | -0.3% | -0.3%
 | All Intra Main | Random Access Main | Low delay B Main
Class F | -1.5% | -0.9% | -0.6%
Class B | -0.6% | -0.2% | -0.2%
SC RGB 444 | -0.3% | -0.2% | 0.1%
SC YUV 444 | -0.8% | -0.5% | -0.5%
RangeExt | -0.5% | -0.3% | -0.2%

## Slide 9: Conclusions
Mirroring of coefficients is applied on blocks where transform is skipped
Consistent coding gains for all test points that benefit from transform skip
  For screen content for all configurations
  For all content types for lossless coding
Further studies reporting interaction of mirroring with other tools from this CE, particularly interaction of mirroring and prediction of residual:
  JCTVC-N0207
  JCTVC-N0353