## Slide 1
Non-RCE2: On sample adaptive intra
prediction for oblique modes in lossless coding
JCTVC-N0176
Haoming Chen, Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation and Prior Work
Sample Adaptive Prediction (SAP) from JCTVC-M0056 for horizontal and vertical modes was adopted in HEVC Range Extensions Working Draft in April 2013 JCTVC meeting.
It was asserted that SAP for other modes (oblique modes) is not fully parallel.
Also, SAP on oblique modes was actually providing less gains for SAP on H+V modes for screen content.
  Propose to solve these 2 problems in this proposal

## Slide 3: Overview of SAP in HM10.1+RExt3.0
Current SAP for Horizontal and Vertical Modes
Proposal: We propose SAP for 7 additional oblique modes
  3 strictly diagonal + 4 pseudo-diagonal
  Fully parallel at the encoder and decoder.
2.1% bit-rate reduction for Screen Content Coding RGB; 1.8 % for Screen Content YUV; 0.8 % for Class F

## Slide 4: Proposed SAP: (a) 3 diagonal modes
  Fully parallel at both the encoder and decoder.
  Additional number of operations even less than Horizontal and Vertical SAP in HM.

## Slide 5: Proposed SAP (b) 4 pseudo diagonal modes
  Fully parallel at both the encoder and decoder.
  Additional number of operations even less than Horizontal and Vertical SAP in HM.

## Slide 6: Experiments
 | All PU sizes | Only 4×4 | 4×4 and 8×8
3 diagonal modes | Test 1 | Test 3 | Test 4
All 7 modes | Test 2 | Test 5 | Test 6
Thanks to Texas Instruments for cross-checking the results
in JCTVC-N0319.
  Anchor : HM10.1 + RExt 3.0 in Lossless setting according to stipulated test conditions in RCE 2

## Slide 7: Results (on all block sizes)
Test 1: SAP for 3 diagonal modes
Test 2: SAP for 7 angular modes

## Slide 8: Comparison across Maximum Block Size
3 diagonal modes with different size limitation
All 7 angular modes with different size limitation
SAP for 4x4 and 8x8 blocks provide most of the gains.

## Slide 9: Results for 3 diagonal modes
Test 3: SAP for 3 diagonal modes on 4×4
Test 4: SAP for 3 diagonal modes on 4×4 and 8×8

## Slide 10: Results for 7 angular modes
Test 5: SAP for 7 angular modes on 4×4
Test 6: SAP for 7 angular modes on 4x4 and 8×8

## Slide 11: Complexity for parallel decoding
 | 4×4 |  | 8×8 | 
 | Additional Complexity | Additions/Sample | Additional Complexity | Additions/Sample
Strictly Diagonal Modes | 14 adds | 0.875 | 140 adds | 2.1875
Pseudo-Diagonal Modes | 6 adds | 0.375 | 84 adds | 1.3125
H or V mode already in HEVC-Range Extensions software | 24 adds | 1.5 | 224 adds | 3.5
Additional complexity for SAP for oblique modes is even less than complexity of SAP for horizontal and vertical modes.

## Slide 12: Conclusions
Proposed SAP for 7 oblique modes for lossless coding.
SAP for these 7 modes is fully parallel at both the encoder and decoder
Gains of 2.1% for screen content RGB; 1.8 % for screen content YUV; and 0.8 % for Class F.
Recommend to adopt proposed SAP for 7 oblique modes in HEVC-Range Extensions WD/CD at PU sizes 4x4 and 8x8.

## Slide 13
Back-Up Slides

## Slide 14: Results from M-0056 for SAP
Interestingly, gains for Screen Content were less when SAP was applied for all modes as compared to SAP only for H+V mode.
Reason: Bilinear interpolation of pixels was being performed for oblique modes, which actually degrades the prediction.
Solution for that in JCTVC-N0183.
SAP for All Modes | All Intra Main
 | Bit-rate saving
Class F | -11.6%
Class B | -5.8%
SC(GBR) | -10.4%
RangeExt | -4.1%
SAP for H+V Mode | All Intra Main
 | Bit-rate saving
Class F | -10.1%
Class B | -4.4%
SC(GBR) | -12.4%
RangeExt | -2.9%