## Slide 1: JCTVC-N0180 Color Mapping SEI message
P.Bordes
14th JCT-VC Meeting: Vienna, July 25- August 2nd, 2013

## Slide 2: Color Mapping SEI message
  Context
    Several color formats (primaries) can be signaled in HEVC syntax (VUI, SEI-tone-mapping)
    Some end-devices may not support all formats because of:
      Limited rendering capability
      New color formats (ex: BT.2020)
      Pointless w.r.t. device/application
      Unspecified color format
  Proposition
    To support color mapping post-processing on reconstructed pictures
    The color mapping function is coded using a 3D Color LUT

## Slide 3: Color Mapping SEI message
new
future
unspecified

## Slide 4: Color Mapping SEI message
  The Color LUT allows mapping the reconstructed pictures to a supported color format
  Advantages
    To increase color adaptability (end-devices not supporting all color format)
    To preserve colorist intent when converting color graded content
    To provide color mapping function tailored to particular applications
    Color LUTs is a common and universal color mapping format

## Slide 5: Color Mapping SEI message syntax
nuh_layer_id identifies the layer of the reconstructed pictures to which the 3D CLUT should be applied.
color_map_id, color_map_cancel_flag, color_map_repetition_period semantic is same as tone_map_id, tone_map_cancel_flag and tone_map_repetition_period defined in SEI tone mapping (Annex D).
colour_map_video_signal_type_present_flag, colour_map_video_format, colour_map_video_full_range_flag, colour_map_description_present_flag, colour_map_primaries, colour_map_transfer_characteristics, colour_map_matrix_coeffs semantic is the same as the semantic of the syntax elements video_signal_type_present_flag, video_format, video_full_range_flag, colour_description_present_flag, colour_primaries, transfer_characteristics, matrix_coeffs in VUI (specified in Annex E) respectively. These syntax elements describe the remapped output decoded pictures video signal characteristics.
bit_depth_lut_minus8 + 8 specifies the bit depth of the 3D LUT samples.
nbp_code indicates the 3D LUT size nbp as listed in Table 2 for the given value of nbp_code (nbp=2(nbp_code-1)+1 ).
colour_mapping_info( payloadSize ) { | Descriptor
colour_map_id | ue(v)
colour_map_cancel_flag | u(1)
if( !colour_map_cancel_flag ) { | 
colour_map_repetition_period | ue(v)
colour_map_video_signal_type_present_flag | u(1)
if(colour_map_video_signal_type_present_flag ) { | 
colour_map_video_format | u(3)
colour_map_video_full_range_flag | u(1)
colour_map_description_present_flag | u(1)
if (colour_map_description_present_flag) { | 
colour_map_primaries | u(8)
colour_map_transfer_characteristics | u(8)
colour_map_matrix_coeffs | u(8)
} | 
} | 
3D_ LUT_ colour_data ( ) | 
} | 
} | 
3D_ LUT_ colour_data ( ) { | Descriptor
bit_depth_lut_minus8 | u(4)
nbp_code | u(3)
coding_octant(0, 0, 0, 0) | 
} | 

## Slide 6: Color LUT coding syntax
Octree based coding using DPCM coding of YUV color vertices
  Unused (or less used) 3D color space regions are encoded with coarsely lattice size
  Each color component of a vertex is predicted with previously encoded color components of neighboring parent octant vertices
encoded_vertex_flag[i] indicates whether the residual components values (resY[i],resU[i], resV[i]) are encoded or all inferred to be zero.
split_octant_flag specifies whether an octant is split into octants with half horizontal and vertical size. The values (y,u,v) specify the location of the first vertex in the 3D LUT.
coding_octant ( layer_id, y,u,v) { | Descriptor
for( i = 0; i < 8 ; i++ ) { | 
encoded_vertex_flag[i] | u(1)
if ( encoded_vertex_flag[i] ) { | 
resY[i] | ue(v)
resU[i] | ue(v)
resV[i] | ue(v)
} | 
} | 
split_octant_flag | u(1)
if ( split_octant_flag ) { | 
for( i = 0; i < 8 ; i++ ) { | 
coding_octant ( layer_id+1, y+dy[i],u+du[i],v+dv[i]) | 
} | 
} | 
} | 

## Slide 7: Example of use of the Color Mapping SEI message
We provide an example of software application based on a modified SHM2.0 encoder and decoder
Encoder
Encoder allows to load one 3D color LUT per layer and to encode one Color Mapping SEI message per layer. Additional config parameters:
    SeiColorLut0 : 1
    SeiColorLutFile0 : lutFileBL.txt
    SeiColorLut1 : 1
    SeiColorLutFile1 : lutFileEL.txt
    TAppEncoderStatic –c cfg –seiColorLut0 1 –SeiColorLutFile0 lutBL.txt –seiColorLut1 1 –SeiColorLutFile1 lutEL.txt
Decoder
The Decoder receiving a Color Mapping SEI message will post-process the output reconstructed frames (output file) of the corresponding layer with the corresponding 3D color LUT. The reference frames in the DPB remain unchanged.