## Slide 1: Non-RCE2: Rice Parameter Initialization JCTVC-N0181
Marta Karczewicz, Joel Sole, Rajan Joshi

## Slide 2: Introduction
Prediction error of screen content and lossless coding has different statistics than lossy coded natural content
  This can be exploited at the residue coding by improving the Rice parameter (cRiceParam) initialization
In HEVC, the Rice parameter is reset to 0 at the beginning of each 4×4 sub-block
Proposal: Modified Rice parameter reset at the beginning of each 4×4

## Slide 3: Proposed Rice Parameter Initialization
For each 4×4 sub-block, the Rice parameter is initialized by
cRiceParam = g_golombTab[ min( statCoeff[ sbType ], 31 )
  where
  Table g_golombTab size is 32
  statCoeff is an 8-bit variable kept for each of the 4 sub-block types
  sbType = 2*isLuma + (iSubSet>0)
  and updated using the value of the first coded coeff_abs_level_remaining of the 4×4 sub-block by
  statCoeff[sbType] += (level == statCoeff) ? 0 : ( ( level < statCoeff ) ? -1 : 1)

## Slide 4: Variants
The proposed initialization combined with the fast update methods in JCTVC-N0101
  They remove one condition in the coding loop
  cRiceParam = Min( cLastRice + ( AbsLevel >> ( 2 + cLastRice ) ), 4 )
The proposed initialization applied only to transform skip blocks

## Slide 5: BD-rate for lossless
HEVC update
Fast update
Max Rice 4 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.9% | -0.1% | -10.4% | -7.7% | -3.1%
RA | -1.0% | 0.0% | -8.9% | -7.1% | -2.4%
LB | -0.6% | 0.0% | -8.1% | -7.3% | -2.4%
Max Rice 5 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -2.1% | -0.1% | -12.5% | -8.5% | -3.4%
RA | -1.1% | 0.0% | -10.6% | -7.6% | -2.5%
LB | -0.7% | 0.0% | -9.7% | -8.1% | -2.5%
Max Rice 4 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -1.8% | -0.2% | -10.2% | -7.6% | -3.4%
RA | -1.0% | 0.0% | -8.9% | -6.9% | -2.7%
LB | -0.6% | 0.0% | -8.0% | -7.3% | -2.7%
Max Rice 5 | Class F | Class B | SC RGB444 | SC YUV444 | RangeExt
AI | -2.1% | -0.1% | -12.6% | -8.6% | -3.6%
RA | -1.1% | 0.0% | -10.5% | -7.8% | -2.8%
LB | -0.6% | 0.0% | -9.9% | -8.2% | -2.8%

## Slide 6: BD-rate for lossy
Case: Max Rice 4 – Always applied (transform & transform skip)
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.6% | -0.8% | -0.7% | -1.0% | -1.1% | -1.1% | -1.4% | -1.5% | -1.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.5% | -3.4% | -3.5% | -5.7% | -5.7% | -5.7% | -8.2% | -8.5% | -8.5%
SC YUV 444 | -0.7% | -0.7% | -0.6% | -1.5% | -1.5% | -1.4% | -2.9% | -2.9% | -3.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 101% |  |  | 102% |  |  | 103% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.6% | -0.6% | -0.7% | -0.8% | -0.8% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -3.0% | -3.0% | -3.0% | -5.0% | -4.9% | -4.9% |  |  | 
SC YUV 444 | -0.4% | -0.4% | -0.3% | -1.1% | -1.1% | -1.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 99% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.3% | -0.2% | 0.1% | -0.5% | -0.4% | -0.5% |  |  | 
Class B | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 0.1% |  |  | 
SC RGB 444 | -2.0% | -2.0% | -2.0% | -4.6% | -4.5% | -4.7% |  |  | 
SC YUV 444 | -0.2% | -0.2% | -0.2% | -0.9% | -0.9% | -0.9% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 103% |  |  | 103% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 100% |  |  |  |  | 

## Slide 7: BD-rate for lossy
Case: Max Rice 4 – Fast update – Always applied (transform & transform skip)
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.7% | -0.9% | -0.8% | -1.2% | -1.3% | -1.2% | -1.6% | -1.7% | -1.7%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.6% | -3.6% | -3.6% | -6.0% | -5.9% | -5.9% | -8.3% | -8.6% | -8.6%
SC YUV 444 | -0.7% | -0.8% | -0.7% | -1.6% | -1.6% | -1.5% | -3.0% | -3.1% | -3.2%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 101% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.5% | -0.5% | -0.8% | -0.8% | -0.8% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -3.1% | -3.1% | -3.1% | -5.1% | -5.0% | -5.0% |  |  | 
SC YUV 444 | -0.6% | -0.6% | -0.5% | -1.1% | -1.1% | -1.0% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 99% |  |  | 100% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | 0.1% | -0.6% | -0.6% | -0.3% | -0.7% |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% |  |  | 
SC RGB 444 | -2.7% | -2.7% | -2.7% | -5.1% | -5.1% | -5.2% |  |  | 
SC YUV 444 | -0.4% | -0.3% | -0.3% | -1.0% | -0.9% | -0.9% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 102% |  |  |  |  | 
Dec Time[%] | 102% |  |  | 101% |  |  |  |  | 

## Slide 8: BD-rate for lossy
Case: Max Rice 5 – Fast update – Always applied (transform & transform skip)
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.7% | -0.9% | -0.8% | -1.1% | -1.2% | -1.2% | -1.6% | -1.6% | -1.6%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.6% | -3.5% | -3.6% | -5.9% | -5.8% | -5.8% | -8.4% | -8.8% | -8.8%
SC YUV 444 | -0.7% | -0.8% | -0.7% | -1.6% | -1.6% | -1.5% | -3.0% | -3.1% | -3.2%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 102% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 98% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | -0.5% | -0.6% | -0.8% | -0.8% | -0.8% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% |  |  | 
SC RGB 444 | -3.1% | -3.1% | -3.1% | -5.0% | -4.9% | -5.0% |  |  | 
SC YUV 444 | -0.7% | -0.7% | -0.6% | -1.2% | -1.2% | -1.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 98% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 97% |  |  | 94% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | 0.0% | -0.6% | -0.6% | -0.4% | -0.8% |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -2.8% | -2.8% | -2.8% | -5.1% | -5.0% | -5.2% |  |  | 
SC YUV 444 | -0.5% | -0.4% | -0.4% | -1.2% | -1.2% | -1.2% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1% |  |  | 
Enc Time[%] | 98% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 96% |  |  | 95% |  |  |  |  | 

## Slide 9: BD-rate for lossy
Case: Max Rice 5 – Fast update – Applied to transform skip only
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.8% | -1.0% | -1.0% | -1.3% | -1.4% | -1.4% | -1.8% | -1.9% | -1.9%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
SC RGB 444 | -3.7% | -3.7% | -3.7% | -6.0% | -6.0% | -5.9% | -8.6% | -9.0% | -8.9%
SC YUV 444 | -0.7% | -0.8% | -0.7% | -1.7% | -1.6% | -1.6% | -3.1% | -3.1% | -3.2%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 102% |  |  | 102% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | -0.7% | -0.7% | -0.9% | -1.0% | -1.0% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -3.1% | -3.1% | -3.1% | -5.1% | -5.0% | -5.1% |  |  | 
SC YUV 444 | -0.5% | -0.5% | -0.5% | -1.3% | -1.2% | -1.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 101% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.5% | -0.6% | -0.9% | -0.7% | -0.7% | -1.0% |  |  | 
Class B | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -2.6% | -2.6% | -2.6% | -5.0% | -4.9% | -5.1% |  |  | 
SC YUV 444 | -0.6% | -0.6% | -0.6% | -1.2% | -1.2% | -1.2% |  |  | 
RangeExt | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 105% |  |  | 105% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 

## Slide 10: Conclusions
Rice parameter initialization method is presented and tested for
  max Rice parameter 4 and 5,
  applied to all transforms and to transform skip only,
  and also, in combination with Rice parameter fast update
Provides large BD-rate gains for
  screen content in the lossy setting, and
  screen content and natural content in the lossless setting

## Slide 11: Non-RCE2: Rice Parameter Initialization JCTVC-N0181
Marta Karczewicz, Joel Sole, Rajan Joshi

## Slide 12: BD-rate for lossy
Case: Max Rice 5 – Always applied (transform & transform skip)
 | All Intra RExt Main-tier |  |  | All Intra RExt High-tier |  |  | All Intra RExt Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class F | -0.6% | -0.8% | -0.7% | -1.0% | -1.1% | -1.1% | -1.4% | -1.5% | -1.5%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
SC RGB 444 | -3.5% | -3.4% | -3.5% | -5.7% | -5.7% | -5.7% | -8.3% | -8.7% | -8.7%
SC YUV 444 | -0.7% | -0.7% | -0.6% | -1.5% | -1.5% | -1.4% | -2.9% | -2.9% | -3.1%
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
 | Random Access RExt Main-tier |  |  | Random Access RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.6% | -0.6% | -0.7% | -0.8% | -0.8% |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% |  |  | 
SC RGB 444 | -3.0% | -3.0% | -3.0% | -5.1% | -4.9% | -5.0% |  |  | 
SC YUV 444 | -0.4% | -0.4% | -0.3% | -1.2% | -1.2% | -1.1% |  |  | 
RangeExt | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 98% |  |  | 99% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 
 | Low delay B RExt Main-tier |  |  | Low delay B RExt High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class F | -0.4% | -0.2% | 0.3% | -0.5% | -0.4% | -0.4% |  |  | 
Class B | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% |  |  | 
SC RGB 444 | -2.1% | -2.0% | -2.1% | -4.7% | -4.7% | -4.8% |  |  | 
SC YUV 444 | -0.3% | -0.3% | -0.3% | -1.2% | -1.2% | -1.2% |  |  | 
RangeExt | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  |