## Slide 1: JCTVC-N0185 On low-delay checking process for SHVC
InterDigital Communications, Inc.
HiSilicon Technologies Co., Ltd.
14th JCT-VC meeting, July 2013
Notes: In this proposal, we have proposed several coding tools to improve the temporal motion vector prediction process of reference index based SHVC.

## Slide 2: Summary
Current TMVP derivation process in SHM-2.0
  Inter-layer prediction (ILP) picture could be used as the collocated picture.
  For bi-predicted PU, the MV of the collocated PU to predict the target MV is determined based on the low-delay flag
  Low-delay flag is set at slice-level according to the POCs of the reference pictures of the current picture
  If low-delay flag is true, the collocated MV is obtained from the same reference list of the target MV
Proposed method
  Propose to set the low-delay flag additionally depending on if ILP picture is used as collocated picture
    If ILP is used as the collocated picture, low-delay flag is set to true
    Otherwise, the default low-delay checking process is applied
  The proposed modification is a slice-level change
Notes: In the current TMVP derivation process of SHM-2.0, inter-layer prediction picture is used as the collocated picture.
If one EL PU is bi-predicted, the selection of collocated MV to predict the target MV is determined based on the low-delay flag.
This low-delay flag is set at the slice-level, according the POCs of the reference pictures of the current picture.
If low-delay flag is true, the collocated MV from the same reference picture list is used for TMVP; otherwise, the collocated MV from the different reference picture list of the target MV is selected.
Given that the EL MV and the collocated BL have a strong correlation in the same reference list, in this contribution, it is proposed to set the low-delay flag additionally based on the ILP picture for EL TMVP.
More specifically, if the ILP picture is used as the collocated, the low-delay flag is always set to true; otherwise, the default low-delay checking process is applied.
As the low-delay is changed at the slice-level, the proposed modification is a slice-level change.

## Slide 3: Simulation Results
SHM 2.0 refIdx is used as anchor
Only the RA performance is influenced
Average BD-rate savings: 0.4%, 0.4% and 0.5% for 2x, 1.5x and SNR scalability respectively
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.3% | -0.5% | -0.5% |  |  |  | -0.4% | -0.8% | -0.9%
Class B | -0.4% | -0.7% | -0.7% | -0.4% | -0.7% | -0.7% | -0.5% | -1.0% | -1.1%
Overall (Test vs Ref) | -0.4% | -0.6% | -0.7% | -0.4% | -0.7% | -0.7% | -0.5% | -0.9% | -1.0%
Overall (Test vs single layer) | 18.7% | 32.4% | 31.1% | 15.7% | 28.0% | 28.2% | 13.9% | 30.9% | 32.8%
Overall (Ref vs single layer) | 19.2% | 33.3% | 32.0% | 16.2% | 28.8% | 29.1% | 14.4% | 32.1% | 34.1%
EL only (Test vs Ref) | -0.6% | -0.9% | -0.9% | -0.6% | -0.9% | -1.0% | -0.7% | -1.2% | -1.3%
We thank Sharp for cross checking (JCTVC-N0260)
Notes: 1. For the experiment, we have used the results of SHM-2.0 as the anchor.
2. As low-delay can only affect the TMVP process when the two reference picture lists of the current picture are different, the proposed change can only affect RA results.

## Slide 4: Conclusion
Modify the low-delay checking process of the EL coding
The proposed modification is a slice-level change
Performance improvement of RA configuration: 0.4%, 0.4% and 0.5% BD-rate savings for 2x, 1.5x and SNR scalability.
Recommend to adopt into SHVC test model