## Slide 1: JCTVC-N0186 Single-loop decoding based SNR scalability for SHVC
Xiaoyu Xiu, Yan Ye, Yuwen He, Yong He
InterDigital Communications, Inc.
14th JCT-VC meeting, July 2013
Notes: In this proposal, we have proposed several coding tools to improve the temporal motion vector prediction process of reference index based SHVC.

## Slide 2: Summary
Current SHVC design for SNR scalability
  Multi-loop decoding based scheme using reconstructed BL picture for inter-layer prediction (ILP)
  Motion compensation (MC) and loop filters have to be applied to BL and EL
  Complexity: both computational complexity and memory access are two times as that of single-layer HEVC
Proposed method for SNR scalability
  Single-loop decoding based scheme
  Hybrid inter-layer prediction (H-ILP) picture
    Using BL motion information to perform MC on EL temporal reference picture
    Adding BL residue to motion compensated EL signal
  Improved decoding complexity and memory access
Notes: The current SHVC design is a multi-loop based solution which uses reconstructed BL pictures for inter-layer prediction.
As the reconstructed BL picture is used for EL coding, both the BL motion compensation and loop filters have to be executed in order to decode EL.
Correspondingly, for SNR scalability, the computational complexity and memory access are two times as that of single-layer HEVC.
In order to reduce the decoding complexity, in this contribution, we propose to use single-loop decoding scheme for SNR scalability.
The proposed single-loop decoding scheme is built based on a new type of inter-layer reference picture which is generated by using the BL motion information and the texture of EL reference pictures. In addition, BL residue is also used to enhance the efficiency of inter-layer prediction.
As both BL and EL information are used for the generation of the proposed inter-layer reference picture, we call this inter-layer reference picture type as hybrid inter-layer reference picture.

## Slide 3: Hybrid Inter-layer Prediction Picture
The BL block is uni-predicted
The BL block is bi-predicted
The BL block is intra-predicted
  The H-ILP block is copied from the samples of the BL block
  Constrained intra prediction
  The BL intra samples are obtained prior to the loop filters (de-blocking filter and SAO)
Notes: This slide shows the generation process of hybrid inter-layer reference picture. And, the main idea of the proposed method is to shift the BL motion compensation process to EL. More specifically, to generate one block in the H-ILP picture, we firstly use the MV of the collocated BL block to find the best matching block in the EL reference pictures. And then, the residue of the collocated BL block is added to the motion compensated EL block to compensate for the quantization error of BL.
Those two equations illustrate the case where the collocated BL block is uni- and bi-predicted.
In case the collocated BL block is intra-predicted, the corresponding H-ILP block will be directly copied from the intra-coded block. However, in order to satisfy the single-loop decoding requirement, two constraints are applied. Firstly, constrained intra prediction is used for BL intra prediction such that inter-coded BL pixels are not used to predict BL intra-coded pixels. Secondly, the BL intra samples that are used to generate H-ILP block are obtained prior to the BL de-blocking and SAO process.

## Slide 4: Single-loop Decoding Scheme
The conventional ILP picture is replaced by the H-ILP picture
BL motion information, BL residue and the texture of EL temporal reference pictures are needed to generate H-ILP picture
No need to perform MC and loop filters to reconstruct BL pictures for EL inter-prediction
No low-level changes to single-layer HEVC decoder design
Notes: 1. Given the proposed H-ILP picture, the single-loop decoding scheme is achieved by replacing the conventional ILP picture by the H-ILP picture in the EL DPB.
2. As both BL motion information and BL residue information that are needed to generate H-ILP picture can be obtained without reconstructing BL picture, there is no need to perform BL motion compensation and loop filters in order to decode EL. This makes the proposed scheme completely satisfy the single-loop decoding requirement.
3. Moreover, as H-ILP picture is used as one reference picture of EL coding, the proposed scheme does not contain any low-level changes to singe-layer HEVC.

## Slide 5: Constraint on EL inter-prediction
EL inter-prediction using H-ILP block
  One EL bi-predicted PU could be predicted from the combination of one H-ILP block and one EL block
  The H-ILP block could be either uni-predicted or bi-predicted
  If the H-ILP block is bi-predicted, three MC operations are required to generate the EL bi-predicted PU
Proposed constraint
  No combined prediction between H-ILP block and EL temporal block when H-ILP block itself is bi-predicted
  Two MC operations are needed at most for decoding one EL PU, which is equal to single-layer HEVC
Notes: As both EL temporal reference pictures and H-ILP picture are used as EL reference picture, one EL PU could be bi-predicted from the combination of one EL temporal block and one H-ILP block.
One the other hand, the H-ILP block itself could be bi-predicted using the BL motion.
In this case, there are three MC operations to generate the EL block, where the two MCs are used to generate H-ILP block and the third one is used to combine EL prediction and H-ILP prediction.
This number is larger than the maximum two MC operations in single-layer HEVC.
In order to make the complexity of single-loop decoding equals to single-layer HEVC, one inter-layer prediction constraint is proposed to disable the combination between H-ILP block and EL temporal block when H-ILP block is bi-predicted.

## Slide 6: Coding Performance
SHM 2.0 refIdx with constrained intra prediction enabled is used as anchor
The EL inter-prediction constraint is disabled
Decoding time is reduced by 25% on average
Average BD-rate increase: 1.3% and 1.5% for RA and LDB respectively
The scheme does not change the BL decoding, with introducing drift error
We thank RWTH Aachen University for cross checking (JCTVC-N203)
 | RA HEVC SNR |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V
Class A | 1.4% | -8.6% | -9.3% | 1.9% | -8.0% | -9.0%
Class B | 1.3% | -7.4% | -10.3% | 1.4% | -7.0% | -9.8%
Overall (Test vs Ref) | 1.3% | -7.7% | -10.0% | 1.5% | -7.3% | -9.6%
Overall (Test vs single layer) | 17.2% | 22.5% | 21.0% | 27.9% | 26.8% | 27.6%
Overall (Ref vs single layer) | 15.8% | 33.7% | 35.8% | 26.0% | 37.5% | 42.6%
EL only (Test vs Ref) | 2.6% | -7.4% | -9.9% | 3.1% | -6.4% | -8.9%
Enc Time[%] | 90.3% |  |  | 89.1% |  | 
Dec Time[%] | 74.0% |  |  | 77.2% |  | 
BL Match | Matched |  |  | Matched |  | 
Notes: We have used the results of SHM-2.0 with constrained intra prediction enabled as the anchor for multi-loop decoding.
The results below are for the single-loop decoding scheme when the EL inter-layer prediction constraint is not applied.
Compared to multi-loop results, the single-loop decoding can improve decoding complexity by reducing the decoding time by 25%.
One the other hand, the single-loop decoding increase the BD-rate by 1.3% and 1.5% for RA and LDB configurations respectively, compared to multi-loop solution.
In the proposed single-loop decoding, the BL bi-stream is independently decodable with introducing any drift error.

## Slide 7: Coding Performance
SHM 2.0 refIdx with constrained intra prediction enabled is used as anchor
The EL inter-prediction constraint is enabled
Decoding time is reduced by 28% on average
Average BD-rate increase: 2.2% and 3.5% for RA and LDB respectively
 | RA HEVC SNR |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V
Class A | 1.8% | -8.0% | -8.8% | 3.3% | -6.4% | -7.6%
Class B | 2.3% | -6.5% | -9.5% | 3.6% | -4.7% | -7.4%
Overall (Test vs Ref) | 2.2% | -7.0% | -9.3% | 3.5% | -5.2% | -7.5%
Overall (Test vs single layer) | 18.2% | 23.5% | 22.0% | 30.4% | 29.6% | 30.5%
Overall (Ref vs single layer) | 15.8% | 33.7% | 35.8% | 26.0% | 37.5% | 42.6%
EL only (Test vs Ref) | 3.6% | -6.4% | -9.0% | 6.1% | -3.4% | -5.9%
Enc Time[%] | 95.8% |  |  | 94.5% |  | 
Dec Time[%] | 71.9% |  |  | 73.9% |  | 
BL Match | Matched |  |  | Matched |  | 
We thank RWTH Aachen University for cross checking (JCTVC-N203)
Notes: 1.The results in this table show the performance of single-loop decoding when the EL inter-layer prediction constraint is enabled.
2. Firstly, the prediction constraint can further reduce the decoding complexity, which can 28% decoding time reduction compared to multi-loop decoding.
3, And, the corresponding BD-rate increase is 2.2% and 3.5% for RA and LDB.

## Slide 8: Complexity Assessment of Average Memory Access
Complexity assessment methodology in AHG17 is applied
The average access of SHM2.0 multi-loop is used as anchor
Single-loop decoding can reduce the average memory access by 36%, 33% and 32% respectively
The EL inter-prediction constraint can provide additional 4% memory access saving
Tested method | Block-based implementation |  | 
 | Pure | DDR2 | DDR3
SHM2.0 single-loop decoding | 64% | 67% | 68%
SHM2.0 single-loop decoding with inter-prediction constraint | 60% | 63% | 63%
We thank RWTH Aachen University for cross checking (JCTVC-N203)
Notes: The table here shows the comparison of real memory access between the single-loop decoding and the multi-loop decoding when running the decoder.
From the number, we can see single-loop decoding can reduce the average memory access by 34% compared to multi-loop decoding.
In addition, the EL inter-prediction constraint could provide another 3% memory access saving.

## Slide 9: Complexity Assessment in Worst Case
Complexity assessment methodology in AHG17 is applied
8x2 memory pattern is used
The worst case of single-layer HEVC is used as the anchor
Tested method | Block-based implementation
SHM2.0 multi-loop decoding | 200%
SHM2.0 single-loop decoding | 193%
SHM2.0 single-loop decoding with inter-prediction constraint | 100%
We thank RWTH Aachen University for cross checking (JCTVC-N203)
Notes: In addition to the decoding time, we also applied the complexity assessment methodology from AHG 17 to evaluate the complexity. The table below shows the worst case memory access of different methods, and the worst case of single-layer HEVC is used as anchor.
Firstly, we can the worst case memory access of multi-loop decoding is two times that of single-layer HEVC.
Secondly, the single-loop result is slightly better than multi-loop, which is however close to 200% of single-layer HEVC, given that the memory access expensive combined prediction between H-ILP block and EL temporal block is enabled.
The problem could be resolved by applying the EL prediction constraint by which the worst case memory access of single-loop decoding could be equal to single-layer HEVC.

## Slide 10: Conclusion
Single-loop decoding scheme for SNR scalability of SHVC
No low-level changes to HEVC decoder design, compatible with refIdx framework
Performance impact
  Significantly reduce the decoding complexity and memory access
  Comparable BD-rate performance to SHM2.0 multi-loop
Recommendations
  Establish CE to further study the single-decoding of SNR scalability
  The current implementation is a true single-decoding implementation, recommend the software as the basis in AHG
Notes: For the conclusion, in this contribution, we have proposed one single-loop decoding scheme for SNR scalability.
The proposed method does not have any low-level changes to single-layer HEVC.
For the performance, the proposed single-loop decoding can significantly reduce the decoding complexity and memory access, while achieve a comparable BD-rate performance to multi-loop decoding.
For the recommendations, firstly, it is recommended to have a core experiment to further study the single-loop decoding for the SNR scalability. Secondly, as our current software is a real single-loop decoding software where the EL can be decoded with the reconstruction of the BL, it is recommended to use the current software in the AHG