## Slide 1: JCTVC-N0187 Performance investigation on using H-ILP picture for SHVC
Xiaoyu Xiu, Yan Ye, Yuwen He, Yong He
InterDigital Communications, Inc.
14th JCT-VC meeting, July 2013
Notes: In this proposal, we have proposed several coding tools to improve the temporal motion vector prediction process of reference index based SHVC.

## Slide 2: Summary
Current SHVC design
  Multi-loop decoding based scheme using reconstructed BL picture for inter-layer prediction (ILP)
Hybrid inter-layer prediction (H-ILP) picture
  Using BL motion information to perform MC on EL temporal reference picture
  Adding BL residue to motion compensated EL signal
H-ILP based multi-loop decoding scheme
  Using both ILP picture and H-ILP picture for EL inter-layer prediction
Notes: The current SHVC design is a multi-loop decoding based scheme which use the reconstructed BL for the inter-layer prediction.
In our previous contribution (186), we have proposed hybrid inter-layer reference picture for the single-loop decoding of SHVC. The hybrid inter-layer reference picture is generated by using the BL motion information and the texture information of the EL temporal reference pictures. In addition, the BL residue is also applied to increase the efficiency of inter-layer pediction.
In this contribution, we have investigate the performance of H-ILP based multi-loop decoding by using both conventional ILP picture and H-ILP picture for EL prediction.

## Slide 3: Hybrid Inter-layer Prediction Picture
The BL block is uni-predicted
The BL block is bi-predicted
Bilinear filter is applied to up-sample the BL residue at fractional pixel positions
BL MVs are scaled according to spatial scalability ratio
Notes: The figure in this page shows the generation process of H-ILP picture. And in details, for each block in the H-ILP picture, the corresponding collocated base-layer is located. Then, the motion information of the collocated BL block is used to find the best matching block in the EL temporal reference picture. In addition, the residue information of BL is added to the motion compensated EL signal to compensate for the quantization error of BL.
The original H-ILP picture idea is only proposed for the SNR scalability. In order to extend the idea to the spatial scalability case, the motion vector scaling and BL residue up-sampling processes are also added to generate the H-ILP picture if the BL and EL have different resolutions.
In order to control the complexity of H-ILP picture, bilinear filter is used to up-sample BL residue at fractional pixels.

## Slide 4: EL Reference Picture Placement
For EL B-Slice, ILP picture and H-ILP picture are placed at the end of reference picture lists L0 and L1 respectively
For EL P-Slice, H-ILP picture is placed after EL temporal reference pictures and ILP picture
Notes: For the EL prediction, the investigated multi-loop decoding scheme uses both ILP and H-ILP pictures in the reference list of EL.
And specifically, for EL B-Slice, the ILP picture and H-ILP picture are placed at the end of reference list L0 and L1 respectively. For EL P-Slice, the H-ILP picture is placed after the EL temporal reference picture and the ILP picture.

## Slide 5: Coding Performance
SHM 2.0 refIdx is used as anchor
Average BD-rate saving: 2.1%, 2.4% and 1.6% for RA, LDB and LDP respectively
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.1% | -4.8% | -4.8% |  |  |  | -1.9% | -5.5% | -6.0%
Class B | -1.8% | -4.1% | -4.7% | -2.2% | -5.2% | -5.8% | -2.0% | -5.2% | -6.3%
Overall (Test vs Ref) | -1.9% | -4.3% | -4.7% | -2.2% | -5.2% | -5.8% | -2.0% | -5.2% | -6.2%
Overall (Test vs single layer) | 16.9% | 27.5% | 25.7% | 13.6% | 22.3% | 21.7% | 12.1% | 25.0% | 25.8%
Overall (Ref vs single layer) | 19.2% | 33.3% | 32.0% | 16.2% | 28.8% | 29.1% | 14.4% | 32.1% | 34.1%
EL only (Test vs Ref) | -3.4% | -5.8% | -6.2% | -5.7% | -8.7% | -9.4% | -3.5% | -7.0% | -8.0%
Notes: For the experiment, we have used the results of SHM-2.0 as the anchor. Based on the results in the table, it can be seen that compared to the anchor, using H-ILP could provide additional coding gain by reducing the BD-rate of 2.1%, 2.4% and 1.6% for RA, LDB and LDP respectively.

## Slide 6: Coding Performance
 | LD-B HEVC 2x |  |  | LD-B HEVC 1.5x |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.3% | -4.8% | -5.0% |  |  |  | -2.2% | -5.1% | -5.5%
Class B | -2.0% | -4.2% | -4.6% | -2.8% | -5.6% | -6.0% | -2.2% | -5.1% | -6.0%
Overall (Test vs Ref) | -2.1% | -4.4% | -4.7% | -2.8% | -5.6% | -6.0% | -2.2% | -5.1% | -5.8%
Overall (Test vs single layer) | 25.8% | 32.8% | 33.1% | 21.3% | 25.6% | 27.7% | 21.5% | 27.8% | 31.2%
Overall (Ref vs single layer) | 28.5% | 39.0% | 39.7% | 24.8% | 33.0% | 35.9% | 24.3% | 34.7% | 39.5%
EL only (Test vs Ref) | -3.6% | -5.9% | -6.1% | -6.4% | -9.1% | -9.6% | -3.7% | -6.7% | -7.5%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.5% | -3.3% | -3.2% |  |  |  | -1.7% | -4.1% | -4.2%
Class B | -1.4% | -2.6% | -3.1% | -1.8% | -3.5% | -3.8% | -1.4% | -3.0% | -3.5%
Overall (Test vs Ref) | -1.4% | -2.8% | -3.1% | -1.8% | -3.5% | -3.8% | -1.5% | -3.3% | -3.7%
Overall (Test vs single layer) | 24.8% | 34.1% | 34.8% | 20.6% | 28.2% | 30.5% | 21.5% | 30.1% | 34.2%
Overall (Ref vs single layer) | 26.6% | 38.0% | 39.1% | 22.8% | 32.8% | 35.6% | 23.4% | 34.6% | 39.4%
EL only (Test vs Ref) | -2.5% | -3.8% | -4.2% | -4.3% | -6.0% | -6.3% | -2.6% | -4.5% | -4.9%

## Slide 7: Conclusion
Investigation of using H-ILP picture for multi-loop decoding of SHVC
H-ILP picture can provide additional BD-rate savings of 2.1%, 2.4% and 1.6% on average for RA, LDB and LDP respectively, compared to SHM2.0
Notes: In this contribution, we have investigated the performance of using H-ILP picture for multi-loop decoding of SHVC.