## Slide 1: AHG 5 and 18: Internal Precision for High Bit Depths
JCTVC-N0188
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Introduction
Range Extensions has been mandated to support higher bit depths.
  Currently 14 bit is specified, but from the outset 16-bit was seen as a possibility.
At the previous meeting the capabilities of HEVC at higher bit depths were presented (JCTVC-M0178).
  Settings were recommended regarding a high-accuracy system, suitable for rate control and high bit depths and high operating points.

## Slide 3: Required Operating Range
When considering operation at higher bit depths the target PSNR must also be higher.
  The suitability of a 16-bit system producing a maximum PSNR of 94.6 is questionable.
    This equates to an MSE of 1.5, which can be achieved by rounding the 16-bit coefficients to 14-bit and using an almost-lossless 14-bit system.
      i.e. the two least-significant bits in the output are effectively random noise.
  Of course, the noise shaping capabilities of the transform permit lower PSNRs to be effective.
  Note that at these high-bit depth operating points, numerical behaviour is paramount, since subjective behaviour is not observable to the human eye.

## Slide 4: Required Operating Range

## Slide 5: Required Operating Range

## Slide 6: HM / RExt3.0 Transform Response
RDOQ off, Transform Skip off, MTDR=ETDR=15, TransformPrecision=6, PCM&Lossless disabled
16-bit degrades in HM due to non-standard clipping on the output to 15-bit (otherwise follows the 14-bit curve up until the entropy coding limit of 15 bits causes a cliff-edge response).

## Slide 7: Proposed Transform Response
RDOQ off, Transform Skip off, MTDR=ETDR=max(15,bitDepth+6), TransformPrecision=14, PCM&Lossless disabled

## Slide 8: Lambda
Lambda has been analysed for the low QP intra operating points
  On average, the current settings in HM are correct.
    Some sequences indicated a slightly lower lambda, some slightly higher, with only negligible deviation in the resulting performance.
  However, the C Model in TComRdCost used parameters describing lambda as UInts, and for 16-bit input data at high QPs (eg 37), this overflowed.
    Those parameters have been changed to Doubles.

## Slide 9: Mixed Coding
Mixed lossy / lossless coding has been studied
        (lossless = transquant bypass and IPCM)
Additional bug-fixes required in the HM / RExt3.0 code.
  Current RExt3.0 does not decode due to illegal QPs being used by the encoder for transquant-bypass CUs
    Errors generated due to the deltaQP mechanism.
  The current cost function is:
      cost=lambda * costbits + costdistortion
    modified to
      cost= costbits + costdistortion / lambda
    Similarly, the estimated cost in intra searching now uses a fixed QP’ of 4 (q of 1).
    These changes makes the lossless costs QP independent (in the mixed system).
      (the initialisation of context variables is still QP dependent)
  The sequence PSNR is formed from the average MSEs, not the average PSNRs
    You can’t average a PSNR=99.99dB (=∞dB) with a PSNR of 40dB.

## Slide 10: Mixed Coding (continued)
Sequence 1 – Hard to compress – 14 bit

## Slide 11: Mixed Coding (continued)
Sequence 2 – Easier to compress – 14 bit

## Slide 12: Conclusion
The base RExt lossy (rate-controllable) coding has been extended from ~80dB to ~120dB producing a consistent response for all transform block sizes over all bit depths.
The various sources of error in the current RExt system have been analysed, and the following recommendations are made:
  To provide better and consistent support for higher bit depths, internal accuracies should be increased:
    MAX_TR_DYNAMIC_RANGE = max(15, bitDepth + 6)
    ENTROPY_CODING_DYNAMIC_RANGE = max(15, bitDepth + 6)
    Transform matrix precision >= bitDepth - 2
A set of higher operating points are recommended for evaluations on the efficacy of high bit depths.